## Slide 1: WPT Waveform Discussion
Date: 2025-07-28
Authors:
Name | Affiliation | Address | Email
Panpan Li | Huawei | Singapore | lipanpan25@huawei.com
Lei Huang |  |  | 
Lumin Liu |  |  | 
Bin Qian |  | Shenzhen, China | 

## Slide 2: Background
Motion #34:
  AMP Energizer is capable of transmitting WPT waveform.
  WPT waveform is transmitted over sub1-GHz.
WPT waveforms have been discussed [1-4].
  [1]: legacy waveforms are preferred, such as OFDM, DSSS, single carrier, etc.
  [2-3]: OFDM is preferred due to high RF-to-DC efficiency.
  [4]: PPM (Pulse Position Modulation) waveform is claimed to provide 10* advantage over OFDM or constant envelope (CE).
This contribution intends to present our views on WPT waveform.

## Slide 3: WPT Waveform Comparison
 | Pros | Cons
continuous wave (CW) | Easy to generate S1G AMP DL/UL PPDU support Adopted by existing WPT devices [5] | Relatively lower RF-to-DC efficiency
OFDM | Can be generated with current WiFi systems May achieve high PAPR, thus increasing RF-to-DC conversion efficiency Suitable for wide bandwidth | High generation complexity compared with CW and PPM Not suitable for ×100kHz narrow band system
DSSS (constant envelope) | Can be generated with current WiFi systems Adopted by existing WPT devices [6] | High generation complexity compared with CW and PPM Low PAPR Not suitable for ×100kHz narrow band system
PPM | very high PAPR Lower interference impact due to lower duty cycles | PPM generally requires a wider bandwidth, not suitable for ×100kHz narrow band system Higher implementation complexity Unstable output of rectifier PPM is particularly vulnerable to multipath interference

## Slide 4: Proposal: WPT waveform
TGbp should recommend CW as the WPT waveform.
  TGbp supports both communication and WPT in UHF RFID bands.
  WPT and communication using same waveform may reduce the complexity
  It has been proposed to use CW as base waveform for S1G AMP communication [7]
  CW is easy to generate.

## Slide 5: Summary
This contribution discusses the AMP WPT waveform in sub-1Ghz
  Recommend CW as WPT waveform

## Slide 6: Reference
[1] 11-25-0029-01-00bp-wpt-protocol-waveform-and-ppdu
[2] 11-24-1551-01-00bp-wpt-waveform-discussion
[3] 11-24-1808-00-00bp-ofdm-based-wpt-waveform
[4] 11-25-0012-00-00bp-wpt-waveform-comparison
[5] https://fcc.report/FCC-ID/2AS57OSSIACOTATX203/4937596.pdf
[6] https://www.mouser.sg/new/powercast/powercast-tx91503-powerspot-transmitter/?srsltid=AfmBOorRR7_ZAHuWZFYWVawqTjj3wbZRpma3iC86cefhUbO9SkAHckkJ
[7] 11-25-0816-00-00bp-feasibility-study-of-mono-static-backscatter-in-sub-1-ghz

## Slide 7: SP 1
Do you agree that 11bp shall specify continuous wave (CW) based WPT waveform?
  Whether this WPT waveform is mandatory/recommended is TBD.
  Yes
  No
  Abstain