## Slide 1: WUR-based Trigger frame for AMP devices
Date: 2025-07-31
Authors:

## Slide 2
Abstract
Consistency between UHF and Active TX-based AMP can be achieved by adapting the AMP trigger frame to indicate the type of communication being used explicitly.

## Slide 3: AMP Trigger Frame Format
Trigger Frame and its sub-types are already defined in the SDF[1]. We propose relocating the sub-type field for the Trigger Frame into the Frame Control field.
The Sub-Type field indicates the type of communication that will occur during the current TXOP. This early indication allows tags of other types to enter sleep mode immediately after receiving the Frame Control field, thereby conserving energy.
Additionally, Sub-Type Dependent fields can be used to carry supplementary data relevant to the specific communication type.
Notes: This frame format is an AMP Trigger frame to indicate the start of the UHF or Active TX slots-based frame exchange.

## Slide 4: AMP UHF Trigger
Instead of attaching the frame type to every UHF frame in AMP [2], we define a Sub-Type within the AMP Trigger frame to signal the start of the UHF frame sequence to all AMP STAs.
STAs, such as dual-mode AMP tags, will begin listening for and responding to UHF RFID commands.
This approach simplifies the MAC layer and facilitates easier extension for supporting all EPC Gen2 commands.

## Slide 5: AMP Trigger Frame for UHF
This frame format is an AMP Trigger frame to indicate the start of the UHF frame exchange.
The Sub-Type field is to indicate that UHF commands and responses will be transmitted in this TXOP.
The ID field can carry the address of the reader.
There is no Frame Body.

## Slide 6: Active TX Time-slot based random access
One of the proposed modes for Active TX in AMP is random-access[3].
An example of random-access Active TX with ECW/ACW = 2:

## Slide 7: AMP Time-slot based random access
For random access Active TX the Sub-Type in the trigger frame will indicate that.
There are some Sub-type dependent fields in the MAC header; these fields determine the Frame body for this trigger frame.

## Slide 8: AMP Time-slot based random access (2)
Sub-type dependent fields are as follows:
There are flags for Slot Duration present and Number of Slots Present
Then two bits Reserved field
Session ID identifies the random-access session
Response Type indicates the type of the solicited uplink response e.g., ID, Sensor Data, etc.
ECW represents total number of random-access slots = 2ECW Allows up to 256 slots
Slot Duration is the time for each slot.
In the end, there is a reserved field.
Notes: Update the image Reserved

## Slide 9: Time-slot based scheduled access example
An example of scheduled access Active TX [4] with ECW = 2:

## Slide 10: Active TX Time-slot based scheduled access
For scheduled access Active TX the Sub-Type in the trigger frame will indicate that.
There are some sub-type dependent fields as follows:
Response Type present = 1 Response type field is in the Frame body
ID present indicates if the is in the Frame Body
Session ID represents the scheduled access session
ECW represents total number of random-access slots = 2ECW , allowing up to 16 slots
There are a couple of reserved bits for future use.
Notes: Swap the order in the frame body and in the flags

## Slide 11: Active TX Time-slot based scheduled access (2)
For scheduled access in Active TX, the ACK frame [5] can be adjusted to simultaneously synchronize [6] the next slot while acknowledging the previous one.
Active Sync = 1 when it is an Active TX Sync as well
ACK previous Slot = 1 will acknowledge the previous slot frame.
The ID in the end is the ID of the AMP non-AP STA (AMP Tag) to transmit in the next slot.

## Slide 12: Conclusion
We define a standardized WUR-based trigger frame format for AMP
We kept the length of MAC, frame control, and FCS the same for all the frame types.
The intent is to start both Backscatter and Active TX TXOP with a similar trigger frame, with the first 8 bits with type and sub-type.
This can be extended to other Active TX methods proposed by the group.

## Slide 13: SP 1
Do you agree that TGbp defines a common trigger frame format that can be used for multiple TGbp AMP transmission modes?
References: 11-25/1258

## Slide 14: SP 2
Do you agree that TGbp defines an ACK frame format that can be used for both as an ACK/NACK + Sync for TGbp AMP transmission modes?
References: 11-25/1258

## Slide 15: SP 3
Do you agree that all UHF frames following the UHF-Trigger frame will be similar to the EPC Gen2 format with no additional?
References: 11-25/1258

## Slide 16: References
[1] Proposed Specification Skeleton for TGbp D0.1, 11-25/0614r3
[2] Rojan et al., Channel access for Backscatter non-AP AMP STAs - way forward, 11-25/0818,
[3] Rojan et al., Random access for Active Tx non-AP AMP STAs, 11-25/0817r0
[4] Rojan et al., Channel access for Active Tx non-AP AMP STAs – follow up, 11-25/0334r0
[5] Chuanfeng He et al., AMP Ack frame, 11-250859
[6] Ugo Campiglio., ACK Message in Time-Slot Based Channel Access for Active AMP STAs, 11-25/1128