## Slide 1: Enhanced Neighbor Discovery
Authors:

## Slide 2
Motivation
Currently, OTA active or passive scanning is typically used for AP discovery, but neither is efficient nor secure
802.11 defines efficient and secure scanning mechanisms for the associated STAs:
  BSS Transition Management (BTM) procedure
  Neighbor Report Request/Response
  Neighbor Report ANQP-element in an ANQP Response frame
For above methods, Neighbor Report element carries information of a reported APs
Reza Hedayat, Apple

## Slide 3
Proposal for Neighbor Report Element
Neighbor Report (NR) element has a flexible structure to optionally include additional sub-elements, if the reporting AP decides to do so
  NR contains only very few mandatory information elements
  The scanning STA does not know what elements the AP will include
To be able to rank the suitability of the reported APs for the roaming, we propose that the following list of elements shall be included in a Neighbor Report of a reported AP
  BSS Load
  RSNE and RSNXE
  UHR Operation and UHR Capabilities elements
  (Extended) Supported Rates and BSS Membership Selectors element
This information is added to NR elements of the BTM Response, Neighbor Report Response and ANQP Response frame (that includes Neighbor Report ANQP-element)
Reza Hedayat, Apple

## Slide 4
This submission proposes a unified content for neighbor report element when it’s reported in a BTM Request frame, Neighbor Report Response frame, or ANQP Response frame (when it includes Neighbor Report ANQP-element)
Summary
Reza Hedayat, Apple

## Slide 5
Do you support that Neighbor Report elements included in BTM Request frame, Neighbor Report Response frame, or ANQP NR in ANQP response frame, transmitted by a UHR AP to a UHR non-AP STA, shall include at least the following information, for each reported AP, to estimate APs suitability as roaming target AP:
  BSS load (if included in the Beacon frame of the reported AP)
  RSNE and RSNXE
  UHR Operation and UHR Capabilities elements
  Supported Rates and BSS Membership Selectors element
  Extended Supported Rates and BSS Membership Selectors element
Straw-poll 1
Reza Hedayat, Apple