## Slide 1: Further Considerations of Active NPCA
Date: 2025-07-23
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Wang | Huawei |  |  | liyanchun@huaewi.com
Yanchun Li |  |  |  | 
Xin Li |  |  |  | 
Xuming Wu |  |  |  | 
Xiang Wang |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Yunbo Li |  |  |  | 
Yuchen Guo |  |  |  | 

## Slide 2: Introduction
TGbn agreed to define NPCA[1] and the NPCA mechanism improves the spectrum utilization, increases the system throughput, and reduces the delay
Basic rules of NPCA
  The NPCA-capable device begins to access the secondary primary channel when it detects the primary channel is occupied
  Duration of NPCA: depend on the PPDU time or NAV
  Two modes of NPCA
    Passive NPCA: AP or Non-AP STA detects and operates the NPCA individually by some common rules
    Active NPCA: Non-AP STA operates the NPCA according to the AP’s Trigger Frame

## Slide 3: Problems of Passive NPCA
  In Passive NPCA, channel switching is triggered by OBSS PPDU. But hidden node problem will lead to unsynchronized channel switching, e.g. while AP(STA) can decode the OBSS packet correctly but STA(AP) can’t.
  Simulation evaluation shows passive NPCA has significant performance degradation in due to synchronization problem.
  In the contribution, we further consider the active NPCA and combine it with Multi-AP coordination scheme to improve the performance of NPCA and avoid the weakness of passive NPCA.
PC: primary channel
NPC: NPCA primary channel

## Slide 4: Proposed Solution 1
ICF
BA
DATA
DATA
Sharing
AP
STA
Shared
AP1
NPC
PC
NPC
PC
NPC
PC
ICR
Active NPCA process
AP Initiates the NPCA
NPCA Transmission
Shared
AP2
NPC
PC
ICR
BUSY
STA1
NPC
PC
BA
STA2
NPC
PC
BUSY
Sharing AP has known the shared Aps support NPCA
Trigger the associated STAs to switch to the secondary primary channel
PC and NPC concurrent transmission
1. Sharing AP indicates its incoming primary channel occupancy.
2. Shared APs notify their STAs to switch to NPCA primary channel.
3. Shared APs perform EDCA channel competition in NPCA primary channel.

## Slide 5: Proposed Solution 2
ICF
BA
DATA
DATA
Sharing
AP
STA
Shared
AP
NPC
PC
NPC
PC
NPC
PC
Resp
Poll
Poll process
Active NPCA and Multi-AP coordination
Sharing AP triggers its own STAs to switch to the secondary primary channel.
Sharing AP leave the transmission opportunity on the primary channel to the shared AP.
- Benefit: Shared AP can support transmission to legacy STAs.
Get transmission requirements

## Slide 6: Summary
  There is synchronization problem with passive NPCA
  Active NPCA scheme can solve the synchronization problem
  Combine the active NPCA and Multi-AP coordination can further improve the communication efficiency

## Slide 7: Straw Poll
Do you agree to use the active NPCA?
  Y
  N
  Abs

## Slide 8: References
[1] 11-24/0209r5 Specification Framework for TGbn
[2] 11-24-1260-01-00bn-further-considerations-on-NPCA
[3] 11-24-0318-00-00bn-robust-secondary-channel-access
[4] 11-24-1838-01-00bn-considerations-on-coordinated-npca
[5] 11-25-0123-01-00bn-further-considerations-on-npca-follow-up
[6] 11-24-2061-02-00bn-usage-of-npca-in-m-ap-coordination
[7] 11-24-1885-04-00bn-npca-hidden-node-problem
[8] 11-24-1853-01-00bn-channel-access-for-npca-operation
[9] 11-24-1867-01-00bn-further-consideration-for-npca-operation