## Slide 1: Further consideration about Fairness in MAP
Date: 2025-07-23
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Wang | Huawei |  |  | wicky.wangweijie@huawei.com
Yanchun Li |  |  |  | liyanchun@huawei.com
Xin Li |  |  |  | 
Xuming Wu |  |  |  | 
Xiang Wang |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Yunbo Li |  |  |  | 
Yuchen Guo |  |  |  | 

## Slide 2: Introduction
TGbn defined a number of Multi-AP coordination schemes share a common Multi-AP (MAP) coordination framework, C-TDMA, C-SR, C-BF, etc.
Fairness is vital to MAP coordination framework:
Allow sustainable coordination
Otherwise, 11bn will degrade to legacy system without MAP.
The main process of MAP coordination includes the following steps
  Multi-AP setup: select a candidate AP (fair player) to form the candidate AP group
  Multi-AP coordination interaction: select the coordination AP from the candidate AP group for the next transmission execution. (grant fair pairing opportunities)
  Multi-AP transmission: execute coordinated transmission. (truthfully channel utilization)

## Slide 3: Problems of MAP
Preamble still arrives at full power(don’t precode on the preamble)
  Most of the proposals about MAP focus on the MAP framework and process based on the friendly coordination between the APs, which take less considerations about the abnormal cases as the following shows
    Case 1: Not grant fair pairing opportunities: Some AP only acts as shared AP but not sharing AP
    Case 2: Not truthfully channel utilization: the shared AP feedbacks there are some packets to send during the Multi-AP coordination interaction but nothing to send for the next transmission in fact
  In this contribution, we propose some solutions to deal with the above problems to improve the fairness and efficiency of MAP

## Slide 4: Case 1—Ensure to grant fair pairing opportunities
AP1
Data
AP2
Some coordinated transmissions
Data
Data
Data
AP1 detects AP2 doesn’t act as sharing AP
Req
Resp
Judge
…
…
AP1start the negotiation process with AP2 and judge whether continue to coordinate with AP2
The time for AP1 to watch AP2’s coordination behavior
Information in Req Frame: fairness negotiation indicator, coordination type(C-SR, C-TDMA,C-BF, etc. ), fairness type, time for AP1 to watch
Information in Resp Frame: coordination type that will use in the watch time
Information in Judge Frame: whether continue to coordinate, coordination type

## Slide 5: Case 2—Ensure truthfully channel utilization
AP1
Data
AP2
Some coordinated transmissions
Data
Data
Data
AP1 detects AP2 feedbacks no traffic frequently in the coordination interaction step
Req
Resp
Judge
…
…
AP1 start the negotiation process with AP2 and judge whether continue to coordinate with AP2
The time for AP1 to watch AP2’s coordination behavior
Information in Req Frame: fairness negotiation indicator, coordination type(C-SR, C-TDMA,C-BF, etc. ), fairness type, time for AP1 to watch
Information in Resp Frame: coordination type that will use in the watch time, traffic information like traffic load, traffic interval, priority, etc.
Information in Judge Frame: whether continue to coordinate, coordination type

## Slide 6: Case 3—other abnormal behavior
AP1
Data
AP2
Some coordinated transmissions
Data
Data
Data
AP1 detects AP2 doesn’t obey the coordination rules
Req
Resp
Judge
…
…
AP1start the negotiation process with AP2 and judge whether continue to coordinate with AP2
The time for AP1 to watch AP2’s coordination behavior
Information in Req Frame: fairness negotiation indicator, coordination type(C-SR, C-TDMA,C-BF, etc. ), fairness type, time for AP1 to watch
Information in Resp Frame: coordination type that will use in the watch time
Information in Judge Frame: whether continue to coordinate, coordination type
Abnormal behavior
  Shared AP doesn’t obey the max power restriction that affects the sharing AP’s transmission
  Shared AP’s C-BF precoding effect is not as good as expect that affects the sharing AP’s transmission

## Slide 7: Summary
  There are some problems existed in the MAP coordination about the efficiency and fairness
  The proposed negotiation process can help the AP detects some abnormal behavior take more information to judge whether to coordinate with other AP

## Slide 8: Straw Poll
Do you agree to add the fairness assurance methods to the MAP framework?
  Y
  N
  Abs

## Slide 9: References
[1] 11-24/0209r5 Specification Framework for TGbn
[2] 11-25-0086-00-00bn-fairness-issue-in-co-tdma
[3] 11-25-0119-00-00bn-consideration-on-fairness-issue-for-map
[4] 11-24-0375-01-00bn-nav-protection-for-c-tdma