## Slide 1: Coordinated Puncturing for MAP
Date: 2025-07-24
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Wang | Huawei | Huawei Industrial Base, Bantian, Shenzhen, China 518129 |  | liyanchun@huaewi.com
Yanchun Li |  |  |  | 
Xin Li |  |  |  | 
Xuming Wu |  |  |  | 
Xiang Wang |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Yunbo Li |  |  |  | 
Yuchen Guo |  |  |  | 

## Slide 2: Introduction
TGbn has defined some Multi-AP coordination schemes in a common MAP coordination framework.
These schemes assume that coordinated APs has a common primary channel.
However, in practice, adjacent APs are assigned different primary channel to minimized the interference.
TGbn has also defined Dynamic Bandwidth Extension (DBE) which can allow AP to make use of leftover channels efficiently.
This contribution discusses about the Multi-AP coordination in DBE operations.

## Slide 3: Motivation
Preamble still arrives at full power(don’t precode on the preamble)
Dynamic Bandwidth Extension (DBE) operation can be traffic load driven:
In DBE, MAP schemes can also be applied and increase system efficiency.
The coordinated puncturing can be beacon interval/SP/ TXOP level, and reuse Multi-AP framework.
BSS1’s transmission
BSS2’s transmission
Ch1: 80MHz
Ch2: 80MHz
BSS1:
-DBE capable
-Primary channel in Ch1
BSS2:
-DBE capable
-Primary channel in Ch1
Interval 1
No Bandwidth Extension
No active channels overlapped between BSS1 and 2.
Interval 2
Bandwidth Extended
Active channels are (partial) overlapped.
BW=160MHz
The same operating channel
Partial overlap operating channel

## Slide 4: Proposed Solution 1
Preamble still arrives at full power(don’t precode on the preamble)
Secondary channel in use
Unused Channel
Primary channel in use
Unused channel
Unused Channel
Secondary channel in use
Primary channel in use
Unused Channel
Sharing AP
Shared AP
STAs
Coord. Req
Coord. Resp
Coord. Trigger
BA
Coord. Req and Coord. Resp: sharing AP asks the shared APs about the coordination information
Coord. Trigger: sharing AP determines whether to apply the coordinated puncturing for the next transmission and notifies the punctured channel information if coordinated puncturing applied
Coordinated Puncturing transmission: sharing AP and shared AP transmit the packets according to the puncturing indication included in the Coord. Trigger Frame
The same operating channel
Non HT DUP

## Slide 5: Proposed Solution 2
Preamble still arrives at full power(don’t precode on the preamble)
Secondary channel in use
Primary channel in use
Unused Channel
Unused Channel
Primary channel in use
Unused Channel
Sharing AP
Shared AP
STAs
Coord. Req
Coord. Resp
Coord. Trigger
BA
Overlapped channels can be assigned to BSS center STAs.
Non-overlap channel can be assigned to BSS edge STAs.
Partial overlap operating channels
Secondary channel in use
Secondary channel in use
ch1
ch2
ch3
ch4
ch1
ch2
ch3
ch4

## Slide 6: Summary
  We can apply the coordinated puncturing in some scenarios when the APs have different primary channel, which can improve the transmission efficiency and decrease the service latency
  The coordinated puncturing reuses the MAP framework that has been defined in the TGbn, only need a little modification about the interactive information

## Slide 7: Straw Poll 1
Do you agree to enable joint operation of the coordinated puncturing and MAP for DBE-capable APs?
  Y
  N
  Abs

## Slide 8: References
[1] 11-24/0209r5 Specification Framework for TGbn
[2] 11-24-0102-00-00bn-multi-ap-coordinated-puncturing
[3] 11-24-1260-01-00bn-further-considerations-on-NPCA
[4] 11-24-1204-00-00bn-coordinated-beamforming-for-11bn
[5] 11-23-1912-00-00bn-coordinated-tdma-procedure
[6] 11-24-0050-00-00bn-coordinated-spatial-reuse-types