## Slide 1: Overview of PQC Exchanges
Date: 2025-07-24
Authors:

## Slide 2: Abstract
This submission provides an overview of the protocol definitions in 11-25/1108r1

## Slide 3: Four New Exchanges + Handshaking
New PQC key exchanges
  Digital signature-based*
  Authentication without signatures
  Password authentication*
  Unauthenticated*
New Handshaking
  Instead of each protocol defining its own KDF in an ad hoc manner to use with the 4-way Handshake post-association…
  Each PQC exchange will generate a hash of the entire transcript of the exchange (minus any fragmentation acks)
  Association will use this transcript digest and the PMK that resulted from successful completion to derive PTK
* Exchanges using classical cryptography exists in 802.11 today

## Slide 4: PQC Handshaking
To provide proper binding of keys it is necessary to include a transcript of the messages that created it
Each PQC exchange creates a digest of all messages sent and received
  Exchange does key generation, handshaking binds and derives keys
  Best practice by other protocols using KEMs (TLS, IKE, etc)
Fragments are included in digest
  The body of each fragment is added to the running digest
  ACKs to the fragments are not included
This digest is used during association to provide proof of possession of the PMK and proper derivation of PTK
  A unified PTK derivation is more easy to analyze
  Less opportunity for subtle mis-binding bugs resulting in attack

## Slide 5: What Does This Look Like?
authentication
frames
auth frame 1
auth frame 2
auth frame n-1
auth frame n
PQC Algorithm generates a PMK, a PMKID,
and a hash of its transcript, T
PQC protocol
MIC, {RSNE [, RSNXE] [, OCI], GTK(N) [, IGTK(M, IPN)]
[, BIGTK(Q, BIPN)] [, WIGTK(R, WIPN)] [,SSID]
MIC, {RSNE [, RSNXE] [, OCI]
association
frames
compute a hash of
the protocol transcript
PTK = HKDF-expand(HKDF-extract(T, PMK),
“PTK derivation”, PTKLen)

## Slide 6
PQC Key Exchanges

## Slide 7: Digital Signature Exchange
Based on SIGMA– Sign and Mac
  Authentication of the (ML-KEM) key exchange
  Binding of the identities with the shared secret
Provides identity protection
Six messages, could be collapsed but fragmentation will result in more messages anyway
  Initial exchange establishes shared secret and sid
  Protected exchange of certificates
  Signature exchange
Provides some crypto agility
  ML-KEM is defined but there is room for others
  ML-DSA is defined but there is room for others

## Slide 8: Digital Signature Exchange
esk, epk = KEM.KeyGen()
AP
STA
c, K = KEM.Encaps(epk)
sid = rand()
ke = KDF(K, “enc key”)
km = KDF(K, “mac key”)
epk
c, {sid}ke
{cert-sta}ke
{cert-ap}ke
K = KEM.Decaps(esk, c)
ke = KDF(K, “enc key”)
km = KDF(K, “mac key”)
msta = HMAC(km, cert-sta)
{sig(epk | c | sid), msta}ke
map = HMAC(km, cert-ap)
{sig(c | epk | sid), map}ke
PMK = KDF(K, …“sig auth”)
PMK = KDF(K,… “sig auth”)

## Slide 9: Signature-less Exchange
Simple two or four message exchange to authenticate both STA and AP
  Optionally, first two messages provide perfect forward secrecy (PFS) in the event of compromise of long-term keying material
  Must treat intermediate secrets as ephemeral, and delete to get PFS
  Second (or only) two messages authenticate and establish key
Assumes possession of trusted public keys
  Keys need not be from same parameter set
  Trust is gained in an out-of-band manner
Mitigates issue with large PQC signatures
  Authentication is through proof of possession of private analog of trusted public key

## Slide 10: Authentication Without Signatures w/PFS
esk, epk = KEM.KeyGen()
AP
STA
ce, Ke = KEM.Encaps(epk)
sid = rand()
ke = KDF(Ke, “enc key”)
epk
ce, {sid}ke
{c1}ke
{c2}ke
Ke = KEM.Decaps(esk, c)
ke = KDF(Ke, “enc key”)
c1, K1 = KEM.Encaps(spka)
ssks, spks = KEM.KeyGen()
sska, spka = KEM.KeyGen()
spks
spka
out of band
K1 = KEM.Decaps(sska, c1)
c2, K2 = KEM.Encaps(spks)
K2 = KEM.Decaps(ssks, c2)
K = HKDF(c1 | c2 | ce,
K1 | K2 | Ke | epk | spks | spka | sid, “string”)

## Slide 11: Authentication Without Signatures
KeyGen
KeyGen
encapsulation key, E1
decapsulation key
ciphertext, C2
Encaps
Decaps
Alice’s copy of K1
Bob’s copy of K1
Encaps
Bob’s copy of K2
Decaps
Alice’s copy of K2
encapsulation key, E2
decapsulation key
ciphertext, C1
K = HKDF(C1 | C2, K1 | K2 | E1 | E2, “string”)
K = HKDF(C1 | C2, K1 | K2 | E1 | E2, “string”)
out of band
Bob
Alice

## Slide 12: Password Authenticated: OQUAKE
Simple two message exchange of NoIC
Does implicit rejection (same as ML-KEM!)
Security proof assumes uniform public keys
  But the ML-KEM pk has too much structure
  Need to randomize pk before passing to 2 round feistel network (2RF) for encryption
draft-veitch-kemeleon-00
  Defines several encodings to randomize ML-KEM public keys and ciphertexts
  One such encoding is “non-rejecting”-– i.e. no looping needed!
Uses two hash functions Htag() and Hkey()

## Slide 13: Password Authenticated Exchange
STA
AP
c, {id}ke
s, T
{sid}ke
c, tag
H(pk)
c, K = KEM.Encaps(pk)
ke = KDF(K, “string”)
K = KEM.Decaps(c, sk)
ke = KDF(K, “string”)
sid = rand()
fsid = sid | id
Z = kemeleon_encode(pk)
(s, T) = 2RF(pwd, r, Z)
((r, Z) = 2RF-1(pwd, s, T)
pk = kemeleon_decode(Z)
(c, K)  KEM.Encaps(pk)
tag  Htag(fsid, pwd, pk, s, T, c, K)
fsid = sid | id
(sk, pk)  KEM.KeyGen()
r  random
PMK = Hkey(fsid, pwd, pk, s, T, c, K)
PMK = Hkey(fsid, pwd, pk, s, T, c, K)

## Slide 14: Unauthenticated Exchange
OWE has been (re)defined in 802.11
  Unauthenticated Diffie-Hellman exchange
  Same use cases as “Open” authentication but provides resistance to passive attack
Useful to provide a PQC version of OWE
  ML-KEM as a drop-in replacement for Diffie-Hellman
  STA generates keypair, sends public key to AP
  AP encaps the public key and sends the ciphertext back to the STA
  STA decaps the ciphertext
  Both sides derive a shared secret

## Slide 15: ML-OWE
AP
pk
c
STA
c, K = KEM.Encaps(pk)
sk, pk = KEM.KeyGen()
K = KEM.Decaps(sk, c)
PMK = HKDF(c, K | pk, “string” )
PMK = HKDF(c, K | pk, “string” )

## Slide 16: Questions
Do we want to do hybrid KEMs?
Do we care about the PFS threat in the no-sig variant?
  Requires an attacker to record exchange and break both private keys
What about 802.1X/EAP-TLSv1.3-CNSA2.0?
  Do 4-way Handshake post association as today?
  Do TGbi’s 802.1X over authentication frames?
Harmonize the PQC key derivation with TGbi
  Get TGbi to adopt TGbt way and include a transcript of the exchange to bind at key derivation time; or,
  Agree that non-PQC exchanges do it TGbi way and PQC exchanges do it TGbt way
Other stuff I forgot about

## Slide 17: References
FIPS 203 https://nvlpubs.nist.gov/nistpubs/FIPS/NIST.FIPS.203.pdf
FIPS 204 https://nvlpubs.nist.gov/nistpubs/FIPS/NIST.FIPS.204.pdf
Kemeleon https://datatracker.ietf.org/doc/html/draft-veitch-kemeleon-00
OQUAKE https://datatracker.ietf.org/doc/html/draft-vos-cfrg-pqpake-00
SIGMA: https://www.iacr.org/cryptodb/archive/2003/CRYPTO/1495/1495.pdf