## Slide 1: High-resolution sensing with multiband communication signals
Date: 2025-07-29
Authors:

## Slide 2: Abstract
Integrated Sensing And Communication (ISAC) systems are expected to perform accurate radar sensing while having minimal impact on communication. Ideally, sensing should only reuse communication resources, especially the spectrum. While multi-static ISAC is ideally suited for wireless networks since it does not require full-duplex, lack of synchronization implies time-varying timing and frequency offsets that prevent the estimation of sensing parameters. We first present how to overcome this challenge using compensates for the timing offset by exploiting the channel correlation across subsequent packets. An additional challenge is that communication systems often operate on narrow subbands with low sensing resolution. Combining contiguous subbands has shown significant resolution gain in active localization. However, multiband ISAC remains unexplored due to communication subbands being highly sparse (non-contiguous) and affected by phase offsets that prevent their aggregation (incoherent). To tackle these problems, we design HiSAC, the first multiband ISAC system that combines diverse subbands across a wide frequency range to achieve super-resolved passive ranging. To solve the non-contiguity and incoherence of subbands, HiSAC combines them progressively, exploiting an anchor propagation path between transmitter and receiver in an optimization problem to achieve phase coherence. We implement HiSAC on an experimental platform in the millimeter-wave unlicensed band and test it on objects and humans. Our results show it enhances the sensing resolution by up to 20 times compared to single-band processing while occupying the same spectrum.

## Slide 3: Motivation for Multi-Static Sensing
Mono-static design requires (simple) full-duplex operation
Make use of the many different available links in a wireless network to learn more about the environment
Transmitter
Receiver
Reflector
micro-Doppler spectrum
Moving parts
Sum of Doppler
shifts
Arms
Torso
Legs
July 2025
Joerg Widmer, IMDEA Networks
Active/passive localization
Micro-Doppler: Small scale Doppler variations around the main Doppler component from moving parts of the object

## Slide 4: Challenge: unsynchronized nodes
Transmitter
Receiver
micro-Doppler
Offset
??
Clock asynchrony Frequency offset
Timing offset
July 2025
Joerg Widmer, IMDEA Networks
Notes: The resulting micro-Doppler frequencies are coupled with the offset
Need to track micro-Doppler over trains of packets
The offset is 2 orders of magnitude bigger  Micro Doppler is destroyed
compensating for the FO for each packet separately removes the FO and the Doppler shift
estimating the phase differences and Doppler shifts requires processing the received samples coherently across subsequent packets.
The FO can not be considered constant within such extended time intervals (several milliseconds), and it makes the phase of signal samples across different packets incoherent, preventing the estimation of Doppler shifts

## Slide 5: JCAS with unsynchronized transceivers (JUMP)
Timing offset compensation
Multipath detection and tracking
CFO removal
+ micro-Doppler extraction
Channel Impulse Responses
Slide 5
July 2025
Joerg Widmer, IMDEA Networks
Notes: Need an approach that works with single RF chain, no synchronized clocks
3 main components: timing offset, object tracking, micro-Doppler estimation
Packet k, BP b, path l

## Slide 6: Timing offset compensation
Multipath environment changes slowly across time
  Holds even with dynamic targets if packet rate is high
Deals with NLOS and multi-path changes
Estimate and compensate
For the relative TO
Cross-correlation
CIR at
CIR at
Slide 6
July 2025
Joerg Widmer, IMDEA Networks
Notes: Assume the multipath environment changes slowly over time
We can then consider the CIR magnitude at 2 subsequent time steps (packets)
If the assumption in the first bullet holds, the 2 CIRs will have the same profile (in approximation) except for a shift in the delay domain due to the RELATIVE timing offset between the two packets
The relative TO can be estimated by detecting the location of the strongest cross-correlation peak
LOS occlusions leads to “slow” disappearance of the corresponding path from the CIR

## Slide 7: Our design: JUMP
Timing offset compensation
Channel Impulse Responses
EKF
Bistatic
localization
Correlator
+ voting
Peak det. &
AoD est.
CIR
shift
Multipath detection and tracking
CFO removal
+ micro-Doppler extraction
July 2025
Joerg Widmer, IMDEA Networks
Notes: Then we do passive localization
Peak detection: via Cell-Averaging Constant False-Alarm Rate (CA-CFAR)
AoD: correlation between each BP shape and the CIR profile for a specific channel tap (TX BP shapes known)
Select strong static reference path

## Slide 8: CFO Compensation
Micro-Doppler extraction needs phase-coherent measurements over (long) sequences of CIR measurements
CFO is
  Time varying: destroys phase coherence across packets
  Two orders of magnitude larger than the Doppler shift of interest
  Example: 60 GHz carrier, Sivers antennas, human motion
 Estimation + compensation is not feasible
Slide 8
July 2025
Joerg Widmer, IMDEA Networks

## Slide 9: Our solution
Doppler only
Offset
only
Doppler + Offset
Conjugate
multiplication
Track static path(s)
Cancel frequency offset
No estimation needed!
Static
TX
RX
Slide 9
July 2025
Joerg Widmer, IMDEA Networks
Notes: Key idea: CFO is constant in all multipath components of the CIR
Conjugate multiplication of the static signal with the dynamic one to remove offset
Cancels out the CFO without estimating it, thus the cancellation is errorless
micro-Doppler is almost as good as the one you get from a phase locked system
micro-Doppler quality depends on the SNR on the static path used for the cancellation

## Slide 10: Our design: JUMP
Timing offset compensation
Channel Impulse Responses
EKF
Bistatic
localization
Ref.
path
Correlator
+ voting
Peak det. &
AoD est.
CIR
shift
Multipath detection and tracking
CFO removal
Spectral analysis
CFO removal + micro-Doppler extraction
July 2025
Joerg Widmer, IMDEA Networks
Notes: Then we do passive localization
Peak detection: via Cell-Averaging Constant False-Alarm Rate (CA-CFAR)
AoD: correlation between each BP shape and the CIR profile for a specific channel tap (TX BP shapes known)
Select strong static reference path

## Slide 11: CFO cancellation
WALKING
SITTING
July 2025
Joerg Widmer, IMDEA Networks
Notes: Key result for CFO cancellation:
With CFO the microDoppler is unusable
Resulting microDoppler after cancellation is almost identical to the one from a phase locked system

## Slide 12: Integrated sensing and communications resolution
Transmitter
Receiver
Communication signals
Targets
Resolvable
Unresolvable
Signal
bandwidth
Resolution

## Slide 13: Multiband ISAC
IDEA: can we overcome the low-resolution by
combining multiple bands?
CHALLENGE: can we do it flexibly leveraging existing multiband communications for sensing with no overhead?

## Slide 14: Coherent multiband processing
TX
RX
Timing offset (TO)
Clock/LO asynchrony
Hardware non/ideality
Carrier
frequency
Offset (CFO)
Extend
Channel Frequency
Response
Extend

## Slide 15: Coherent multiband processing
TX
RX
Timing offset (TO)
Clock/LO asynchrony
Hardware non/ideality
Carrier
frequency
Offset (CFO)
Extend
Channel Frequency
Response
Extend
Extend
Phase mismatch
Slide 15

## Slide 16: Our high-resolution multiband sensing approach
1) Compressed sensing coherent
combination
Gaps
Gaps
2) Phase offsets compensation
3) Single-band aided fullband combination
4) Moving average temporal aggregation

## Slide 17: Phase offsets compensation
2) Phase offsets compensation
        Optimization problem
    Initialization
Delay
Delay
|CIR|
|CIR|
TO is shared by all paths
Find optimal phase rotation and re-modulation

## Slide 18: Experimental setup (60 GHz band)
Metal
cylinders
People

## Slide 19: Wideband channel reconstruction
1.2 GHz
58 MHz

## Slide 20: Moving people sensing
Full 1.2 GHz
bandwidth
Comparable resolution
58 MHz
subbands

## Slide 21: Cross-technology – 5G-NR & WiGig
5G-NR
OFDM
IEEE 802.11ay SC
59.69 GHz
62.64 GHz
400 MHz
1.76 GHz
1.86 GHz Gap

## Slide 22: Concluding remarks
Developments
High-resolution single- and multi-band ISAC
3x to 20x resolution gain
No additional overhead
Cross-technology
Frequency anisotropy
Impact of Doppler

## Slide 23: References
Jacopo Pegoraro, Jesus Omar Lacruz, Tommy Azzino, Marco Mezzavilla, Michele Rossi, Joerg Widmer, and Sundeep Rangan. JUMP: Joint communication and sensing with unsynchronized transceivers made practical. IEEE Transactions on Wireless Communications, Feb. 2024
Jacopo Pegoraro, Jesus O. Lacruz, Michele Rossi, and Joerg Widmer. 2024. HiSAC: High-Resolution Sensing with Multiband Communication Signals. In Proceedings of the 22nd ACM Conference on Embedded Networked Sensor Systems (SenSys '24). Association for Computing Machinery, New York, NY, USA, 549–563. https://doi.org/10.1145/3666025.3699357.