## Slide 1: Localized SC-FDMA with Constant Envelope
Date: 2025-07-27
Authors:

## Slide 2: Abstract
Reduction of PAPR is one target in TGbr. This contribution reviews the generation of low-PAPR signals based on OFDMA using the well-known techniques from single-carrier (SC) FDMA. Two variants are highlighted. The classical approach applies root-raised cosine filtering in each OFDMA resource block and reaches PAPR99% between 6.3 and 2 dB with 64-QAM and π/2-BPSK, respectively. Pure phase modulation like GMSK can realize the ultimate PAPR of 0 dB.

## Slide 3: Outline
Introduction
Evolved SC-FDMA transmitter
Evolved SC-FDMA receiver
Results
Conclusions

## Slide 4: Motivation
TGbr scope includes reduction of the PAPR [1]
Lower PAPR is desirable
  to increase the link margin or reduce power
  to increase the link distance that can be bridged
OFDM(A) based on 802.11ax can be used in 802.11bb
  complex-valued OFDM waveform modulates an IF subcarrier
When modulating the light, intensity cannot be negative
  a DC bias current is applied; modulation is always around it
  to avoid clipping, the modulation amplitude can be reduced
  at high spectral efficiency, reduction can cost 10 dBel link margin
  at low spectral efficiency, the modulation amplitude can be higher

## Slide 5: What is SC-FDMA?
SC-FDMA is a variant of OFDMA which promises reduced PAPR
  OFDMA assigns groups of sub-carriers to individual users
  SC-FDMA performs additional DFT-spreading inside each group [2, 3]
However, DFT-spread SC-FDMA reduces the PAPR only marginally
  reaching lower PAPR with SC-FDMA is possible, but more sophisticated
    frequency-domain RRC filtering can reach 2 dB PAPR [3]
    sub-carrier phase modulation, like GMSK [10], can reach 0 dB PAPR

## Slide 6: Localized SC-FDMA
DFT-spread OFDMA [3, 4]
  if N=M, DFT and IDFT cancel each other
  the result is a serially modulated single carrier signal with cyclic prefic (CP)
  typically, N < M is used: equivalent to a rectangular filter in the frequency domain
  this filter causes „ringing“ in the time domain
sin(x)/x envelope in the time domain distorts SC-FDMA waveform  PAPR
  idea: use better filtering
  may need more bandwidth

## Slide 7: Frequency-domain filtering
  Realize filtering in the frequency domain
    filtering needs up-sampling in the time domain
    equivalent to repetition in the frequency domain
    then apply the frequency-domain filter
    apply cyclic shift to the intended sub-band
Source:
Qualcomm

## Slide 8: GMSK in 2G GSM [6-9] SC-FDMA [10]
  Up-sample the binary symbol sequence a(n)
  Pass it through a Gaussian filter  c(k)
  Feed it into a minimum shift keying (MSK) modulator:
    accumulate the signal in an IIR filter (to reduce out-of-band emission [5-8])
    apply single-sideband (SSB) modulation
  Apply GMSK to localized SC-FDMA
    do up-sampling and Gaussian filtering in the frequency domain
    use MSK modulator in the time-domain

## Slide 9: GMSK over SC-FDMA [10]
Source:
Qualcomm
  Why in time-domain?
    phase modulation is non-linear process: carrier phase modulated using sine and cosine
    creates four-wave mixing  out-of-band radiation is minimized with BT=0.3 in 2G

## Slide 10: Results [10]
  A p/2 BPSK w/o filter
    discussed at but not used
  B RRC filter impact onto BPSK
    envelope is the filtered data sequence
    zero-crossings are still problematic
  C Filtered p/2-BPSK
    no more zero crossings
    envelope is not yet constant
  D GMSK over SC-FDMA
    constant envelope

## Slide 11: PAPR99% results [10]
  DFT-spread SC-FDMA
    only 1.7 dB better than OFDMA
  p/2 BPSK w/o filter
    2.6 dB better than SC-FDMA in LTE
  RRC-filtered BPSK
    needs 20% more bandwidth
    4.4 dB better than DFT-spread SC-FDMA
  Filtered p/2 BPSK
    6 dB better than DFT-spread SC-FDMA
  GMSK over SC-FDMA
    7.9 dB better than DFT-spread SC-FDMA

## Slide 12: Conclusions
  Evolutions of the basic SC-FDMA concept can significantly lower the PAPR.
  Root raised-cosine filtered π/2-BPSK can reach PAPR99% of 1.9 dB. GMSK over SC-FDMA may even reduce the PAPR downto 0 dB.
  There is additional effort to fit filtered SC-FDMA into the existing 802.11 PHY framing. Filtering requires more sub-carriers/time slots for same data.
  Other techniques do not have this issues: Constant-Envelope (CE-) OFDM and On-Off Keying (OOK) [10].

## Slide 13: References
[1] TGbr PAR in doc. 11-25/0185r2
[2] A. Krishnamoorthy, „PAPR reduction considerations
[3] R1-050702 “DFT-Spread OFDM with Pulse Shaping Filter in Frequency Domain in Evolved UTRA Uplink,” 3GPP TSG RAN WG1 42, London, UK, 2005.
[4] V. Jungnickel, T. Hindelang, T. Haustein, and W. Zirwas, “SC-FDMA Waveform Design, Performance, Power Dynamics and Evolution to MIMO,” in Proc. IEEE PORTABLE, May 2007.
[5] M. J. Narasimha, J. W. Kim, Y. Yu, J. H. Park “Methods and Systems for PAPR Reduction in SC-FDMA Systems“, US Patent No. US 8,264,946, Apr. 17, 2009.
[6] K. Gentile, “The Care and Feeding of Digital, Pulse-Shaping Filters,” www.rfdesign.com , April 2002
[7] K. Murota and K. Hirade, “GMSK Modulation for Digital Mobile Radio Telephony,” IEEE Transactions on Communications, vol. 29, no. 7, pp. 1044–1050, July 1981.
[8] T. Turletti, “GMSK in a Nutshell,” 1996, http://citeseerx.ist.psu.edu/viewdoc/summary?doi=10.1.1.39.9127
[9] R. Sawai and H. Harada, “Simulation Program to Realize GMSK Transmission System” www.codeforge.com/read/142158/gmsk.m
[10] V. Jungnickel, L. Grobe. “Localized SC-FDMA with constant envelope,” in Proc. IEEE PIMRC, 2013
[11] H. Camporez, W. Costa, M. Pontes, M. Segatto, H. Rocha, J. Silva, M. Hinrichs, A. Paraskevopoulos, V. Jungnickel, R. Freund, “Increasing the reach of visible light communication links through constant-envelope OFDM signals,” Optics Communications, Mar. 2023, 129179, ISSN 0030-4018, https://doi.org/10.1016/j.opt-com.2022.129179.

## Slide 14: Receiver [10]
  Perform reverse operations at the Rx
    demodulate MSK in the time domain
    match output to a Gaussian filter
    add redundant signals in the frequency domain
    feed them back into the N-IDFT

## Slide 15: Pre-FEC bit error rates [10]
  The gain in PAPR causes no loss at the receiver
    For same block size N, penalty is always less than 0.2 dB at the receiver side
    For small N, very low SNR is possible (full power, fractional bandwidth per user)
  If we increase N, required SNR increases linearly, due to more noise.