## Slide 1: NPCA EDCA Slot Boundaries
Date: 2025-09-10
Authors:

## Slide 2: Background
D1.0:
- “A first STA shall not initiate a transmission on the NPCA primary channel to a second STA until the second STA’s NPCA switching delay time has elapsed…”
“The NPCA Switch(#1500) Delay field indicates the time needed by an NPCA AP(#2948) to switch from the BSS primary channel to the NPCA primary channel in the unit(#1502) of 4 μs.”
The NPCA Switch Delay field is 6 bits for both AP and non-AP STAs
  =>

## Slide 3: Problem Statement
How to take into account different switching delays of the peer STAs?
  How to prevent collisions when multiple STAs, targeting the same peer STA, complete their switch to and backoff on the NPCA channel before the peer STA finishes switching?
  How to retain EDCA ACs prioritization?
The problem concerns the channel access rules, hence, should be defined in the standard

## Slide 4: Why are different switching delays an issue?

## Slide 5: What if APs switching delay is shorter?
Unnecessary internal collisions from AP ACs finishing the backoff are still unavoidable.

## Slide 6: Avoiding Excessive Collisions Upon Switching
Let us define NPCA Activation Time as the time the STA may start EDCA procedures on the NPCH
Option 1. Let the NPCA Activation Time for a STA1 be the moment the switching delay of STA1 expires.
If the switching time of a peer-STA of STA1 is long enough that STA1 backoff expires earlier, STA1 shall re-select the backoff without changing the QSRC

## Slide 7: Option 1. STA restarts the backoff until the peer STA is available

## Slide 8: What if AC_VO and AC_BK of AP A contend?

## Slide 9: Maintaining EDCA Priorities
Option 2. Let the NPCA Activation Time be the moment both the STA and its peer STA(s) are available at the NPCA primary channel.
*
* AIFS may end by the time the peer STA is available
*

## Slide 10: Option 2. Issue
Another STA may capture the medium while the NPCA STAs are waiting for their peers to become available on the NPCH

## Slide 11: Option 3. Reserve the medium by sending a special frame
AC priorities are preserved
Faster-switching STAs get priority when accessing NPCH
Reduced chances of NPCA STAs losing contention to the NPCH residents
Channel is occupied with unnecessary transmissions
The channel reserving frame needs to have variable length, i.e., CTS-to-self doesn’t fit perfectly

## Slide 12: SPs
SP1. Do you agree that backoff rules at the NPCA shall take into account the NPCA switching delays of peer STAs?
SP2. Which option to resolve the issue of different switching delays of an NPCA STA and its peer NPCA STA do you prefer?
  Option 1. The NPCA STA shall restart the backoff if it completes before the peer STA is available on the NPCH
  Option 2. The NPCA STA shall start the backoff only when its peer STA is available on the NPCH
  Option 3. After completing the backoff, the NPCA STA may send a frame to reserve the medium until the peer STA is available on the NPCH