## Slide 1: Considerations on Co-RTWT Negotiation Response
Date: 2025-09-09
Authors:

## Slide 2: Introduction
The MAPC framework has been agreed. [2][3]
As part of MAPC Negotiation, an AP that receives a MAPC Negotiation Request frame shall respond with a MAPC Negotiation Response frame indicating accept, reject, or alternate with suggestion.
However, a MAPC requesting AP may face difficulty when attempting a Co-RTWT negotiation to align its R-TWT schedule with the alternate schedule proposed by the MAPC responding AP.
Furthermore, if the MAPC responding AP receives again a Co-RTWT negotiation request that differs from its previous suggestion, it may again reply with another alternate response.
In this contribution, we discuss the issue of repeated alternate responses in Co-RTWT negotiations and propose a signaling mechanism to improve the efficiency of the negotiation process.

## Slide 3: Recap: 37.15.2.4.2 Co-RTWT negotiations [1]
A Co-RTWT requesting AP may request to establish, update, or tear down the Co-RTWT agreement(s)
  The Co-RTWT requesting AP shall include one or more MAPC Scheme Request fields in the MAPC Negotiation Request frame, with each field corresponding to an R-TWT schedule.
  If the MAPC Request Parameter Set field is present in a MAPC Scheme Request field for an R-TWT schedule, it shall specify the associated Co-RTWT Parameter Set field, as described in 9.4.2.aa3.2.5 (Co-RTWT profile), and in accordance with the Restricted TWT Parameter Set field corresponding to the associated R-TWT schedule announced by the Co-RTWT requesting AP in its own BSS (see 35.8.3.1).
An AP that responds to a Co-RTWT requesting AP is referred to as a Co-RTWT responding AP, and it responds with MAPC Negotiation response frame
  In the MAPC Negotiation Response frame, each Per-Scheme Profile subelement may include a MAPC Scheme Request field with MAPC Operation Type field set to 4 (Agreement Reject)
  When providing a response for a specific R-TWT schedule by setting the MAPC Operation Type field in the MAPC Scheme Request field associated with that schedule to 5 (Agreement Alternate), the Co-RTWT responding AP shall include the MAPC Request Parameter Set field containing the suggested parameters for the corresponding Co-RTWT agreement.

## Slide 4: Problem Statements
Unlike other MAPC schemes, Co-RTWT negotiation is initiated by the requesting AP based on its existing R-TWT schedule. The requesting AP seeks to protect its R-TWT schedule for the periodic low-latency traffic with its associated non-AP STAs.
When a MAPC responding AP suggests a new set of Co-RTWT parameters, it may be difficult for the requesting AP to modify its existing R-TWT schedule to match the suggested parameters, due to constraints such as pre-established R-TWT schedules, or other operational requirements.
If the requesting AP submits a new request that remains different from the suggestion, the responding AP may again provide an alternate response. This process can result in repeated exchanges and an inefficient negotiation loop.

## Slide 5: Problem Statements
As described in the previous slide, the Co-RTWT negotiation procedure between a requesting AP and a responding AP can become repetitive. This occurs when the requesting AP continues to request protection for its R-TWT schedule that does not align with the alternate parameters suggested by the responding AP.
MAPC Requesting AP
MAPC Responding AP
MAPC Negotiation Request frame
MAPC Negotiation Response frame
MAPC Negotiation Request frame
MAPC Negotiation Response frame
First Co-RTWT Negotiation
Second Co-RTWT Negotiation
Requests the Co-RTWT Agreement Establishment
Responds the Alternate with suggestion
Requests the Co-RTWT Agreement Establishment
Responds the Alternate
with suggestion
MAPC Negotiation Request frame
MAPC Negotiation Response frame
N-th Co-RTWT Negotiation
Requests the Co-RTWT Agreement Establishment
Responds the Accept
…
R-TWT schedule
Suggested
R-TWT schedule
Modified
R-TWT schedule
Suggested
R-TWT schedule
Modified
R-TWT schedule

## Slide 6: Proposed Solution
To prevent repetitive alternate responses in Co-RTWT negotiation, we propose a signaling method that allows a responding AP to indicate the reason for rejecting a requested R-TWT schedule (with or without an alternate suggestion).
A MAPC responding AP may include this rejection information in the MAPC Negotiation Response frame along with the suggested R-TWT schedule. The rejection information can be conveyed in each Co-RTWT profile as a compact Reason Code.
  Examples of rejection reasons include:
    Overlap with the MAPC responding AP’s existing R-TWT schedules.
    Frequent overlap with the MAPC responding AP’s TBTT.
    [Additional reasons can be defined as needed].
MAPC Per-Scheme Info field of the Co-RTWT profile format
Broadcast
TWT ID
Last Co-RTWT Request
Reason Code

## Slide 7: Proposed Solution (cont’d)
Upon receiving the Reason Code in the MAPC Negotiation Response frame, the MAPC requesting AP checks the responding AP’s Beacon frame and obtains the detailed information indicated by the Reason Code.
Based on the suggested R-TWT schedule and the detailed information, the MAPC requesting AP can make an informed decision and avoid entering an endless negotiation loop.
  For example, the requesting AP may attempt a new negotiation with an R-TWT schedule that takes into account both the responding AP’s suggestion and the reason for rejection.

## Slide 8: Summary
We discussed the issue of repetitive alternate responses in Co-RTWT negotiation.
To address this, we proposed a signaling mechanism for alternate responses. The mechanism allows the responding AP to include reason information within the Co-RTWT Profile to explain the rejection, thereby improving the efficiency of the negotiation process.

## Slide 9: Straw Poll 1
Do you agree to add the following into the 11bn SFD ?
  In a Co-RTWT negotiation, a MAPC responding AP may include additional information in its MAPC Negotiation Response frame to indicate the reason why a requested R-TWT schedule is rejected

## Slide 10: References
[1] Draft P802.11bn_D1.0
[2] 11-25/0600 PDT MAC Co-RTWT Signaling and Protocol Aspects Giovanni Chisci
[3] 11-25/0599 PDT MAC MAPC Signaling and Protocol Aspects Giovanni Chisci