## Slide 1: Frame Format Discussion
Date: 2025-08-10
Authors:

## Slide 2: Recap: Backscatter Frame Format
Frame Header
Frame Body
(Optional)
FCS
Frame
Type
Protection
Indication
ID Flag
Reserved
RA/TA ID
(Optional)
A 11bp frame includes the following fields
  Frame Header
    Frame Control field
      Backscatter Indication (1 bit)
      Frame Type (4 bits),
      Protection Flag(1 bit),
        This may not be required if the response of Authentication is the only frame with the protection.
      ID Flag(1 bit)
      Type Spec Flag (1 bit)
      Reserved bits
    RA/TA ID of DL unicast frame
      The RA/TA ID of UL unicast frame to identify the STA may be required.
    Type Specific
  Optional Frame body.
    Updated RFID command
  FCS.
    8bits or 16 bits
Frame Control
Type Specific
(Optional)
Type Spec
Flag
4
1
bits
1
1
1

## Slide 3: Response Rate Flag for Backscatter Tag
Without the Response Rate Flag, the reader occupies the medium for tag’s UL frame transmission, based on the minimal date rate and the length of the responding frame.
  With the Response Rate Flag, the accurate medium time is allocated to the UL frame transmission.
Another difficulty is that there is no date rate indication in 11bp uplink PHY header.
  Without the Response Rate Flag, the PHY header for backscatter use case needs to be updated in order to support the multiple data rates.
The tag’s implementation is simplified.
Frame Header
Frame Body
(Optional)
FCS
Frame
Type
Protection
Indication
ID Flag
UL
Rate
RA/TA ID
(Optional)
Frame Control
Type Specific
(Optional)
Type Spec
Flag

## Slide 4: Tag’s ID
Why RFID uses RN16 as tag’s identifier.
  RFID occupies the medium one time for the information exchanges.
  No TXOP limit exists.
11bp restriction:
  TXOP limit exists.
    One medium occupancy can’t finish the information exchanges between a reader and a tag.
    The tag can’t maintain 16-bit RN16 across TXOPs.
Why CRC16 of EPC can address the issue:
  EPC acquiring is the mandatory first step for the additional information exchange.
  Once the EPC of a tag is acquired by a reader, both the reader and the tag know the CRC16 of the tag’s EPC.

## Slide 5: AP’s (Reader’s) ID
Observation:
  For backscatter use case, the frame exchange with a tag is always solicited by the AP.
  A tag has no capability to store the AP’s ID under the information exchange through multiple TXOPs.
  There is no reader’s ID in RFID commands.
Option 1:
  There is no AP’s ID in the frames for backscatter use case.
Option 2:
  For backscatter use case, the AP’s ID in the frames can be ignored by a tag.

## Slide 6: Length Further Discussion
Frame Header
Frame Body
(Optional)
FCS
Frame
Type
Protection
Indication
ID Flag
UL Rate
RA/TA ID
(Optional)
PHY layer needs to know the ending time of PPDU decoding.
  There is no Length field in PHY header.
PHY PPDU decoding ending assisted by MAC layer
  Method 1
    MAC’s notification of PPDU decoding ending time
      The PHY layer doesn’t need to figure out the frame length.
  Method 2:
    Frame Length field always exists in the fixed location of any frame, e.g. at the beginning of the frame.
    Frame length indication even if the frame has no optional field.
Frame Control
Type Specific
(Optional)
Type Spec
Flag
Frame Header
Frame Body
(Optional)
FCS
Frame
Type
Protection
Indication
ID Flag
UL Rate
RA/TA ID
(Optional)
Frame Control
Type Specific
(Optional)
Type Spec
Flag
Length
4
1
bits
1
1
1
8
4
bits
1
1
1

## Slide 7: SP 1
Do you agree to add the following text to 11bp SFD:
  For mono-static backscatter use case, the MAC header field in DL frame that solicits UL frame carries the UL Rate field to indicate the data rate of the UL frame being solicited.
    Which type(s) of DL frame to carry the UL rate indication is TBD.

## Slide 8: SP 2
Do you agree to add the following text to 11bp SFD:
  for mono-static backscatter use case, the STA’s 16-bit STA AMP identifier obtained from the output of CRC16 over the global identifier of the STA is used as the STA’s ID.
    NOTE: the global identifier is TBD.