## Slide 1: Flexible Multiple BSSID Set
Date: 2025-09-09
Authors:

## Slide 2: Problem Statement 1
Current Multiple BSSID behavior:
  All BSSIDs (typically each a separate SSID) in the MBSSID Set must have same PHY generation
  Capabilities and Operation elements are always inherited for NonTx BSSID from the TxBSSID
This causes client’s disconnection when PHY gen changes for SSIDs in the field
  This is a big issue, specially in deployments where strict WLAN connectivity SLA is needed (e.g. Healthcare needs reliable connectivity 24/7)
Field Use Cases | Description
UC1: Phased rollout of a new PHY generation (e.g. from 11be to 11bn) | Customers prefer to perform phased rollout of new PHY gen over different BSSIDs (SSIDs), to minimize any interop impacts to clients from previous gen (N-1, N-2). Currently, such phased roll out leads to MBSSID set regrouping – which causes reset of all BSSIDs/VAPs in current MBSSID set and the new MBSSID set  disconnecting all clients connected to all VAPs in the two MBSSID sets. NOTE: customers typically first upgrade nonTx BSSID to contain any interop issues.
UC2: Per SSID config changes for PHY generation | Customers can configure/change PHY generation on a per SSID basis post AP hardware refresh. When an SSID’s PHY gen is changed (upgraded or downgraded), that SSID needs to be moved to a different MBSSID group, causing MBSSID regrouping for two MBSSID sets - which causes reset of all BSSIDs/VAPs in both sets  disconnecting all clients connected to all VAPs in two MBSSID sets.

## Slide 3: Possible Solutions (1)
Solution 1: AP does not deploy MBSSID Sets in 6 GHz
There is requirement for APs to deploy MBSSID Set in 6 GHz (from Wi-Fi 6E), when multiple BSSIDs/VAPs are deployed on a given 6GHz channel
Given client disconnection issues across many VAPs due to MBSSID set regrouping, one solution is for AP to not deploy MBSSID sets on 6 GHz (change the requirement). AP will deploy SSIDs as standalone SSIDs avoiding MBSSID regrouping related issues
  Given observed Channel Utilization (CU) is low on 6 GHz today, no strong need for beacon airtime optimization
Assume no impact to clients – clients will see beacons for each SSID w/o any Multiple BSSID element
However, this may not be desirable when CU starts to grow on 6GHz as more devices use that band. Hence, we need a solution that makes use of MBSSID set, achieving beacon airtime optimization

## Slide 4: Possible Solutions (2)
Solution 2: Support flexible MBSSID set
Propose to define flexible MBSSID set - which allows BSSIDs of different PHY generations in an MBSSID set
This would minimize client disconnections by avoiding MBSSID set regrouping when PHY gen changes
  When a nonTx BSSID PHY gen changes, then only that BSSID is reset. No impact to other BSSIDs in the set. When a Tx BSSID PHY gen changes, then all BSSIDs in that set are reset, but no impact to any BSSIDs in other MBSSID set.
To support most common customer UC of upgrading nonTx BSSID first, need to allow Tx BSSID to be either lower or higher PHY gen – allow Tx BSSID to be Wi-Fi7 with nonTx BSSID as Wi-Fi8
In a flexible MBSSID Set with TxBSSID as Wi-Fi7 - set relevant fields in the Capability Information and TIM IE in Tx BSSID beacon for UHR critical updates
Only support flexible MBSSID set for mix of 11be & 11bn and future generations (to avoid legacy interop with Wi-Fi 6E)
Possible MBSSID Set options

## Slide 5: Flexible MBSSID Set
A Tx BSSID can be non-UHR EHT BSSID or UHR BSSID
When Tx BSSID is a non-UHR EHT (11be):
  a nontransmitted BSSID can be UHR and carries UHR elements (UHR Operation, UHR Capabilities, UHR Operating Modes etc.) in its nontransmitted BSSID profile. Tx BSSID beacon sets fields in Capability Information and in TIM IE for UHR critical updates
  a nontransmitted BSSID can be non-UHR EHT (11be) and inherits EHT Operation and EHT Capabilities element from Tx BSSID (per baseline behavior)
When Tx BSSID is UHR:
  a nontransmitted BSSID can be a non-UHR EHT (11be) BSSID, and has the UHR elements (UHR Operation, UHR Capabilities, UHR Operating Modes etc.) listed in the Non-Inheritance element in its nontransmitted BSSID profile.
  a nontransmitted BSSID can be a UHR BSSID and inherits at least UHR Capabilities element. TBD on inheritance for UHR Operation element per options on slide 7.
Possible MBSSID Set options

## Slide 6: Problem Statement 2
For UHR, we are defining several operating modes - NPCA, DSO, AP PUO, DBE, DUO, P_EDCA, LLI, DPS (mobile AP)
For some UHR operating modes, it is desired to allow flexibility of different enablement status and/or different parameters for BSSIDs in an MBSSID Set, to enable network to apply different SSID specific policy in the set.
Use case: Guest SSID and Employee SSID in the same MBSSID set. Enterprise network needs to apply different policy for these SSIDs (as done typically today)

## Slide 7: Solution for Problem Statement 2
A simplified proposal for current set of UHR modes include:
  Support same enablement status across all UHR BSSIDs in an MBSSID set for: NPCA, DSO, AP PUO, DBE, DPS (mobile-AP) (since these are radio level modes)
  Allow different enablement for: P-EDCA and LLI (since these are not radio level, related to LL support and the policy can be BSS specific)
  Allow different BSS-specific parameters for P-EDCA and DUO (for policy reasons)
For any new UHR mode, evaluate if different enablement status or parameters are needed across BSSIDs in an MBSSID set for policy reason
Two possible options to support this flexibility:
  Option 1: Allow UHR Operation element to be carried in a nonTx BSSID profile, indicating different enablement status and/or parameters for one or more UHR modes. In this case UHR Operation element is not inherited when enablement status and/or parameters are different and instead carried in the nonTx profile.
  Option 2: Define a new UHR Operating Modes element that carries enablement and/or parameters only for UHR modes that are BSSID specific. The new element may be inherited (if same) or overwritten (if different) for a nonTx BSSID. Other UHR modes are carried in UHR Operation element that is always inherited.

## Slide 8: Summary
We propose Flexible MBSSID set to allow mix of UHR and EHT PHY generations in the same set, to avoid client’s disconnections due to MBSSID regrouping when PHY gen changes
  Use cases are common in the field: phased gen rollout and config changes to PHY gen later
In a Flexible MBSSID set, a Tx BSSID can be either non-UHR EHT BSSID or UHR BSSID, to support most common customer UC of upgrading nonTx BSSID first
  Define enhanced inheritance rules to support this (in an interop friendly way)
  When Tx BSSID is a non-UHR EHT, in Tx BSSID beacon set fields in Capability Information and in TIM IE for UHR critical updates (per 11bn D1.0)
We propose to allow flexibility of supporting different enablement status and/or different parameters for some UHR modes for BSSIDs in an MBSSID Set, to enable network to apply different SSID specific policy.
  Two possible options are proposed to enable this flexibility

## Slide 9: SP1
Do you support that BSSIDs in a multiple BSSID Set can have different PHY generations in UHR?
A Tx BSSID can be non-UHR EHT BSSID or a UHR BSSID
When Tx BSSID is a non-UHR EHT (11be):
  a nontransmitted BSSID can be UHR and carries UHR elements (UHR Operation, UHR Capabilities, UHR Operating Modes etc.) in its nontransmitted BSSID profile. Tx BSSID beacon sets fields in Capability Information and in TIM IE for UHR critical updates (as defined in D1.0)
  a nontransmitted BSSID can be non-UHR EHT (11be) and inherits EHT Operation and EHT Capabilities element from Tx BSSID (per baseline behavior)
When Tx BSSID is UHR:
  a nontransmitted BSSID can be a non-UHR EHT (11be) BSSID, and has the UHR elements (UHR Operation, UHR Capabilities, UHR Operating Modes etc.) listed in the Non-Inheritance element in its nontransmitted BSSID profile.
  a nontransmitted BSSID can be a UHR BSSID, and inherits at least UHR Capabilities from Tx BSSID
    TBD: Inheritance of UHR Operation element

## Slide 10: SP2
Do you support that BSSIDs in an MBSSID Set can support different enablement status or different parameters for UHR modes as per rules below?
  Support same enablement status across all UHR BSSIDs in an MBSSID set for: NPCA, DSO, AP PUO, DBE, DPS (mobile-AP) (since these are radio level modes)
  Allow different BSSID specific enablement for: P-EDCA and LLI (since these are not radio level, related to LL support and policy can be BSS specific)
  Allow different BSSID specific parameters for: P-EDCA and DUO (for policy reasons)

## Slide 11: SP3
Which option do you choose to support different enablement status and/or different parameters for UHR modes for BSSIDs in an MBSSID Set?
Option 1: Allow UHR Operation element to be carried in a nontransmitted BSSID profile, indicating different enablement status and/or parameters for desired UHR modes. In this case UHR Operation element is not inherited when enablement status and/or parameters are different and instead carried in the nontransmitted BSSID profile.
Option 2: Define a new UHR Operating Modes element that carries enablement status and/or parameters only for UHR modes that are BSSID specific. The new element may be inherited (if same) or overwritten (if different) for a nonTx BSSID. Other UHR modes are carried in UHR Operation element that is always inherited for every UHR nonTx BSSID.