## Slide 1: DBE Operation with DSO
Authors:
Date: 2025-09-15

## Slide 2: Introduction
11bn D1.0 [1] defines DBE and DSO operating modes
When AP supports DBE, it can dynamically expand its operating BW to operate over a DBE BW that is >BSS BW, for DBE supporting STAs.
11bn D1.0, defines DSO mode to be over the BSS BW
  “DSO is a mechanism where a DSO non-AP STA that has an operating bandwidth narrower than the DSO AP can dynamically be allocated frequency resources outside of its current operating bandwidth within the DSO AP’s BSS bandwidth, on a per-TXOP basis.”
Enterprise deployments where BSS BWs are typically low (20/40/80 MHz) due to frequency reuse, can benefit from using DSO when the BW is expanded with DBE
  When operating in DBE mode, an AP can use DSO for STAs that support DSO and DBE, to move those STAs to DSO subbands over the DBE BW.
In this presentation, we propose behavior for DBE operation with DSO, with the goal to minimize changes needed for using DSO over the DBE BW.

## Slide 3: DBE Operation with DSO (1)
For DBE and DSO operation, considering 80 and160 MHz STAs as examples
If a STA supports & enables both DBE and DSO, then can be moved to DSO subbands in the DBE BW
A BSS can benefit from DBE BW (160/320 MHz) even if only few STAs can operate over that DBE BW, if there are DSO STAs that can be moved to DSO subbands in the DBE BW
80 MHZ STAs:
  STA indicates max BW capability to be 80 MHz in baseline BW capability indication
  STA indicates DBE support (with max DBE BW of 80 MHz) and enables DBE
  STA indicates DSO Support and enables/negotiates one 80 MHz DSO subband
  AP initially operating over 20/40 BSS BW, expands to DBE BW of 160 or 320 MHz
  Then such a STA can be moved to 80 MHz DSO subbands in S80 or S160 (per DSO rules) – since STA supports/enables both DBE and DSO
160 MHz STAs:
  STA indicates max BW capability to be 160 MHz in baseline BW capability indication
  STA indicates DBE support (with max DBE BW of 160 MHz) and enables DBE
  STA indicates DSO Support and enables DSO for S160 MHz DSO subband
  AP initially operating over 20/40 BSS BW, expands to DBE BW of 320 MHz
  Then such a STA can be moved to S160 DSO subband – since STA supports/enables both DBE and DSO

## Slide 4: DBE Operation with DSO – Example 1
DSO over DBE BW when associated STA are 80/160 MHz STAs
After DBE mode is enabled, AP performs DSO for 80/160 STAs that support/enable DSO & DBE over the DBE BW by moving DSO STAs to S80 and/or S160 (per DSO rules). After DBE mode is disabled, no DSO by the AP.
STAs can enable DSO and DBE before DBE mode is enabled (to avoid gold-rush of DSO enablements to the AP)

## Slide 5: DBE Operation with DSO – Example 2
DSO over DBE BW when associated STA are 20/80/160 MHz STAs
DSO can be performed for 20 MHz STAs even before DBE enabled over BSS BW
After DBE mode is enabled, AP can additionally perform DSO for 80/160 STAs that support/enable DSO & DBE over the DBE BW by moving DSO STAs to S80 and/or S160 (per DSO rules). After DBE mode is disabled, no DSO for 80/160M STAs

## Slide 6: DBE Operation with DSO (2)
Capability indication: AP & STA indicate capability for using DSO over the DBE BW
  DBE Support = 1: indicates that STA/AP is capable of operating over the DBE BW up to the max BW capability indicated by the STA.
  D1.0 DSO Support = 1: indicates that STA/AP is capable of DSO per DSO procedure/rules for 20/80/160 MHz STAs – e.g. an 80MHz STA can be moved to other 80MHz DSO subbands, a 160MHz STA can be moved to S160 DSO subband. An AP supports moving STAs to allowed DSO subbands.
  STA that sets both DBE Support = 1 and DSO Support =1: indicates that STA can operate up to its max BW capability over the DBE BW and can be moved to relevant DSO subbands
    E.g. If a STA’s max supported BW capability is 80 MHz, and it sets both DBE Support and DSO Support to 1, then STA supports moving to DSO subbands over 160/320 MHz DBE BW.
  AP that sets DBE Support = 1 and DSO Support = 1: indicates that it can perform BW expansion up to AP’s max DBE BW capability and supports scheduling STAs to 20/80/160 DSO subbands in those DBE BWs.
  These existing capability fields suffice for supporting DSO operation over DBE BW. No new capability field is needed.

## Slide 7: DBE Operation with DSO (3)
Enabling use of DSO for DBE BW by the AP:
  In 11bn D1.0, there is no dynamic enable/disable for DSO from the AP side in UHR Operation
  DSO is always enabled for AP to use if supported (per DSO Support =1)
  DBE is explicitly enabled by the AP by setting DBE Enabled = 1
  When an AP that supports DSO also enables DBE, it implies that the AP can perform DSO over the DBE BW (since AP supports performing DSO over all possible DSO subbands)

## Slide 8: DBE Operation with DSO (4)
Enabling DSO for DBE BW by the Non-AP STA:
  A non-AP STA uses OMP procedure (per 11bn D1.0) to enable DBE and DSO modes with the AP
  When a non-AP STA enables/negotiates DSO, STA can be moved to negotiated DSO subbands
  A non-AP STA must enable both DBE and DSO for AP to use DSO over the DBE BW
  Proposal: For DSO over DBE BW, we should allow DBE non-AP STAs to perform DSO enable/negotiation with the AP using OMP up to the max supported DBE BW by the AP
    Example: if BSS BW is 40 MHz, and AP supports DBE up to 320 MHz, then DSO and DBE supporting STAs can perform DSO negotiation up to 320 MHz
    Non-AP STAs should perform DSO enable/negotiation over max DBE BW in advance of DBE mode enablement, to avoid gold rush of STAs performing DSO enable/negotiation after DBE mode enablement
    When DBE mode enablement is being announced, then STA performs DSO calibration per its prior OMP negotiation for DSO
    If DBE BW is changed, then non-AP STA can renegotiate DSO with the AP using OMP. E.g. if DBE BW changes from 160->320, then STA can renegotiate for using S160 for DSO subband (if desired).
    AP should also support receiving DSO enable/negotiation after DBE mode is enabled

## Slide 9: Conclusion
In enterprise deployments where BSS BWs are typically low (20/40/80 MHz) due to frequency reuse, BSS can benefit from using DSO when the BW is expanded with DBE
A BSS can benefit from DBE BW (160/320 MHz) even if only few STAs can operate over the expanded DBE BW, if there are DSO STAs that can be moved to DSO subbands in the DBE BW
When an AP supports DSO and DBE, it can move DSO & DBE supporting STAs to DSO subbands in the DBE BW, if those STAs have enabled DSO & DBE
DSO can be supported over DBE BW w/o new signaling, by adding some rules:
  Existing DBE and DSO capability fields suffice for supporting DSO over DBE BW
  When an AP that supports DSO also enables DBE, then AP can perform DSO over the DBE BW
  For DSO over DBE BW, allow DBE non-AP STAs to perform DSO enable/negotiation using OMP up to maximum supported DBE BW by the AP (even before DBE mode is enabled to avoid gold rush of STAs)
  STA can perform DSO calibration when DBE enablement is being announced, to get ready for DSO operation after DBE is enabled
  AP also supports receiving DSO enable/negotiation after DBE mode is enabled

## Slide 10: Straw Poll (1)
SP1:
Do you support that an AP can use DSO over the DBE BW when DBE mode is enabled, for a non-AP STA that supports and have enabled both DBE and DSO?
  AP performs DSO per the OMP negotiation for DSO performed for that non-AP STA

## Slide 11: Straw Poll (2)
SP2:
Do you support that a DBE non-AP STA can perform DSO enablement/ negotiation with the AP for up to the maximum supported DBE BW by the AP, using the OMP procedure defined for DSO?
SP3:
Do you support that a DBE non-AP STA should perform DSO enablement/ negotiation with the AP for up to the maximum supported DBE BW of the AP, in advance of DBE mode enablement, to avoid gold-rush of DSO enablement/ negotiation after DBE mode is enabled?

## Slide 12: Straw Poll (3)
SP4:
Do you support that when the DBE BW is updated to a different BW (e.g. 160 to 320 MHz), a non-AP STA that has enabled both DBE and DSO can perform DSO renegotiation with the AP using the OMP procedure?