## Slide 1: CBF/CSR Frame Exchange Sequence Further Details
Date: 2024-08
Authors:
Name | Affiliation | Address | Phone | Email
Kaiying Lu | MediaTek | 2840 Junction Ave., San Jose, CA | 408-3872160 | Kaiying.lu@mediatek.com
Eric Pc | MediaTek |  |  | 
James Yee | MediaTek |  |  | 

## Slide 2: Background and Issue1
For a Co-BF coordinated AP to accept a Co-BF invitation, it must prepare and finalize a significant amount of information within a short time (aSIFSTime) after receiving the Invite frame. This includes selecting a candidate STA list, verifying STA status, determining PHY transmission parameters, and more.
Similarly, the CoBF joint PPDU must be transmitted aSIFSTime after the end of the CoBF Trigger frame. The Co-BF coordinated AP must prepare the DL PPDU based on information shared in the CoBF Trigger frame.
As a result, paddings may be required in the CoBF Invite frame and CoBF Trigger frames to provide the coordinated AP sufficient time to process this information. The coordinated AP begins handling these tasks at the start point of the padding bits in these frames.
However, if an FCS check fails at the end of the Co-BF Invite or Co-BF Trigger frame, the coordinated AP must cancel all ongoing preparations and release any allocated resources and status related to the process. Given that Co-BF coordination involves substantial preparation, error recovery would significantly complicate implementation.

## Slide 3: Proposal
11bn shall allow the CoBF Invite frame and CoBF Trigger frame to include IFCS field if the coordinated AP requires non-zero padding in these frames.
  During the setup of an MAPC negotiation agreement for a Co-BF scheme, an AP may inform a peer coordinating AP of its padding requirements for the Co-BF Invite frame and the Co-BF trigger frame.
  The AP may also indicate to the peer coordinating AP whether it requests the inclusion of an IFCS field in the Co-BF Invite frame and Co-BF Trigger frame.
  When the peer coordinating AP invites this AP (as a Co-BF coordinated AP) to participate a Co-BF transmission TXOP, it shall include an IFCS field in the Co-BF Invite frame and the Co-BF Trigger frame if this AP has indicated non-zero padding requirements and the need for IFCS.

## Slide 4: SP1
Do you support that a Co-BF coordinating AP shall include an IFCS field in the Invite frame and MAPC Trigger frame if the Co-BF coordinated AP has indicated non-zero padding requirements during the MAPC negotiation agreement setup procedure for Co-BF scheme?
  Note: An “IFCS request” indication may be negotiated as part of the MAPC negotiation agreement setup procedure.

## Slide 5: Background and Issue 2: Extended TimeOut
AP2
(shared AP)
Response
ICF1
ICR2
CBF/CSR PPDU
CBF/CSR PPDU
MAPC
Trigger
Invite
ICR1
ICF2
BA1
BA2
MU-BAR2
MU-BAR1
MAPC
Trigger
CBF/CSR PPDU
CBF/CSR PPDU
AP1
(sharing AP)
AP1-STA(s)
AP2-STA(s)
The coordinating AP must indicate an extended timeout value in its ICF1 to its EMLSR or DPS clients. This value depends not only on the duration of its own transmission (e.g., MAPC Trigger) but also on the length of the coordinated AP’s frame exchange with its associated non-AP STAs (ICF2/ICR2, MU-BAR2/BA2).
Similarly, the coordinated AP must indicate an extended timeout value in its ICF2 to its EMLSR or DPS clients. This value depends on the transmission duration from the coordinating AP, which may include the MAPC Trigger frame, MU-BAR1/BA1 or BA1 if MU-BAR information is aggregated in the Co-BF PPDU.
The extended timeout value must be sufficiently long to cover all relevant silent periods. This ensures that EMLSR or DPS clients do not switch back to listening operation or LC mode prematurely and miss the Co-BF PPDU transmission. At the same time, the timeout should not be overly conservative, to avoid unnecessary power consumption at the client or missed transmission opportunities.
However, variations in the selected data rates for MAPC Trigger frame, ICF/ICR, MU-BAR/BA can lead to significant differences in frame length. The variability makes it challenging for a peer AP to accurately estimate and set the appropriate extended timeout value in its ICF.
Silent period
Silent period
Silent period
Silent period
Silent period

## Slide 6: Proposal
A Co-BF/Co-SR coordinating AP shall include the extended timeout information in the Invite frame for the coordinated AP to set the extended timeout interval in its ICF if exist?
  E.g., The extended timeout information is based on the larger duration of MAPC Trigger frame and MU-BAR/BA frame exchange between the coordinating AP and its associated non-AP STAs.
The coordinated AP shall include the extended timeout information in the Response frame for the coordinating AP to set the extended timeout interval in its ICF if exist.
  E.g., The extended timeout information is based on the larger duration of ICF/ICR and MU-BAR/BA frame exchange between the coordinate AP and its associated non-AP STAs

## Slide 7
SP2: Do you support that the coordinating AP shall include the extended timeout information in the Invite frame for the coordinated AP to set the extended timeout interval in its ICF if exists?
  E.g., the extended timeout information is based on the larger duration of MAPC Trigger frame and MU-BAR/BA frame exchange between the coordinating AP and its associated non-AP STAs.
SP3: Do you support that the coordinated AP shall include the extended timeout information in the Response frame for the coordinating AP to set the extended timeout interval in its ICF if exists?
  E.g., the extended timeout information is based on the larger duration of ICF/ICR and MU-BAR/BA frame exchange between the coordinate AP and its associated non-AP STAs

## Slide 8: Reference
[1] IEEE802.11bn Draft 1.0