## Slide 1: MAPC Negotiation Further Details
Date: 2025-09
Authors:
Name | Affiliation | Address | Phone | Email
Kaiying Lu | MediaTek | 3201 Vernazza Ave. San Jose, CA, USA |  | Kaiying.lu@mediatek.com
James Yee | MediaTek |  |  | 

## Slide 2: Background and Problem Statement
IEEE 802.11bn Draft 1.0 defines a MAPC framework that includes multiple schemes such as Co-BF, Co-SR, Co-TDMA, Co-RTWT, and Co-CR.
An AP may initiate a MAPC negotiation as an MAPC requesting AP for one or more MAPC schemes with another AP as an MAPC responding AP.
When multiple BSSID sets or Co-hosted BSSID sets are involved in such a negotiation, it becomes highly inefficient and impractical for each virtual AP within one set to negotiate individually with each virtual AP in another set due to complicated MAPC agreement management and more hardware resource to store the information.

## Slide 3: Discussion: MAPC Coordination in MBSSID Environment
Virtual APs within a single set share the same physical radio and medium access resources. The MAPC negotiation process must facilitate successful negotiation and execution of MAPC operations between physical devices. Adherent to the standard is mandatory; However, the internal management of MAPC capabilities across virtual APs remains an implementation-specific detail.
when an AP participating in MAPC negotiation (as either a requester or responder) belongs to a multiple BSSID set or a Co-hosted BSSID set, efficiency is gained by treating the entire set as a unified entity. This approach allows for a single agreement on MAPC scheme(s) and the assignment of an AP ID to the peer AP (or peer AP set).
As defined in 802.11 baseline, a cohosted BSSID set compromises HE BSSs that are not part of a multiple BSSID set (i.e., dot11MultiBSSIDImplemented is false) but share the same operating class, channel, antenna connectors.
For UHR APs that establish virtual APs and support MAPC schemes, implementing a multiple BSSID set is more efficient than a Co-Hosted BSSID set. This architecture provides a stronger foundation for unified MAPC negotiation and resource management.

## Slide 4: MAPC BSSID & Max MAPC BSSID Indicator
During an MAPC agreement establishment or update procedure, an MAPC AP/Set may initiate MAPC Negotiation Request/Response Frame exchange which shall carry MAPC BSSID and Max MAPC BSSID Indicator.
  MAPC BSSID indicates the reference identifier/BSSID for an MAPC AP/Set
    the MAPC BSSID is the transmitted BSSID of a MBSSID set or the BSSID of a member of the co-hosted BSSID set
    the MAPC BSSID is the BSSID of the MAPC AP if it does not belong to an AP set
  Max MAPC BSSID Indicator with a value of n indicates the maximum number of BSSIDs in the MAPC BSSID set of which an MAPC AP belongs to.
    Max MAPC BSSID Indicator has a smaller or the same value as Max Co-Hosted BSSID Indicator or MaxBSSID Indicator.
    Max MAPC BSSID Indicator has the value of 0 if the MAPC AP does not belong to an AP set.
  Members of the MAPC BSSID set have the same 48 – n bits (BSSID[0:(47 – n)]) in their BSSIDs.
    Each member of the MAPC BSSID set may use the same MAPC BSSID as its identifier or its own BSSID in the frame it transmits to the peer MAPC AP/Set.
    Each member of the MAPC BSSID set shares the same AP ID assigned by the peer MAPC AP/Set during the MAPC agreement establishment or update procedure
MAPC common info length | MAPC Capabilities | MAPC Parameters | AP ID | MAPC BSSID | Max MAPC BSSID Indicator
0 or 6
0 or 1
MAPC Common Info Field Format
0 or 2
1
1
1
Octets:

## Slide 5: MAPC BSSID & Max MAPC BSSID Indicator
MAPC BSSID and Max MAPC BSSID Indicator can be carried in MAPC Common info field of MAPC element if needed by at least one MAPC scheme agreement to be established or updated.
“MAPC BSSID and Max MAPC BSSID Indicator Present” indication can be carried in MAPC Control field of MAPC element.
  the MAPC BSSID field and the Max MAPC BSSID Indicator field are present in the MAPC Common info field of MAPC element, if the “MAPC BSSID and Max MAPC BSSID Indicator Present” indicates present.
AP ID Present | MAPC BSSID and Max MAPC BSSID Indicator Present | Reserved
1 bit
6 bits
MAPC Control Field Format
1 bit

## Slide 6: Usage Example of MAPC AP ID
During an MAPC agreement establishment or update procedure, MAPC requesting and responding AP/Set assign an AP ID to each other. The assigned AP ID is shared by all members of the MAPC BSSID set identified by the MAPC BSSID and Max MAPC BSSID Indicator.
The TA and/or RA field of a unicast frame exchange between the pair of MAPC APs during the coordination operation can use the MAPC BSSID or an BSSID of the MAPC AP which is a member of the MAPC BSSID set identified by the MAPC BSSID and Max MAPC BSSID Indicator.
The intended recipient MAPC AP can identify that it is the intended recipient by the RA field or AID12 subfield of the User Info field with AP ID assigned by its peer MAPC AP identified by TA field.

## Slide 7: Summary
This contribution addresses some challenges in MAPC negotiation arising from the deployment of virtual APs that support MAPC schemes.
We propose treating a unified MAPC BSSID set as a single entity – whether acting as an MAPC negotiation requester or responder. This approach enables the establishment of a single agreement on MAPC scheme(s) and streamlines the assignment of an AP ID to the peer AP (or peer AP set).

## Slide 8: SP1
Do you support that if an AP set - such as a Co-hosted BSSID set, an MBSSID set sharing the same operating class, channel, and antenna connectors – shall be treated as an MAPC BSSID Set and is assigned an AP ID by a peer AP/AP set during a MAPC negotiation procedure?
  Virtual APs in the MAPC BSSID set inherit the same AP ID assigned by the peer AP/AP set, without the need for separate MAPC negotiations

## Slide 9: SP2
Do you support to define a Max MAPC BSSID as the reference BSSID of the MAPC BSSID set and a Max MAPC BSSID Indicator for the MAPC BSSID set to indicate the maximum number of BSSIDs in the MAPC BSSID set?
  Max MAPC BSSID Indicator with a value of n indicates the maximum number of BSSIDs in the MAPC BSSID set.
  Members of the MAPC BSSID set have the same 48 – n bits (BSSID[0:(47 – n)]) as that of the reference BSSID of the MAPC BSSID set
  Value of 0 indicates that the MAPC AP does not belong to an MAPC BSSID set.

## Slide 10: Reference
[1] 802.11bn Draft 1.0.