## Slide 1: Co-TDMA Transmission Bandwidth
Date: 2025-09
Authors:
Name | Affiliation | Address | Phone | Email
Kaiying Lu | MediaTek | 2840 Junction Ave. San Jose, CA, USA |  | Kaiying.lu@mediatek.com
James Yee | MediaTek |  |  | 

## Slide 2: Background
The Co-TDMA procedure enables an AP to share a time portion of an obtained TXOP with another AP that belongs to a set of APs to transmit one or more PPDUs.
The figure below shows an example of Co-TDMA procedure that includes a polling phase, a TXOP allocation phase, and a TXOP return phase
Sharing AP(AP1)
ICF
To AP2 & AP3
Frame exchange(s) among AP1 and its STA(s)
Polled AP(AP2)
ICR to AP1
MU-RTS TXS to AP3
CTS to AP1
Polling phase
TXOP allocation phase
Frame exchange(s) among AP3 and its STA(s)
TXOP return to AP1
TXOP return phase
Polled AP(AP3)
ICR to AP1

## Slide 3: Problem Statement 1
A coordinating AP and its coordinated AP(s) must share the same primary 20MHz channel but may operate with the same or different available bandwidth.
During the Co-TDMA polling phase, ac coordinating AP that obtains a TXOP may transmit an ICF across its available bandwidth.
The BSRP NTB or TB ICF may specify a UL BW or allocate RU(s) to the polled AP(s) within their respective bandwidths. A polled AP may respond with an ICR only if the channel is available within the indicated BW or allocated RU; otherwise, it must not respond. consequently, the channel availability at the polled AP can affect whether the coordinating AP successfully obtains the TXOP.
To improve the likelihood of securing the TXOP, the coordinating AP may prefer to indicate a uplink bandwidth or allocate an RU within a narrower bandwidth – such as 20MHz – to the polled AP. However, the bandwidth of the ICR response may subsequently restrict the bandwidth available for the coordinating AP’s in-BSS frame exchanges after the polling phase, in accordance with baseline TXOP BW rules.

## Slide 4: Proposal on Co-TDMA In-BSS Transmission Bandwidth
  During In-BSS transmissions within the TXOP, the coordinating AP may initiate frame exchanges with its associated STA(s) using the bandwidth established by the ICF during the polling phase, irrespective of the bandwidth of the ICR received from the polled AP.
  For example:
    The coordinating AP transmits a BSRP NTB ICF with a bandwidth of 160MHz
    The UL BW indicated for the polled AP is 20MHz.
    The polled AP successfully responds with an ICF on the primary 20MHz channel.
    Subsequent in-BSS frame exchanges may utilize the full 160MHz bandwidth, as bounded by the original ICF.
Sharing AP(AP1)
ICF
Frame exchange(s) among AP1 and its STA(s)
Polled AP(AP2)
ICR
Polling phase
20MHz
160MHz
160MHz
…
…

## Slide 5: Problem Statement 2
During the Co-TDMA TXOP allocation phase, a Co-TDMA coordinated AP must transmit the PPDU carrying the CTS frame on the 20 MHz channel(s) indicated in the RU Allocation field of the User Info field within the MU-RTS TXS Trigger frame that allocated the transmission time to it.
However, if the Co-TDMA coordinated AP detects activity on any 20MHz channel within the allocated RU Allocated, it cannot transmit the CTS frame and must relinquish the assigned transmission opportunity.
This scenario may arise when the devices that are hidden from the coordinating AP - but not from the coordinated AP - initiate transmissions during an in-BSS transmission of the coordinating AP. Such transmissions may render one or more 20 MHz channels unavailable to the coordinated AP.

## Slide 6: Proposal on Co-TDMA TxOP Allocation Phase
  During the Co-TDMA TXOP allocation phase, the PPDU carrying the CTS frame from a Co-TDMA coordinated AP shall be transmitted on the 20 MHz channel(s) indicated in the RU Allocation field of the User Info field of the MU-RTS TXS Trigger frame
  The number of 20MHz channels used for the CTS frame may be less than or equal to the allocated RU size based on channel availability status.
  Note: The coordinating AP is not required to be aware of the bandwidth of the CTS frame
Sharing AP(AP1)
ICF
Frame exchange(s) among AP1 and its STA(s)
Coordinated AP(AP2)
ICR
MU-RTS TXS
CTS
Polling phase
TXOP allocation phase
Frame exchange(s) among AP2 and its STA(s)
160MHz
20MHz
160MHz
< = 80MHz

## Slide 7: Summary
This contribution discusses specific details regarding the Co-TDMA TXOP polling phase and allocation phase.
  Polling phase: the ICR bandwidth should not constrain the BW of the in-BSS transmission
  Allocation phase: 20MHz channels used by the CTS frame may be less than or equal to the size of the allocated RU
Key Benefits
  Reduces the likelihood of the coordinating AP losing the TXOP
  Ensures sufficient bandwidth for in-BSS frame exchanges, while minimizing negative impacts from time-sharing with other AP
  Increases the probability that the coordinated AP can successfully utilize the allocated time

## Slide 8: SP1
8
Do you support that during the in-BSS transmission within the Co-TDMA TXOP, the coordinating AP may initiate frame exchange with its associated STA(s) within the bandwidth of ICF obtained during the polling phase, regardless of the bandwidth of ICR from the polled AP.

## Slide 9: SP2
9
Do you support that during the Co-TDMA TXOP allocation phase, the number of 20MHz channels used for the CTS frame may be less than or equal to the allocated RU size
  Note: The coordinating AP is not required to be aware of the bandwidth of the CTS frame

## Slide 10: Reference
[1] 11bn Draft 1.0