## Slide 1: NPCA Consideration for NSTR
Date: 2025-10-13
Authors:
Name | Affiliations | Address | email
Haorui Yang | China Mobile | Hangzhou, Zhejiang, China | yanghaorui0217@163.com

## Slide 2: Introduction
The feature NPCA has been specified in 802.11bn D1.0[1].
In 802.11be, the NSTR operation was introduced considering the non-AP MLD radio capability.
  In 11be, the EDCA is performed per link and the NPCA is naive to follow this logic.
When NPCA is introduced to NSTR non-AP MLD, there is some issue to be considered.

## Slide 3: Issue
Case 1: the transmission over one NSTR link at non-AP STA is prohibited due to UL transmission by NPCA on the other link of the same NSTR link pair.
  NPCA is triggered over the NSTR Link 1, during which the non-AP STA2 wins the EDCA contention and cannot initiate the transmission due to NSTR limitation.
non-AP STA 1
non-AP STA 2
AP 1
AP 2
NPCA for UL
TXOP
TXOP
Time
MU EDCA
NSTR non-AP MLD
AP MLD
NSTR Link 1
NSTR Link 2

## Slide 4: Issue
Case 2: the transmission over one NSTR link at non-AP STA is prohibited due to the DL transmission by NPCA on the other link of the same NSTR link pair.
  AP1 obtains TXOP by performing NPCA to send DL PPDU or trigger non-AP STA1 for UL PPDU, which prevent the non-AP STA2 from transmitting due to NSTR limitation.
non-AP STA 1
non-AP STA 2
AP 1
AP 2
NPCA for DL
TXOP
TXOP
Time
MU EDCA
NSTR non-AP MLD
AP MLD
NSTR Link 1
NSTR Link 2

## Slide 5: Issue
Transmission over one NSTR link is prohibited due to the NPCA “bonus TXOP” over the other link of the same NSTR link pair, which cause longer delay and is not fair.
  The transmission over the NSTR Link 2 should have obtained TXOP but now it has to be delayed after NPCA.
non-AP STA 1
non-AP STA 2
AP 1
AP 2
NPCA
TXOP
TXOP
Time
MU EDCA
NSTR non-AP MLD
AP MLD
NSTR Link 1
NSTR Link 2

## Slide 6: Solution
Solution 1: NPCA cannot be performed over the NSTR link pair.
  A simple solution but may waste some opportunity if no NSTR limitation happens.
Solution 2: the TTLM is updated to make all the service use the link utilizing the NPCA.
  Since NPCA happens during the OBSS TXOP which is not a long duration, the TTLM updating will happen frequently and not in time.

## Slide 7: Solution
Solution 3: the STA obtaining TXOP by NPCA can share a portion of its TXOP to another STA in the same non-AP/AP MLD, if needed.
  For Case 1
    The non-AP STA2 requests the non-AP STA1 to share TXOP then sets its TXOP duration to the shared time, e.g. as the duration field of RTS.
    How to determine the shared portion is left to implementation.
  For Case 2
    The non-AP STA2 requests AP2 to ask AP1 to share TXOP and AP2 responses with the shared time.
    The non-AP STA2 sets its TXOP duration to the shared time, e.g. as the duration field of RTS.
    How to determine the shared portion is left to implementation.

## Slide 8: Summary
This submission discusses the case when one non-AP STA obtains TXOP by NPCA resulting to the loss of transmission over the other link of the same NSTR pair.
  This reduces the transmission performance degradation over the other NSTR link and also is not fair.
There are 3 solutions proposed and the Solution 3 is preferred that the STA shares a part of TXOP to another STA in the same NSTR link pair to guarantee the QoS of transmission.

## Slide 9: References
[1]: IEEE Std 802.11bn D1.0