## Slide 1: Follow Up Discussion on Co-BF/Co-SR Valid Reject Reasons
Date: 2025-09-15
Authors:
Name | Affiliations | Address | Phone | Email
Mahmoud Hasabelnaby | Huawei |  |  | Mahmoud.Hasabelnaby@huawei.com
Junghoon Suh |  |  |  | 
Osama Aboul-Magd |  |  |  | 
Yan Xin |  |  |  | 
Abdallah Hussein |  |  |  | 

## Slide 2: Co-BF Transmission Reject Reasons
According to motion #480 [1-2]:
  A Shared (Responding) AP may reject a Co-BF/Co-SR transmission or Co-BF sounding invitation received from a Sharing (Initiating) AP.
    In case of rejection, the Shared (Responding) AP can include the reason for rejection in the Co-BF/Co-SR Response or Co-BF Sounding Response frame.
    Reasons for rejecting a Co-BF/Co-SR transmission or Co-BF sounding invitation are TBD.
In case of rejection, it is important to allow the coordinated AP to include its reject reason(s) (if applicable) in response to a received invitation from the Coordinating AP [3]. This reject reason can help the two APs address an existing failure or issue or be considered in future invitations.
Accordingly, a Co-BF/Co-SR Status Code field is included in the Co-BF/Co-SR Response frame to indicate whether the Co-BF/Co-SR Coordinated AP accepts the Co-BF/Co-SR invite from the Co-BF/Co-SR Coordinating AP, and the reason for rejection if the Co-BF/Co-SR invite is not accepted [4].
In this contribution, we define valid reject reasons for Co-BF/Co-SR transmission invitations.

## Slide 3: Common Reject Reasons for Co-BF/Co-SR (1/2)
Some valid reject reasons are common for rejecting a Co-BF/Co-SR transmission invitation, such as:
  Unspecified Reason: The coordinated AP may choose not to provide a specific reason for rejecting the invitation, indicating an unspecified failure.
  Reject due to Unavailability of the Coordinated AP: The coordinated AP may be temporarily unavailable (e.g., due to in-device coexistence issues or other SP-based MAPC agreements like Co-RTWT) and unable to participate in a Co-BF or Co-SR transmission, or Co-BF Sounding.
  Reject due to Unavailability of the Coordinated AP’s non-AP STAs: The coordinated AP’s associated non-AP STAs, which are eligible for Co-BF sounding, have already been Co-BF sounded for a Co-BF transmission, or are eligible for a Co-SR transmission, may be temporarily unavailable and unable to participate in a Co-BF or Co-SR transmission, or Co-BF Sounding.
  Reject due to No Pending DL Buffered Data: At the time of the Co-BF or Co-SR transmission invitations, the coordinated AP may not have any pending downlink (DL) buffered transmissions for the sounded non-AP STAs in the case of Co-BF or for eligible non-AP STAs in the case of Co-SR.

## Slide 4: Common Reject Reasons for Co-BF/Co-SR (2/2)
Some valid reject reasons are common for rejecting a Co-BF or Co-SR transmission invitation, such as:
  Reject due to Invalid Parameters: one or some parameters included in the Co-BF/Co-SR Invite frame or the Co-BF Sounding Invite frame may mismatch the desired parameters of the Coordinated AP. The Coordinated AP may not specify which parameter(s) are mismatched.
  Reject due to other reasons outside the scope of the standard: There may be reasons outside the scope of the standard that prevent the Coordinated AP from accepting a Co-BF or Co-SR transmission invitation, at a particular time.
As a result, we propose utilizing some status codes within the Co-BF Status Code or Co-SR Status Code to represent the aforementioned rejection reasons. These status codes can be used by a Coordinated AP to reject a Co-BF/Co-SR transmission invitation.

## Slide 5: Specific Reject Reasons for Co-BF/Co-SR (1/2)
In addition to the common reject reasons, there are some valid reject reasons specific to rejecting a Co-BF transmission invitation, such as:
  Reject due to Failure in Co-BF Sounding: The Co-BF Coordinated AP shall reject a Co-BF transmission invitation if it has not successfully received the cross-BSS CSI reports from the Co-BF Coordinating AP’s associated non-AP STAs, or if it detects that the CSI reports (cross-BSS and in-BSS) from its associated non-AP STAs are expired or invalid.
    Note: This reject reason may be split into two distinct reasons: a) Reject due to Failure to receive the cross-BSS CSI reports. b) Reject due to Expired or invalid CSI reports.
  Reject due to specific parameter(s) mismatch: The Co-BF Coordinated AP may declare that it rejects the Co-BF transmission due to specific parameter(s) included in the Co-BF Invite frame that may mismatch its desired parameters value such as: a) Reject due to Bandwidth Mismatch. b) Reject due to Punctured Channel Pattern Mismatch. c) …..

## Slide 6: Specific Reject Reasons for Co-BF/Co-SR (2/2)
In addition to the common reject reasons, there are some valid reject reasons specific to rejecting a Co-SR transmission invitation, such as:
  Reject due to Invalid Transmit Power Limit: The Co-SR Coordinated AP shall reject a Co-SR transmission invitation if it detects that the transmit power limit value, already agreed on during the Co-SR negotiation phase is invalid to serve the associated non-AP STAs it plans to serve.
  Reject due to specific parameter(s) mismatch: The Co-BF Coordinated AP may declare that it rejects the Co-BF transmission due to specific parameter(s) included in the Co-BF Invite frame that may mismatch its desired parameters value such as: a) Reject due to Number of LTF Symbols Limit: This rejection reason has already been adopted under Motion #472. b) …
The Coordinated AP may need to indicate multiple reasons (e.g., more than one reason) for rejecting a Co-BF/Co-SR transmission invitation. For example, the rejection may be based on a mismatch in two or more transmission parameters.
As a result, certain Co-BF/Co-SR Status Codes may be defined to indicate a combination of two or more valid rejection reasons that can occur simultaneously.
However, careful consideration is needed regarding which combinations of reject reasons are valid to include in the Co-BF/Co-SR Status Code.

## Slide 7: Summary
In case of rejection, it is important to allow the coordinated AP to include its reject reason(s) (if applicable) in response to a received invitation from the Coordinating AP. This reject reason can help the two APs address an existing failure or issue or be considered in future invitations.
In this contribution, we discussed some valid reject reasons for Co-BF/Co-SR transmission invitations.

## Slide 8: References
11-25/865r0, “Considerations on Co-BF Sounding Failure”.
11-24/209r19, “Specification Framework for TGbn”.
11-25/1431r0, “PDT MAC Co-BF and Co-SR Part 2”.
11-25/768r12, “PDT MAC and CR Coordinated Beamforming Protocol”.

## Slide 9: Straw Poll 1
Do you support that a Co-BF Coordinated AP may reject a Co-BF transmission invitation due to one of the following reasons:
  Unspecified Reason.
  Reject due to Unavailability of the Coordinated AP or Coordinated AP’s sounded non-AP STAs.
  Reject due to No Pending DL Buffered Data for the Coordinated AP’s sounded non-AP STAs
  Reject due to a Failure in Co-BF Sounding.
  Reject due to Bandwidth Mismatch.
  Reject due to Punctured Channel Pattern Mismatch.
  Reject due to other reasons outside the scope of the standard
  Other reject reasons are TBD.

## Slide 10: Straw Poll 2
Do you support that a Co-SR Coordinated AP may reject a Co-SR transmission invitation due to one of the following reasons:
  Unspecified Reason.
  Reject due to Unavailability of the Coordinated AP or any Coordinated AP’s non-AP STA eligible for Co-SR
  Reject due to No Pending DL Buffered Data for any Coordinated AP’s non-AP STA eligible for Co-SR
  Reject due to Invalid Transmit Power Limit
  Reject due to Number of LTF Symbols Limit
  Reject due to other reasons outside the scope of the standard
  Other reject reasons are TBD.

## Slide 11: Straw Poll 3
Do you support that certain Co-BF/Co-SR Status Codes may be defined to indicate a combination of two or more valid rejection reasons that can occur simultaneously?