## Slide 1: Enabling Co-BF and Co-SR for Co-RTWT Negotiation and Operation
Authors:

## Slide 2: Recap - MAPC
Multi-AP Communication (MAPC) is being discussed in IEEE 802.11bn Task Group (TG) where an AP forms coordination with an Overlapping Basic Service Set (OBSS) AP to efficiently share the wireless medium and other wireless resources e.g., time, space, transmit power etc. between them for interference mitigation, better medium utilization, increased reliability and improved latency
  The MAPC framework introduces a set of multi-AP coordination schemes such as Coordinated Beam-forming (Co-BF), Coordinated Spatial Reuse (Co-SR), Coordinated Time Division Multiple Access (Co-TDMA) and Coordinated Restricted Target Wake Time (Co-RTWT).
  An AP can establish coordination for one or more coordination scheme(s) with an OBSS AP which supports the same set of coordination scheme(s) via MAPC Discovery and MAPC Negotiation procedures defined in IEEE 802.11 TGbn

## Slide 3: Recap – Co-RTWT
Coordinated Restricted Target Wake Time (Co-RTWT) is being discussed in IEEE 802.11bn Task Group where an AP requests for protection for one or more of its RTWT schedule(s) to an Overlapping Basic Service Set (OBSS) AP where the latter extends protection for one or more of the requested RTWT schedule(s)
  An AP that requests for protection for its RTWT schedule(s) is called a Co-RTWT Requesting AP
  An OBSS AP that extends protection for one or more of the RTWT schedule(s) requested by a Co-RTWT
  Requesting AP is called a Co-RTWT Coordinated AP
  Via Co-RTWT negotiation, a Co-RTWT requesting AP and a Co-RTWT Coordinated AP establish a Co-RTWT agreement corresponding to a requested RTWT schedule
The Co-RTWT negotiation procedure is part of IEEE 802.11bn Multi-AP Coordination (MAPC) negotiation where
  The Co-RTWT requesting AP includes a Co-RTWT scheme sub-element in the Negotiation MAPC element transmitted in an individually addressed MAPC Negotiation Request frame to an OBSS AP that supports Co-RTWT
  The Co-RTWT scheme sub-element includes one or more MAPC Scheme Information field(s) where each contains Co-RTWT parameters corresponding to an requested RTWT schedule that requires protection
  The Co-RTWT coordinated AP responds to accept or reject the protection request via an individually addressed MAPC Negotiation Response frame

## Slide 4: Recap – Co-BF, Co-SR
Coordinated Beamforming (Co-BF) and Coordinated Spatial Reuse (Co-SR) are being discussed in IEEE 802.11 TGbn as multi-AP schemes which enable simultaneous transmissions by coordinating among two or more OBSS APs to increase medium utilization
  Co-BF enables coordination between two APs with multiple antennas where each AP beamforms to the negotiated STAs associated with it
  Co-SR enables coordination among multiple APs by controlling transmit power while transmitting to the negotiated STAs associated with it
  Through coordinated simultaneous transmissions, both Co-BF and Co-SR increases medium utilization, mitigates interference and increases reliability of transmission
In IEEE 802.11 TGbn, Co-BF and Co-SR negotiation procedures are defined similar to Co-RTWT negotiation where MAPC Negotiation Request and Response frame corresponding to each MAPC scheme contain respective scheme sub-elements inside MAPC element
  A Co-BF scheme sub-element inside a MAPC element contains parameters related to a Co-BF agreement
  A Co-SR scheme sub-element inside a MAPC element contains parameters related to a Co-SR agreement

## Slide 5: Enhancements to Co-RTWT
Current IEEE 802.11 TGbn defines protection rules for Co-RTWT where an AP if extends protection of the RTWT schedule(s) of another AP through negotiation or other means, then
  The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)
  The AP, if it has at least one associated STA that is capable of rTWT, shall advertise in the beacon frames it transmits the OBSS rTWT schedule so that its associated STAs supporting rTWT follow the baseline rTWT rules for the OBSS rTWT schedule
In the current protection rule, an AP that agrees to protect RTWT schedule(s) of another AP loses channel access in turn loses transmission opportunities for the entire duration of RTWT Service Periods (SPs)
  This decreases medium utilization efficiency
  If an AP does not agree to protect the RTWT schedule(s) requested by an OBSS AP, then uncoordinated simultaneous transmissions in two BSSs causes a lot of interference to the latency-sensitive traffic flows during RTWT SPs which in turn deteriorates performance
Incentivisation in Co-RTWT feature is currently missing for the AP that is providing protection
  Currently, there is no incentive for the AP extending protection to do so as it is losing channel access for the duration
  Need to bring schemes to incentivize protection for Co-RTWT

## Slide 6: Motivation
Our idea is to incentivise the AP that is extending protection to the AP requesting for Co-RTWT agreement by allowing usage of Co-BF and Co-SR during the protection period
  As part of Co-RTWT agreement, it is negotiated that during a Co-RTWT SP there is also an additional agreement to enable Co-BF and Co-SR
  This incentivises the AP extending protection

## Slide 7: Advantages of the proposed scheme
Current Co-RTWT negotiation restricts the Co-RTWT coordinated AP from continuing its ongoing frame transmission if it has any exchanges in the BSS. The ongoing transmission may be important due to its time-sensitive nature and the coordinated AP may want to continue to use the channel instead of deferring its transmission and stay idle for the entire duration of the Co-RTWT SP.
The proposed scheme improves the chance of negotiation success in Co-RTWT through incentivisation. Currently, there is no incentive for the AP extending protection to do so as it is losing channel access for the duration of the Co-RTWT SP. With proposed scheme, the AP extending protection may continue its transmission by sharing time (Co-TDMA), frequency (Co-NPCA) or spatial resources (Co-SR/ Co-BF) with the Co-RTWT requesting AP.

## Slide 8: Abstract
In this contribution, we introduce additional protection levels in Co-RTWT negotiation procedure
  Enable Co-BF/ Co-SR as part of Co-RTWT agreement
We propose an approach to enable Co-BF and Co-SR as part of Co-RTWT agreement
  We define protection levels for Co-RTWT operation to add Co-BF/Co-SR as part of Co-RTWT negotiation procedure
  We define sequence of exchanges/operation to enable Co-BF and Co-SR incentivising extension of protection in a Co-RTWT negotiation
  We propose to reuse the existing Co-BF and Co-SR procedure as part of Co-RTWT agreement

## Slide 9: Protection levels for Co-RTWT operation
Protection levels:
  We define protection levels for Co-RTWT operation in addition to the current protection mechanism which is to extend protection for the entire duration of a RTWT schedule(s)
    Enable Co-BF agreement as part of extending protection to a requested RTWT schedule
    Enable Co-SR agreement as part of extending protection to a requested RTWT schedule
  We propose to introduce a new field – “RTWT Schedule Protection Level Info” as part of Co-RTWT parameter set
    This can be exchanged along with other Co-RTWT parameters during Co-RTWT negotiation

## Slide 10: Option 1: Co-BF/Co-SR negotiation embedded
Co-RTWT Requesting AP, AP 1
Co-RTWT Coordinated AP, AP 2
R-TWT
STA 11
R-TWT
STA 12
R-TWT
STA 22
R-TWT
STA 21
Co-RTWT Negotiation Request message: Co-RTWT Scheme Information set - RTWT Schedule Protection Level Info (optional), RTWT STA Info (optional) [Req. for protection]
Co-RTWT Negotiation Response message: Co-RTWT Scheme Information set - RTWT Schedule Protection Level Information – enable Co-BF/Co-SR, RTWT STA Information (optional)
[Accept to protect]
Co-BF/Co-SR Negotiation and Agreement: Co-BF/Co-SR Scheme Information Set exchange
Intra-BSS Announcement
Intra-BSS Announcement
Request to initiate Co-BF/Co-SR agreement or initiates directly
(optional)
[Accept to condition]
Co-RTWT Negotiation Confirmation and Agreement formation
(optional)

## Slide 11: Option 1: Co-BF/Co-SR negotiation embedded (Contd.)
Co-BF/Co-SR negotiation and agreement formation that is required as a part of the Co-RTWT negotiation is performed separately i.e., the message exchanges required for Co-BF/Co-SR negotiation is performed independently and in a successive manner after the Co-RTWT negotiation is initiated
  Some parameter exchanges required for Co-BF/Co-SR negotiation e.g., STA Information is optionally exchanged along with Co-RTWT parameter exchanges during the Co-RTWT negotiation phase
The Co-RTWT requesting AP optionally includes the supported modes of protection mechanism, RTWT Schedule Protection Level Information for its requested RTWT schedule(s) in the Co-RTWT Negotiation Request frame and the Co-RTWT responding AP can select the suitable mode (enable Co-BF/Co-SR) supported by it in the Co-RTWT Negotiation Response frame
The final Co-RTWT Negotiation confirmation and agreement formation takes place after both the APs successfully complete the Co-BF/Co-SR negotiation and agreement formation after which an optional confirmation and agreement formation message exchange is performed between the APs
  APs exchange required parameters for Co-BF/Co-SR e.g., no. of Spatial Streams (SS), no. of Tx/Rx antenna, transmit power etc. during Co-BF/Co-SR negotiation. Exact parameters required for Co-BF/Co-SR are TBD
After the Co-RTWT negotiation is completed, The Co-RTWT requesting and responding AP broadcasts the negotiated RTWT schedule(s) and its related parameters and the negotiated protection mechanism to its associated STAs as an intra-BSS announcement which marks the end of Co-RTWT Negotiation phase

## Slide 12: Option 2: Joint Co-BF/Co-SR and Co-RTWT negotiation
Co-RTWT Requesting AP
Co-RTWT Responding AP
R-TWT
STA 11
R-TWT
STA 12
R-TWT
STA 22
R-TWT
STA 21
Co-RTWT Negotiation Request message: Co-RTWT Scheme Information set - RTWT Schedule Protection Level Info (optional), RTWT STA Information, Co-BF/Co-SR Scheme Information set
[Req. for protection]
Co-RTWT Negotiation Response message: Co-RTWT Scheme Information set - RTWT Schedule Protection Level Information – enable Co-BF/Co-SR, RTWT STA Information, Co-BF/Co-SR Scheme Information set
[Accept to protect]
Intra-BSS Announcement
Intra-BSS Announcement
Co-RTWT Negotiation Confirmation and Agreement formation, Co-BF/Co-SR Negotiation Confirmation and Agreement formation

## Slide 13: Option 2: Joint Co-BF/Co-SR and Co-RTWT negotiation (Contd.)
Co-BF/Co-SR negotiation and agreement formation that is required as a part of the Co-RTWT negotiation is performed jointly i.e., the message exchanges for Co-RTWT negotiation may contain Co-BF/Co-SR Scheme Information set(s) required for Co-BF/Co-SR negotiation along with Co-RTWT Scheme Information Set
  Parameter required for Co-BF/Co-SR negotiation e.g., RTWT STA Information, other Co-BF/Co-SR Scheme Information set (e.g., No. of Spatial Streams, No. of Tx/Rx antenna etc) are exchanged along with Co-RTWT Scheme Information set exchanges during the Co-RTWT negotiation phase. Exact parameters required for Co-BF/Co-SR are TBD
The Co-RTWT negotiation request frame contains Co-RTWT Scheme Information set, Co-BF/Co-SR Scheme Information set required for the Co-RTWT negotiation
  The Co-RTWT requesting AP optionally includes the supported modes of protection mechanism for its requested RTWT schedule(s) in the Co-RTWT Negotiation Request frame
The Co-RTWT responding AP selects the suitable mode of RTWT protection (enable Co-BF/Co-SR) supported by it in the Co-RTWT Negotiation Response frame along with Co-BF/Co-SR Scheme Information set required for the Co-RTWT negotiation
The final Co-RTWT Negotiation confirmation and agreement formation takes place after both the APs successfully complete the Co-BF/Co-SR negotiation and agreement formation
After the Co-RTWT negotiation is completed, The Co-RTWT requesting and responding AP broadcasts the negotiated RTWT schedule(s) and its related parameters and the negotiated protection mechanism to its associated STAs as an intra-BSS announcement which marks the end of Co-RTWT Negotiation phase

## Slide 14: Straw Poll 1
Do you support to define a mechanism in IEEE 802.11bn to extend protection for Co-RTWT negotiation?
  Enable Co-BF agreement as part of extending protection to a requested RTWT schedule
  Enable Co-SR agreement as part of extending protection to a requested RTWT schedule