## Slide 1: UL Transmission in SMD BSS Transition
Date: 2025-9-4
Authors:

## Slide 2: Introduction
Uplink data continuity is essential for ensuring communication reliability, supporting diverse scenarios, and enabling a smooth user experience.
However, UL transmission during SMD BSS transition is not explicitly defined in the D1.0, so uplink data continuity may not be provided.
When one MAC SAP is used in the SMD, the non-AP MLD does not need to suspend and can send UL transmission to the current AP MLD after the ST execution request.
  This behavior is not explicitly specified but can be implemented.
When separate MAC SAP per AP MLD is used in the SMD, there are some proposals to prohibit UL transmission from the non-AP MLD after the ST execution request.
This contribution proposes procedures to allow UL transmission during SMD BSS transition when separate MAC SAP is used.

## Slide 3: Current status of D1.0 about SMD BSS transition
MAC SAP types, overall procedures and frames are defined. Also, DL transmission during SMD BSS transition is defined.
It is defined that UL transmission to the target AP MLD during SMD BSS transition is NOT allowed.
  “The non-AP MLD shall not transmit Class 3 frames to the target AP MLD until it has received the ST execution response with Status Code field set to SUCCESS from the current AP MLD for at least one link.”
It is NOT defined whether a non-AP MLD is allowed to send data to its current AP MLD after sending an ST execution request, especially when a separate MAC SAP per AP MLD is used. When one MAC SAP is used, this is implicitly allowed.

## Slide 4: Necessity of UL data continuity improvement
In various use cases, low latency UL transmission is required.
  XR (e.g. See-through) use cases: UL pose/control information needs to be delivered within a certain period because DL video traffic is generated based on the UL traffic.
  Haptics use cases: Real-time and bidirectional communication is required. In case of Industrial IoT, it could be mission critical use cases [1].
If non-AP MLD is buffering low latency traffic for such use cases, both DL and UL data continuity cannot be maintained if there is UL suspension during SMD BSS transition.
  The UL suspension between the ST execution request and the ST execution response can extend to tens of milliseconds. Depending on the network architecture, the DS mapping update may take time, and if the non-AP MLD requests the transfer of SN, the context must be transferred before the ST execution response.
Hence, we will address improvement of UL data continuity, minimizing the impact on the SMD BSS transition procedure.
 | Haptics (Automotive) | XR
Reliability | 99.999 (w/compr.) % | 99 %
Latency | 1-10 ms | 10 ms
Requirements[2-3]
ST
execution
request
UL1
UL2
ST
execution
response
Drop
UL suspension
Non-AP
MLD
Current AP MLD
Target AP MLD
Buffered traffic
Lifetime
Lifetime

## Slide 5: UL transmission during SMD BSS transition
UL data shall eventually be delivered to the target AP MLD and the target AP MLD shall pass it up to the DS for UL data continuity.
There are two methods for delivering UL data to the target AP MLD during SMD BSS transition.
  The non-AP MLD transmits UL data to the current AP MLD first, and the current AP MLD forwards the UL data to the target AP MLD.
    To avoid DS mapping switchback, the current AP MLD should not pass up data to the DS and should forward to the target AP MLD in principle.
  The non-AP MLD transmits UL data to the target AP MLD directly.
    This is not allowed in D1.0, but can be conditionally allowed.

## Slide 6: Concerns in UL transmission to the current AP MLD and UL data forwarding
There is no guarantee that the current AP MLD can forward all UL data to the target AP MLD.
  The amount of data that can be forwarded from the current AP MLD to the target AP MLD depends on backhaul link conditions.
The ST execution request may be rejected by the target AP MLD.

## Slide 7: Proposed procedure of UL transmission to the current AP MLD
  The current AP MLD shall indicate its capability of UL data forwarding to the non-AP MLD.
  The current AP MLD shall limit UL transmission based on its condition (e.g., backhaul condition) to ensure UL data forwarding. This limitation could be as follows.
  Limitation by time (UL Draining Period)
  Limitation by SN (Last SN that can be transmitted)
  Limitation by flow (ACs/TIDs/etc.)
If the current AP MLD limits UL transmission by time, the current AP MLD shall indicate UL Draining Period duration to the non-AP MLD. UL Draining Period starts after the reception of the acknowledgement of the ST execution request and the non-AP MLD can send UL data to the current AP MLD until the UL Draining Period expires.
  If the non-AP MLD receives ST execution response before the UL Draining Period expires, it should stop sending UL data.
The current AP MLD forwards all UL data received within UL Draining Period to the target AP MLD.
If the target AP MLD rejects ST execution request, the current AP MLD should pass up UL data to the DS.
Current
AP MLD
Target
AP MLD
STA
ST execution request
ST execution response
acknowledgement
UL
UL data forwarding
acknowledgement
UL
Draining
Period
ST preparation request
acknowledgement
ST preparation response
acknowledgement

## Slide 8: Concerns in UL transmission to the target AP MLD
Sending the data directly to a better channel condition of the target AP MLD is better than sending the data frame first to the current AP MLD through a worse channel condition.
However, there are some concerns in UL transmission to the target AP MLD.
  Current spec prohibits the non-AP MLD from transmitting Class 3 frames to the target AP MLD until it has received the ST execution response with Status Code field set to SUCCESS for at least one link due to following reason.
    The target AP MLD may not be ready to receive uplinks because the target AP MLD will need to be notified by the current AP MLD that the non-AP MLD wants to execute roaming. If the target AP MLD is not ready (so not expecting the non-AP MLD), the UL frames from the non-AP MLD will be dropped.
  If the target AP MLD rejects the ST execution request, UL data may be dropped at the target AP MLD.
  If the Per-AP MLD PTK mode is used, the non-AP MLD has not installed the Per-AP MLD PTK as its PTK.

## Slide 9: Proposed procedure of UL transmission to the target AP MLD
The non-AP MLD notifies the target AP MLD that the non-AP MLD wants to execute roaming by the ST execution request.
Considering the contexts from the current AP MLD,
  if the non-AP MLD has requested not to transfer UL SN to the target AP MLD, the non-AP MLD will reset SN to 0 and transmit Data frames to the target AP MLD. In this case, the target AP MLD does not need to wait for UL SN from the current AP MLD.
  if the non-AP MLD has requested to transfer UL SN to the target AP MLD, the target AP MLD shall wait for the contexts from the current AP MLD. In this case, the non-AP MLD shall indicate the target AP MLD not to discard UL data from the non-AP MLD before the target AP MLD receives contexts from the current AP MLD (UL Buffer Request).
    This indication can be included in the ST execution request.
If the non-AP MLD receives ST execution response with the Status Code field set to REJECTED_ST_EXEC, the non-AP MLD should resend UL data to the current AP MLD.
  If SMD has UL data forwarding capability, the target AP MLD may forward UL to the current AP MLD.
The non-AP MLD should transmit Data frames to the target AP MLD only when the Per-SMD PTK mode is used.

## Slide 10: Conclusion
UL transmission during SMD BSS transition is not defined in D1.0.
UL data forwarding is beneficial in various scenarios.
We propose a UL data transmission procedure for SMD BSS transition.
  The non-AP MLD can transmit UL to the current AP MLD.
    If the non-AP MLD sends an ST execution request to the current AP MLD.
    If the SMD supports UL data forwarding.
    If the current AP MLD indicates information about UL transmission.
  The non-AP MLD can transmit UL to the target AP MLD.
    If the per-SMD PTK mode is used.
    If the non-AP MLD sends an ST execution request to the target AP MLD.
    If the non-A MLD requests the target AP MLD to receive UL data.

## Slide 11: References
[1] 24/1493r1, “Use Cases for Wi-Fi Business Solutions in UHR,” Akira Kishida (NTT)
[2] O. Holland et al., “The IEEE 1918.1 “Tactile Internet” Standards Working Group and its Standards,” in Proceedings of the IEEE, vol. 107, no. 2, pp. 256-279, Feb. 2019.
[3] “Study on XR (Extended Reality) evaluations for NR,” 3GPP TR 38.838 v 17.0.0, Dec. 2021.

## Slide 12: SP1
Do you agree that the current AP MLD may forward received UL data to the target AP MLD?
  SMD Information element shall provide the capability that the forwarding of UL data from the current AP MLD to the target AP MLD is supported or not.
  The current AP MLD shall provide information about limitations on UL transmission to the non-AP MLD.
    This information is included in ST preparation response.
    One of this information is UL Draining Period duration. Other information is TBD.
    How to decide UL Draining Period duration depends on implementation.
    UL Draining Period starts after the reception of the acknowledgement of the ST execution request.
    The non-AP MLD shall not transmit UL data to the current AP MLD after the UL draining period expires.
  If the target AP MLD rejects the ST execution request, the current AP MLD should pass up UL data to the DS.

## Slide 13: SP2
Do you agree that a non-AP MLD may transmit Data frames to the target AP MLD before it receives ST execution response under following conditions?
  The Per-SMD PTK mode is used.
  If the non-AP MLD sends an ST execution request to the target AP MLD and the ST execution request has a request indication for the target AP MLD to receive Data frames before ST execution response.
    The target AP MLD may indicate its capability to buffer Data frames from the non-AP MLD prior to the ST execution request.
  If the non-AP MLD receives ST execution response with the Status Code field set to REJECTED_ST_EXEC, the non-AP MLD should resend UL data to the current AP MLD.
    If SMD has UL data forwarding capability, the target AP MLD may forward UL data to the current AP MLD.

## Slide 14: Appendix
 | B0 | B1 B3 | B4 | B5 | B6 B7
 | DL Data Forwarding | Max Number Of Prepared Target AP MLDs | SMD Type | UL Data Forwarding | Reserved
Bits: | 1 | 3 | 1 |  | 3
SMD Capabilities field format |  |  |  |  | 

## Slide 15: Appendix
 | Status Code | Reserved | Presence Bitmap | AID | DL BA Info | UL BA Info | SCS List | UL Draining Period Duration
Octets: | 2 | 1 | 1 | 0 or 2 | variable | variable | variable | 0 or 2
Figure 9-K7— ST Info field format in an ST preparation response
 | B0 | B1 | B2 | B3 | B4 | B5 B7
 | AID Present | DL BA Info Present | UL BA Info Present | SCS List Present | UL Draining Period Duration Present | Reserved
Bits: | 1 | 1 | 1 | 1 | 1 | 3
Figure 9-K9— Presence Bitmap field format in an ST preparation response

## Slide 16: Appendix
 | Reserved | Presence Bitmap | DL TID Bitmap | UL Buffer Request
Octets: | 1 | 1 | 1 | 1
Figure 9-K12— ST Info field format in an ST execution request
 | B0 | B1 | B2 B7
 | DL TID Bitmap Present | UL Buffer Request Present | Reserved
Bits: | 1 | 1 | 7
Figure 9-K14— Presence Bitmap field of the ST Info field format in an ST execution request
Reserved bit could be used to indicate UL buffer request from the non-AP MLD to the target AP MLD.

## Slide 17: Appendix
UL data transmission related comments from CC50.
  During the seamless roaming procedure, when the current AP has a large amount of uplink data buffered, how to switch the DS path to the target AP as quickly as possible should be considered.
  UL Data forwarding or retransmission should be considered in case there are UL MPDUs not acked during the roaming preparation procedure.
  During the roaming procedure, when a non-AP MLD has a large amount of data buffered on the link associated with the current AP, to avoid retransmissions after receiving the roaming response, the non-AP MLD should be allowed to transmit data to the current AP.