## Slide 1: Considerations on Direct Roaming through Target AP MLD
Date: 2025-9-11
Authors:

## Slide 2: Abstract
In this contribution, we discuss the direct roaming procedure through the target AP MLD (Sequence 3) based on [1].

## Slide 3: Background
According to [1], it is proposed that the non-AP MLD performs SMD BSS transition directly the through target AP MLD without any preparation with the current AP MLD (this is called Sequence 3 in [1]).
Sequence 1
Sequence 2
Sequence 3
STA
Current AP
Target AP
SMD
STA
Current AP
Target AP
SMD
STA
Current AP
Target AP
SMD
ST preparation
ST preparation
ST execution
ST execution
ST execution
BTM request
Roaming preparation
Roaming execution
Roaming preparation
Roaming execution
Pre-roaming preparation
Roaming execution

## Slide 4: Benefits of Sequence 3
  There are many use cases which the non-AP MLD needs to perform roaming directly to the target AP MLD due to sudden RSSI drop [1].
    In these cases, the non-AP MLD cannot predict when it should roam to the target AP MLD, so the non-AP MLD may not be able to perform any preparation with the current AP MLD when it decides to roam.
  In such use cases, Sequence 3 enables the non-AP MLD to continue connectivity, so the performance of SMD BSS transition improves in UHR network.

## Slide 5: Sequence 3 for Factory
Sequence 3 has an important role for AGV to perform SMD BSS transition in some situations.
  In general, AGVs are moving around the factory in which there are a lot of objects. These AGVs often move to the place which is blind to their current AP and do not back to the AP’s sight immediately.
  AGVs carrying containers often stop to unload and/or pick up some container. Then, the AGVs become an obstacle for other STA connected with an AP if the AGVs stop between the STA and the AP.

## Slide 6: Sequence 3 for Warehouse
Replacing cargoes in the warehouse is also significant use case for Sequence 3.
  Many cargoes are often replaced in the warehouse. There is no problem when there is no cargo between an STA and its current AP, but a cargo become an obstacle if it is placed between the STA and the AP. The STA cannot predict when this cargo is placed there.
  This situation also happen when the layout of the warehouse changes.

## Slide 7: Proposal: Sequence 3 should be supported
Sequence 3 should be supported to enable the non-AP MLD to perform SMD BSS transition in some use cases.
  Also, there are some features on Sequence 3 we should discuss
    Pre-roaming preparation
      e.g. Who initiates pre-roaming preparation procedure?
    Timeout
      e.g. Do we need a timeout between pre-roaming preparation and roaming execution?
    Random MAC address for Roaming
    DL/UL data transmission
      e.g. Whether DL/UL data transmission gaps are necessary for Sequence 3?

## Slide 8: References
[1] 25/0408, Roaming Through Target AP - Follow Up, Binita Gupta