## Slide 1: Non-AMP portion of AMP PHY preamble follow-up
Date: 2025-09-15
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek |  |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Thomas Pare |  |  |  | 
Alice Chen | Qualcomm Technologies Inc. |  |  | alicel@qti.qualcomm.com

## Slide 2: Recap: passed motion
[Motion #28, [1]]
  The preamble of an AMP DL PPDU includes L-STF, L-LTF, L-SIG, RL-SIG, and U-SIGs for AMP enabled non-AP STA and active TX non-AP AMP STA in 2.4 GHz.
[Motion #86, [1]]
  The RATE field in L-SIG of an AMP DL PPDU in 2.4 GHz shall be set to the value representing 6 Mb/s in the 20 MHz channel spacing.
  The LENGTH field in L-SIG of an AMP DL PPDU in 2.4 GHz is set to a value satisfying the condition that the remainder is zero when LENGTH is divided by 3.
[Motion #87, [1]]
  An DL AMP PPDU in 2.4 GHz is identified in its U-SIG with the following setting:
  PHY version value sets to 0
  One or multiple Validate bit subfields sets to 0 or subfield(s) set to a validate state.

## Slide 3: AMP PPDU indication for third-party STAs
We propose that a DL AMP PPDU in 2.4 GHz is identified in its U-SIG with the following setting:
  PHY version value sets to 0
  PPDU Type And Compression Mode value sets to 3.
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
U-SIG1 | PHY version |  |  | Bandwidth |  |  | UL/DL | BSS color |  |  |  |  |  | TXOP |  |  |  |  |  |  | Disregard |  |  |  |  | Validate
U-SIG2 | PPDU Type |  | Validate | punctured channel info |  |  |  |  | Validate | EHT-SIG MCS |  | Number Of EHT-SIG Symbols |  |  |  |  | CRC |  |  |  | Tail |  |  |  |  | 
AMP DL PPDU:
U-SIG fields |  | Description | 
UL/DL | PPDU Type | EHT PPDU format | Note
0 (DL) | 0 | EHT MU | DL OFDMA (including non-MU-MIMO and MU-MIMO).
 | 1 | EHT MU | EHT SU transmission or EHT sounding NDP
 | 2 | EHT MU | DL non-OFDMA MU- MIMO.
 | 3 | AMP | AMP DL PPDU

## Slide 4: Straw Poll #1
Do you agree to update the following text in the SFD:
  An DL AMP PPDU in 2.4 GHz is identified in its U-SIG with the following setting:
    PHY version value set to 0
    One or multiple Validate bit subfields sets to 0 or subfield(s) set to a validate state.
    PPDU Type And Compression Mode value sets to 3.