## Slide 1: Minimalist Beacon for NSA mmWave
Date: 2025-08-27
Authors:

## Slide 2: Abstract
Since the beginning of time, beacon has been a staple of any 802.11 BSS
NSA mmWave design discussions in TGbq have revisited many 802.11 design fundamentals
  Beacon design has been identified in contributions and floor comments as an area needing extensive optimization
  Our previous contribution [1] provides design principles for optimizing mmWave beacon
In this presentation, we –
  Elaborate on beacon design principles for NSA mmWave link
  Present device’s point of view on the beacon design problem

## Slide 3: Role of an 802.11 Beacon
Beacons are essential in maintaining and managing connectivity between AP and STAs:
  Network discovery
    Enables STAs to discover Wi-Fi networks
    Estimate channel condition
    Determine a suitable network to connect to
  Convey operation parameters
    E.g., synchronization, operations elements
  Capabilities advertisement
    E.g., capabilities elements
  Roaming trigger conditions
    Device side implementations often use missed beacon count to trigger a roam point
  Power management support
    Periodic beaconing enable devices to wake up at pre-known times from a power save mode to check for network updates
  Indoor positioning and navigation
    Beaconing enables device side solutions related to indoor positioning and navigation, enable location based notification services, asset tracking, etc.
  …

## Slide 4: Beaconing in 11ad/ay
802.11ad and ay introduced a new beaconing design to meet the needs of mmWave access network
A beacon interval (BI) in 11ad/ay contains –
  Beacon header interval (BHI):
    Beacon transmission interval (BTI): includes a sweep of DMG beacons on different sectors to cover all possible directions
    Association beamforming training (A-BFT): used by STAs to train their antenna sector for communication with the AP
    Announcement Transmission Interval (ATI): management information exchanges between AP and associated beam-trained STAs.
  Data transmission interval (DTI)
BTI
A-BFT
ATI
BHI
DTI
…
A-BFT slot
A-BFT slot
…
Beacon sweeping
Beacon Interval (BI)
Fig. 2 DMG Beacon frame format
Fig. 1 Beacon interval structure. Note: figure is not to scale

## Slide 5: Multi-link Operation Beaconing
MLO introduced in 802.11be provides a set of procedures for communication between MLDs over one or more links.
Beacon frame is transmitted on each link.
Beacon frame carries information useful for non-AP MLD for MLO discovery, configuration updates such as AP removal, etc.
Depending on the scenario, beacon frame body can contain a number of elements to achieve this objective.
NON-AP STA3
NON-AP STA2
NON-AP STA1
AP 1
AP 2
AP 3
Non-AP MLD
AP MLD
2.4GHz
5 GHz
6 GHz
2.4GHz
5 GHz
6 GHz
Beacon frame
Beacon frame
Beacon frame
Fig. 1 Frame exchange for MLO discovery based on beacon transmission
Fig. 2 Contents of a Beacon frame transmitted by an AP corresponding to the transmitted BSSID during MLO discovery

## Slide 6: Rethinking Beacon Design for NSA mmWave Operation
NSA Operation must be leveraged to optimize beacon design and procedure:
  Overhead: 11bq will also need to sweep beacons in different directions. Sweeping a traditional 11be beacon (with ML info) will result in forbiddingly high overhead.
  Power consumption and channel utilization: A longer beacon also means a longer total sweep duration. This can require battery powered devices to stay awake for a longer total sweep duration (worse case).
  Frame errors: Shorter frame reduces chances of frame errors and enables edge devices to receive beacons efficiently.
  …
 What is a beacon for a NSA link?

## Slide 7: Minimalist Art
Strip away all non-essential elements to focus on the artwork’s fundamental components such as its form, material and presence in real space.
  Art work conveys the bare minimum to convey the idea.
  Remaining information:
    Subconscious mind fills the remaining details.

## Slide 8: Minimalist Beacon (1/2)
Strip away all the non-essential aspects to focus on the fundamental components needed to operate the NSA mmWave link
  NSA beacon conveys the bare minimum information needed to operate the mmWave link
  Remaining information:
    Sub-7 link frame exchanges
    mmWave link (on demand)

## Slide 9: Minimalist Beacon (2/2)
Minimalist content: Beacon content for NSA mmWave link must convey minimum needed information for mmWave link operation
  Offload non-essential items to sub-7 GHz links. Either in beacons or other frames exchanged on sub-7.
    Needs further consideration as those links are already overloaded. Do we further increase the load on all of them?
    See [1] for more details.
  Provide non-essential items on mmWave link on-demand.
  Beacon will act as a backbone of beam management.
    Beacon will provide some mmWave specific information for beam management
Minimalist procedure: Beaconing procedure can also retains only essential aspects
  Beacon can be periodically broadcasted as in legacy systems
  Additionally, a mode to sweep a beacon on-demand should also be allowed. More details will be shared in a follow-up contribution

## Slide 10: Minimalist Beacon Contents: AP Identifier
1. AP identifier: Entire BSSID (48 bits) OR preferably a few bits long time varying cookie
  Enable reachability assessment:
    STAs that have setup a link detect if link is lost using missed beacon count.
    A STA that has not setup a link with mmWave AP needs to know if it is within the range and how good the link will be.
    Solely depending on procedures such as probe request/response for this purpose will introduce inefficiencies in operation. E.g., individual sweeps increasing airtime consumption.
  Enable other device side solutions that use AP identifiers:
    Those related to indoor positioning and navigation, location based notification services, asset tracking, etc.

## Slide 11: Minimalist Beacon Contents: Transmit Beam Index
2. Transmit beam index: 6 – 10 bits for beam index
  Beacon will act as a backbone of beam management
    Successfully decoding a beacon should provide a STA information on receive beam and AP's transmit beam index.
    Additionally AP can also acquire TX/RX beam to communicate with a given STA, basic link quality. This could be done through sub-7 polling/reporting.

## Slide 12: Minimalist Beacon Contents: TSF
3. TSF:
  For 11bq, MLO architecture must continue to allow mmWave link carrier generation and TSF to use a different oscillator than sub-7 GHz link:
    11ad/ay timer accuracy requirements were different compared to sub-7.
    11bq must not force a high speed internal connection between sub-7 and mmWave PHY to exchange TSF.
      Timestamp field carries TSF value at the time that the start of the data symbol containing the first bit of timestamp field appears at the transmitting antenna connector.
      Timestamp field is also carried in other frames besides beacon (although on demand).
  Beacon must continue to carry the TSF to enable the STA to periodically synchronize its internal clock with the AP.
    It may be possible to convey only partial TSF (a few LSBs) in mmWave

## Slide 13: Minimalist Beacon Design for NSA mmWave Operation
The minimum that a NSA mmWave beacon must contain:
 | Information | Comments
1. | BSSID | Entire BSSID (48 bits) OR preferably a few bits long time varying cookie
2. | Transmit beam index | 6 – 10 bits for beam index; implicitly or explicitly.
3. | Timestamp | TSF
4. | ?? | 
After a STA decodes a beacon:
  STA side acquires:
    Receive beam, AP’s transmit beam index, basic link quality for a given AP and TSF.
  AP side can acquire (possibly through sub-7 polling and reporting):
    AP’s TX/RX beam for a given STA, basic link quality.

## Slide 14: Conclusion
NSA mmWave link must continue to carry a beacon
Design principles that should be followed for NSA mmWave link beacon
  Minimalist beacon conveying only minimum information needed for mmWave link
  NSA Operation must be leveraged to optimize beacon design and procedure
Minimalist beacon content:
  BSSID
  Transmit beam index
  TSF
  TBD

## Slide 15: Straw Poll
Do you agree that NSA mmWave link beacon shall provide minimal information necessary for operation of mmWave link?
  Note: Minimal information includes at least BSSID, transmit beam index, TSF.

## Slide 16: References
[1] IEEE 802.11-25/632, “Anchor Link for ML Operation with mmWave Link”