## Slide 1: Discovery of Active Tx and Backscatter AMP STAs
Authors:
Date: 2025-08-22
Name | Affiliations | Address | Phone | email
Sanket Kalamkar | Qualcomm Technologies Inc. |  |  | sankal@qti.qualcomm.com
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 

## Slide 2: Introduction
Active Tx and backscatter AMP non-AP STAs may not have persistent memory
  These STAs may lose any data not hardcoded once power is lost
  Power loss is a risk for AMP STAs due to the unpredictable nature of energy harvesting
  Writing data to non-volatile memory requires additional energy consumption [1]
Persistent memory—adhere to baseline procedures
  Devices capable of retaining data through power cycles allow an AMP AP to assign temporary IDs during association [2], e.g., AID12
  Authentication keys can be maintained over multiple sessions
Non-persistent memory—use permanent IDs
  AMP AP assigning temporary IDs won’t work
  Instead, permanent IDs (hardcoded in the device) need to be used
    MAC addresses for Active Tx non-AP AMP STAs and EPCs for backscatter AMP STAs
This contribution focuses on AMP non-AP STAs lacking persistent memory
  How to discover these STAs, retrieve their permanent IDs, and facilitate frame exchanges

## Slide 3: E2E AMP Operation
Offline Onboarding
  Password configuration, which establishes the Pairwise Master Key (PMK) on both the AMP AP and AMP STA.
Initial Information Exchange (Discovery)
  Following offline onboarding, the AP and STAs exchange fundamental information for the first time.
    Examples include MAC addresses and basic device details.
    In some cases, this can occur offline.
      For instance, the AP may obtain the client's MAC address through a QR code located near the STA.
  This process enables the AP to detect the presence of active AMP STAs.
AMP Operation Mode Information Exchange
  The AP queries the STA for its operational capabilities and more comprehensive information.
  This exchange helps the AP determine the appropriate Tx/Rx parameters.
AMP Trigger/Uplink Response
  The AP initiates UL transmissions by triggering the client, which then responds by sending uplink data.

## Slide 4: AMP Discovery
The AMP AP and AMP STA share non-sensitive data.
  For example, MAC addresses or EPC to be used as permanent identifiers
No security is required
AMP Discovery frame can be broadcast
  Uplink responses can use random access methods
    For example, slotted ALOHA
AMP Discovery frame
UL Response (Permanent ID)
After on-boarding
AMP AP
AMP STA

## Slide 5: Short ID
AMP AP can assign a short ID (X bits) derived from the permanent ID to identify an AMP STA
  E.g., By default, use the X LSBs of the permanent ID
If a collision occurs of short IDs, the AP uses the X LSBs of a hash of the full permanent ID instead.
A one-bit flag to indicate whether the default short ID is in use.
The AP may also use a short ID for its own identification.

## Slide 6: An E2E View
The AP and STAs may use short IDs (if they need to be present) when they exchange frames
One-time authentication may use short IDs to derive the transient key for MIC and encryption.
Unprotected AMP Trigger frame (with ANonce)
[Encrypted response] + MIC + SNonce
AMP AP
AMP STA
Generate SNonce
Compute transient key for MIC/Encryption
Decryption + Integrity check
One-shot authentication
AMP AP and AMP STA know PMK used to generate a transient key through offline onboarding

## Slide 7: Additional Thoughts
In the absence of persistent memory, an AMP STA may fail to recall previously sharing its permanent ID with the AP
  The AMP STA might resend the ID if it does not remember having sent it before.
  This behavior offers an added benefit:
    When an AMP STA resends its ID, the AP can infer that the STA may have forgotten prior communication with the AP.
    Consequently, the AP can initiate measures to re-establish the setup, such as requesting the STA’s capabilities.
The configuration for Active Tx and backscatter non-AP STAs lacking persistent memory can also be applied to those with persistent memory.
  But recommend to use methods similar to baseline procedures for devices with persistent memory.

## Slide 8: Summary
For AMP STAs with persistent memory—methods similar to baseline procedures
  E.g., use AID12 as a STA identifier
For AMP STAs lacking persistent memory—use permanent IDs
  E.g., MAC address or EPC
Short IDs can be used by AMP AP and AMP STA
  Derived from permanent IDs

## Slide 9: SP1
Do you agree to add the following text to the 802.11bp SFD:
  802.11bp uses a discovery frame to discover Active Tx non-AP AMP STAs.

## Slide 10: SP2
Do you agree to add the following text to the 802.11bp SFD:
  When an Active Tx non-AP AMP STA responds to the discovery frame, the non-AP STA shall include its MAC address.

## Slide 11: SP3
Do you agree to add the following text to the 802.11bp SFD:
  For an Active Tx non-AP AMP STA without persistent memory, an AMP AP shall use an identifier derived from the MAC address of the non-AP AMP STA.
    The default option is to use the TBD LSBs of the MAC address of the non-AP STA.
    If a collision occurs in the TBD LSBs of the MAC address (default option), use the TBD LSBs of the hash computed over the MAC address of the non-AP STA.

## Slide 12: References
[1] Amichai Sanderovich et. al., “Considerations for AMP Devices”, IEEE 802.11-23/1140r0, July, 2023.
[2] Rojan Chitrakar et. al., “AMP Pairing and ID Assignment,” IEEE 802.11-25/1241r1, July 2025.