## Slide 1: Complete Profile for IMMW
Date: 2025-09-15
Authors:
Name | Affiliation | Address | Phone | Email
Insun Jang | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insun.jang@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Hongwon Lee |  |  |  | hongwon.lee@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St, San Diego CA 92131 , USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
Essentially in 11bq, we expect the information of IMMW STA can be obtained from reporting STA operating on a link in Sub-7GHz band using MLO defined in 11be
  The reported IMMW STA doesn’t need to generate and transmit the MGMT frames, e.g., (Re)Association/Probe Request/Response frames and other (E.g., Link Reconfiguration frames)
In this contribution, we discuss how to construct the complete profile for IMMW in Multi-link element
  in terms of STA Info and STA Profile fields

## Slide 3: STA Control/Info in Complete Profile
If we reuse current STA Info using subIE ID = 0,
  STA MAC address and TSF Offset are necessary
  Enhanced Critical Updates Information can be used for IMMW as a type
  The others are NOT necessary
  We have only 2 reserved bits which can be used for IMMW
    Maybe, if we move most of information to STA Profile, it could be enough
Alternative #1: Unnecessary information is replaced (still using subIE ID = 0) with IMMW info
  It assumes an awareness that it is the complete profile for the IMMW STA
Alternative #2: Define IMMW Per-STA Profile, e.g., using subIE ID = 1
  It is dedicated to IMMW STA
  Necessary fields for IMMW would be included
STA Control From 11be
Amendment from 11bn

## Slide 4: STA Profile in Complete Profile
We expect to have some IMMW-related IEs/fields, e.g.,
  IMMW Capabilities IE (e.g., BFT-related capabilities, Supported TX/RX Capa, …)
  IMMW Operation IE (e.g., Channel, BW, BSS color, …)
Simply, we can add the fields/elements to MGMT frame and then follows baseline

## Slide 5: STA Profile in Complete Profile (Cont’d)
However, if we see the following baseline
  “The complete profile of a reported STA in a Basic Multi-Link element consists of all the elements and fields that would be included in a Management frame that is of the same subtype as the frame transmitted by the reporting STA carrying the Basic Multi-Link element as if the reported STA were to transmit the frame and subject to inheritance rules”
  Such MGMT frames including IMMW-related information wouldn’t be transmitted on IMMW link, which means
Therefore, as another way, we can add IMMW-related fields/elements to STA Profile field NOT MGMT frame body
  The main reason is the fields/elements itself are never be carried in MGMT frame body (e.g., Probe Response/Association Request/Response)

## Slide 6: Conclusion
We discussed how to construct the complete profile of STA operating on IMMW link(s)
In Complete Profile of IMMW STA,
  Current STA Control/Info can be reused, but as alternatives, we replace some unnecessary fields with IMMW-related fields or define IMMW Per-STA Profile
  STA Profile can be constructed by adding IMMW-related fields/elements without including them in the corresponding MGMT frame
    Even though MGMT frame includes those information, it never be transmitted with the information

## Slide 7: Straw Poll 1
Do you support the following text in TGbq?
  When the complete profile of IMMW STA is provided, IMMW-related field(s) and/or element(s), which includes in a STA Profile field in a Multi-Link element, are not included in a Management frame
    The Management frame is an Association Request/Response frame, or Probe Request/Response frame

## Slide 8: References
[1] 24/459, Multi-link Operation for IMMW
[2] 25/431, MLO-based Scheduling for IMMW
[3] 11-25/433, Channel Access for IMMW
[4] 11-25/841, Some considerations for MLO-based BFT Announcement
[5] 24/1312, Draft P802.11bq PAR
[6] 11-23/1905, High Level Thoughts on IMMW
[7] 11-23/1819, Integrated mmWave Design Considerations
[8] 11-23/1968, Discussion on general direction of integrated mmWave
[9] 11-25/1563, Discussion on Time Synchronization for IMMW