## Slide 1: PHY Design for AMP in S1G
Date: 2025-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Ke Wang |  |  |  | 
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 2: Abstract
In this contribution, we discuss the PHY design for AMP in S1G covering issues including coverage, channelization, frequency hopping and PPDU design.
Doc.: IEEE 802.11-25/1565r0

## Slide 3
Impacts of Coverage Enhancement in S1G
  The coverage for mono-static backscattering AMP devices is expanded from few tens of centimetres in 2.4 GHz to a few meters in S1G.
    AMP AP can trigger long distance AMP non-AP STAs, thus a moving reader, e.g., a cell phone, can trigger an area with tens of m2.
    Interference:
      Interference between readers;
      Interference between AMP non-AP STAs;
      Interference to other legacy systems.
    One to many communication
      TDM: multiple AMP non-AP STAs in one PPDU with multiple excitation within one PPDU
      FDM: different frequency shift for each AMP device.
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 4
Channelization
  Agreement: 11bp shall adopt the following channelization scheme for China:
    Operating bands: 920-925MHz
    Bandwidth 250kHz
    There are 20 channels, with center frequency (MHz): (920.125+N*0.25) MHz, N=0,…,19
  Regulations in USA and EU
    US
      The frequency regulation in FCC 15.247 covers frequency bands 902-928MHz.
      There’s no fixed channel bandwidth cap
    EU:
      ETSI Harmonised Standards cover the 863 to 870 MHz and 915 to 921 MHz band.
      Channel bandwidth: 200kHz, 250kHz, 400kHz, 800kHz and 1MHz depending on different system configurations
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 5
Channelization
  Uniform channel bandwidth: 250kHz for all regions/countries
    Pros:
      Unified PPDU design and data rate.
      Good interoperability across countries and areas
    Cons:
      250kHz may not applicable to many EU countries;
      Inefficient frequency band utilization, low data rate;
      Coexistence issue, especially in the US where legacy 802.11ah has been deployed.
  Dynamic bandwidth in different regions/countries: USA 1MHz, EU 200kHz, China 250kHz
    Pros:
      Maximize the frequency band utilization;
      High data rate in some countries;
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 6
Channelization
  Dynamic bandwidth in different regions/countries: USA 1MHz, EU 200kHz, China 250kHz
    Cons:
      Different PPDU design due to different bandwidth;
      Interoperability issue.
  WUR like design: 1MHz for optional legacy preamble and 200kHz/250kHz for AMP part
    Pros:
      Support coexistence with legacy systems;
      Similar bandwidth for 200kHz and 250kHz  same PPDU design for AMP part;
      Optional legacy preamble can be transmitted when necessary to support coexistence.
    Cons
      1MHz legacy preamble is not supported in some regions/countries.
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 7
Frequency Hopping
  USA
    Requirements
      frequency hopping is needed for less than 500kHz.
    Frequency hopping is at least needed for uniform channel bandwidth, i.e., 250kHz for all regions/countries.
  EU
    Requirements
      The maximum transmission time is 4s, followed by a break of at least 100ms;
      Duty cycle of 10% for AP and 2.5% otherwise
    Frequency hopping is not needed.
    Impacts of duty cycle restriction needs to be further investigated.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 8
Frequency Hopping
  China
    Requirements
      The maximum transmission time is 2s.
    Frequency hopping is not needed since the Tx time should be less than 2s.
  Frequency hopping requirements for different channelization
    Uniform channel bandwidth  needed in some countries;
    Dynamic bandwidth in different regions/countries  not needed;
    WUR like design  not needed.
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 9
PPDU Design
  PPDU format
    Agreed to reuse 2.4GHz PPDU format
  Optional Non-AMP preamble
    Considering coexistence with existing S1G system, e.g., 802.11ah, legacy preamble is needed
      AMP part can be with narrower BW
      Legacy preamble can be used for coexistence when 802.11ah is deployed
      Legacy preamble can be removed when 802.11ah is not deployed
      Such PPDU format can work across different regions/countries.
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 10
Coexistence
  Different level of coexistence
    Coexistence between WPT and other S1G systems
      Coexistence is crucial since WPT signal is usually with high Tx power
    Coexistence between WPT and legacy 802.11 devices, i.e., 802.11ah
      Can be addressed by adding optional legacy preamble as aforementioned.
    With S1G AMP communication, coexistence should be further considered between AMP communication and WPT
      Communication signal cannot overlap
      WPT can overlap with another WPT but not communication signal
      Some solutions have been proposed in companion contribution
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 11
Summary
  The following issues are discussed and analysed in this contribution
    Coverage enhancement;
    Channelization;
    Frequency hopping;
    PPDU design;
    Coexistence
Doc.: IEEE 802.11-25/1565r0
September 2025

## Slide 12: SP 1
Doc.: IEEE 802.11-25/1565r0
September 2025
  IEEE 802.11bp will specify, in S1GHz, an AMP Downlink PPDU which can contain an optional 802.11 preamble field.
  • The details of the 802.11 preamble field are TBD.

## Slide 13: SP 2
Doc.: IEEE 802.11-25/1565r0
September 2025
  IEEE 802.11bp will specify at least one or more of the following channel bandwidth for the AMP part in EU and US.
  200kHz
  250kHz
  Note: further down selection is TBD.