## Slide 1: On-Demand Beaconing for NSA mmWave Operation
Date: 2025-08-27
Authors:

## Slide 2: Abstract
In this presentation, we present our views on on-demand beaconing

## Slide 3: Traditional Beaconing
Traditional beaconing adopts a persistent approach:
  APs send out beacons at a set interval (typically 102.4 ms)
  Beacons are transmitted regardless of how many devices are connected to the AP
Persistent beaconing has many benefits even with no devices connected to the AP:
  Enables unassociated devices to discover the AP. In general, used by devices for RRM of both infra and P2P/Wi-Fi Aware
  Enables applications such as indoor positioning, navigation, etc.
  …
While persistent beaconing has its merits, it has its downsides especially when no active users are present in the network range:
  Power consumption (against green network principles), in particular for Mobile AP
  RF pollution/interference
  …

## Slide 4: Optimizing Beaconing Procedure Using NSA Operation
TGbq intends to design mmWave link as a non-standalone (NSA) link.
While persistent beaconing can continue to be the default beaconing mode, NSA link in an MLD offers a new semi-persistent beaconing mode that can leverage sub-7 support:
  In NSA mode of operation, a device is expected to first detect a sub-7 link or have at least one active before adding the mmWave link
  Discovery of NSA link can be achieved via sub-7 links
  Coverage area of sub-7 link can be expected to be larger compared to a collocated mmWave link.

## Slide 5: On-Demand Beaconing
We propose to define a ‘semi-persistent’ beaconing mode leveraging NSA operation:
  When no STA has added the mmWave link, AP may stop sending beacons on the mmWave link
  Existence of the mmWave link can still be discovered via a sub-7 link
  AP can start beaconing when needed. E.g., when a non-AP MLD requests to add the mmWave link to its setup link

## Slide 6: General On-Demand Beaconing
For an NSA link, on-demand beaconing can be realized in two ways with varying degrees of complexity:
  Semi-persistent beaconing: periodic beaconing can be enabled/disabled as needed
  Non-AP STA specific on-demand beaconing: beaconing can be performed using non-AP STA specific signaling
In this contribution, we proposed a semi-persistent mode of beaconing.
Non-AP STA specific on-demand beaconing is an advanced solution and needs more discussion.

## Slide 7: Conclusion
In this presentation, we introduce a simple semi-persistent on-demand beaconing mode for mmWave link operation
  Allows an AP to stop beaconing when no non-AP MLD has added the mmWave link to its setup links.
  AP can start to beacon when at least one non-AP MLD has added the mmWave link to its setup links.

## Slide 8: Straw Poll
Do you agree that TGbq should define a semi-persistent mode of beaconing?
  Semi-persistent mode is where the beaconing on an NSA link can be temporarily disabled