## Slide 1: Follow-up on sync field for AMP PPDU
Date: 2025-09-12
Authors:
Name | Affiliation | Address | Phone | Email
Ke Wang | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Yinan Qi |  |  |  | 
Doc.: IEEE 802.11-25/1580r1
September 2025

## Slide 2: DL SYNC field for non-Backscatter AMP (1)
  Analysis of DL sync sequence
Doc.: IEEE 802.11-25/1580r1
Source | Candidate Sequence | Auto-correlation | One-shot False-Alarm Rate for Differential decoder due to noise
Source [1] | 01011010010111000110001011101100 | AC=16/3+16/3 | 2*3.9221e-5
Source [2] | 10100101110011001010010111001100 | AC=8/2 | 2*1.8641e-5
Source [3] | 00101011011100011010011011101000 | AC=16/3+16/3 | 2*5.0982e-05
Our new sequence 1 | 00110011100010111010001011010110 | AC=16/2+16/3 | 2*3.7281e-5
Our new sequence 2 | 01011010010111010001100011100110 | AC=16/3+16/3 | 2*2.9416e-5

## Slide 3: Auto-correlation analysis for correlation receiver
Doc.: IEEE 802.11-25/1580r1
  Main peak is 16.
  Max side lode peak is 3.
  Min side lode peak is -3.
  Main peak is -16.
  Max side lode peak before main peak is 2.
  Min side lode peak before main peak is -2.

## Slide 4: Auto-correlation analysis for differential decoder
Doc.: IEEE 802.11-25/1580r1
  Main peak is 19.
  Max side lode peak is one chip before main peak.
  All other side lode peaks are lower than 3.
  Main peak is -18.
  Max side lode peak is one chip before main peak.
  All other side lode peaks are lower than 3.

## Slide 5: Special Segment
  For correlation receiver, threshold based OOK symbol detection can be used to decode the special segment. However, threshold based OOK symbol detection can NOT be used by differential decoder since it is not able to sample and buffer DL sync signal.
  All “ones” and all “zeros” sequence can be used to differentiated with the Manchester codes data, but they can’t be used as the special segment for a differential decoder, since the output will be “X”s [6], which are uncertain values.
  In order to facilitate the differential decoder, the special segment needs to be Manchester coded, e.g., 101010…
Doc.: IEEE 802.11-25/1580r1
Figure 5: Differential decoder receiver [4]

## Slide 6: False Alarm
  For differential decoder, false alarm can take place in both data part and in white noise case
    There is probability that random noise or data can be decoded into same or similar output sequence as the output sequence of sync sequence
  For both correlation decoder and differential decoder, the longer the sequence, the lower the false alarm rate.
    the length of the segment can be determined based on the original FAR(False alarm rate) P_FAR original and the target FAR (e.g. lower than 1%)
Doc.: IEEE 802.11-25/1580r1
  For correlation receiver, false alarm is mainly triggered in the data part[5] in higher SNR, as shown in the right Figure[5]
    This is because sync sequence has very good auto-correlation
    In lower noise, false alarm is mainly triggered by noise

## Slide 7: FAR due to noise for differential decoder
  With differential decoder, for a specific sync sequence S, its output can be represent as:
  ;
    Wherein are the segments that doesn’t contain X. And , are the segments that contains X
  For example:
  Assuming =[01011010010111010001100011100110]
  Then [101X010X101XX010XX1X0XX1XX0X1X0];
  For ; ; ; ; ; ; ; ;
  ; ; ; ; ; ; ; ; ; ;
  If represent the probability of that white Nosie is decoded as segment , can be used to represent the probability that white Nosie is decoded as .
  Since both S and S_bar needs to be considered.
  Using simulation, we find that
Doc.: IEEE 802.11-25/1580r1
M | M1 | M2 | M3 | M4 | M5 | M6 | M7 | M8
P | 0.5 | 0.33 | 0.2083 | 0.132 | 0.0846 | 0.0543 | 0.034 | 0.0222
  = 2.9416;

## Slide 8: Simulation
  Simulation 1: False alarm handling in data portion for correlation receiver
    Case 3-1: 250kbps
    Case 3-2: 1Mbps
    This is to evaluate the needed length of special segment
  Simulation 2: Synchronization performance for correlation receiver
    Case 1-1: without special segment
    Case 1-2: segment detection using differential decoder
    Case 1-3 : segment detection based on threshold detection
    This is to evaluate the sync performance of the proposed sync sequences and the impact from the special segment
  Simulation 3: Synchronization performance for differential decoder
    Case 2-1: without special segment
    Case 2-2 :segment detection using differential decoder
    Case 2-3 : segment detection based on threshold detection
    This is to evaluate the sync performance of the proposed sync sequences and the impact from the special segment
  Simulation 4: False alarm handling in case of Noise
Doc.: IEEE 802.11-25/1580r1

## Slide 9: Simulation assumptions
  Signal model: 5ms noise + legacy preamble + Sync field (sync sequence + special segment) + data
    Length of data is 100bits
  Channel: AWGN
  Clock set：0ppm
  Sync sequence length: 32
  Receiver type: correlation detector /differential decoder
  correlation decoder threshold: 0.04
  differential decoder threshold: 18
  Segment:
    12bits: 101010101010 (2us)
    8bits:10101010(1us)
    8bits:10101010(2us, in Appendix)
    6bits:101010(1us, in Appendix)
  Segment decoding method:
    1) based on detection threshold
    2) base on differential decoding
Doc.: IEEE 802.11-25/1580r1

## Slide 10: False alarm handing in data portion(1)
Doc.: IEEE 802.11-25/1580r1
Observation: In case of 250kbps and without special segment, FAR is quite high (>50%) for sync detection in data portion. FAR can be reduced to less than 1% with 12 bits special segment (chip duration of 2us).

## Slide 11: False alarm handing in data portion(2)
Doc.: IEEE 802.11-25/1580r1
Observation: In case of 1Mbps, FAR can be reduced to much lower than less than 1% with 12 bits special segment. This is because that the chip duration of the special segment (2us) is different with that of data portion(0.5us).

## Slide 12: False alarm handing in data portion(3)
Doc.: IEEE 802.11-25/1580r1
Observation: For data rate of 250kbps, if the chip duration of the special segment is changed from 2us to 1us, FAR can be reduced to much lower than 1% with 8 bits special segment(10101010).

## Slide 13: False alarm handing in data portion(4)
Doc.: IEEE 802.11-25/1580r1
Observation: For data rate of 1Mbps, if the chip duration of the special segment is changed from 2us to 1us, FAR can be reduced to lower than 1% with 8 bits special segment(10101010).

## Slide 14: Synchronization performance for correlation receiver(1)
Doc.: IEEE 802.11-25/1580r1
Observation: There is about 3.5dB loss for segment decoding based on threshold detection while 1.6dB loss for segment decoding using differential receiver.
  Note: Sync failure is defined as cases when the sync error is great than ¼ chip.
  Note: the segment is 12bit 101010101010 and chip duration is 2us.

## Slide 15: Synchronization performance for correlation receiver(2)
Doc.: IEEE 802.11-25/1580r1
Observation: There is about 5dB loss for segment decoding based on threshold detection while 3dB loss for segment decoding using differential receiver.
  Note: Sync failure is defined as cases when the sync error is great than ¼ chip.
  Note: the segment is 8bit 10101010 and chip duration is 1us.

## Slide 16: Synchronization performance for differential decoder(1)
Doc.: IEEE 802.11-25/1580r1
Observation: Without special segment, there is a high sync failure floor for differential decoder. The Sync failure can be reduced to less than 1% with the special segment.
  Note: Sync failure is defined as cases when the sync error is great than ¼ chip.
  Note: the segment is 12bit 101010101010 and chip duration is 2us.

## Slide 17: Synchronization performance for differential decoder(2)
Doc.: IEEE 802.11-25/1580r1
Observation: Without special segment, there is a high sync error floor for differential decoder. The Sync failure can be reduced to less than 1% with the special segment.
  Note: Sync failure is defined as cases when the sync error is great than ¼ chip.
  Note: the segment is 8bit 10101010 and chip duration is 1us.

## Slide 18: Summary
Doc.: IEEE 802.11-25/1580r1
New DL sync sequence is proposed: 00110011100010111010001011010110
In order to support both correlation receiver and differential decoder, the special segment needs to be Manchester coded.
Both 12 bits special segment 101010101010 with chip duration of 2us, and 8 bits special segment 10101010 with chip duration of 1 us can reduced FAR to low than 1%.

## Slide 19: Straw Poll #1
Doc.: IEEE 802.11-25/1580r1
Do you agree to add the following content to the 802.11bp SFD?
  Special Segment in the DL sync field is Manchester coded.
  The special segment is constructed by a sequence of 101010101010.

## Slide 20: Appendix
September 2025
Doc.: IEEE 802.11-25/1580r1

## Slide 21: False alarm handing in data portion(5)
Doc.: IEEE 802.11-25/1580r1
Observation: In case of 250kbps, with 8 bits special segment(chip duration of 2us), FAR is a little bit higher than 1%.

## Slide 22: False alarm handing in data portion(6)
Doc.: IEEE 802.11-25/1580r1

## Slide 23: False alarm handing in data portion(7)
Doc.: IEEE 802.11-25/1580r1

## Slide 24: False alarm handing in data portion(8)
Doc.: IEEE 802.11-25/1580r1

## Slide 25: Synchronization performance for correlation decoder(3)
Doc.: IEEE 802.11-25/1580r1

## Slide 26: Synchronization performance for correlation decoder(4)
Doc.: IEEE 802.11-25/1580r1

## Slide 27: Synchronization performance for differential decoder(3)
Doc.: IEEE 802.11-25/1580r1
Observation: Without special segment, there is a high sync error floor for differential decoder. The Sync failure can be reduced to less than 1% with the special segment.
  Note: Sync failure is defined as cases when the sync error is great than ¼ chip.
  Note: the segment is 8bit 10101010, every chip duration is 2us.

## Slide 28: Synchronization performance for differential decoder(4)
Doc.: IEEE 802.11-25/1580r1
Observation: With 6 bits special segment(chip duration of 1us), sync failure is a little bit higher than 1% for differential receiver.

## Slide 29: Reference
IEEE 802.11-25/1222r0 AMP Downlink Sync Field Design for Transmission to Non-Backscatter STAs
IEEE 802.11-25/1248r1 Discussions on DL Sync Field for Non-Backscatter STAs: Part I
IEEE 802.11-25/1223r0 SYNC Field Design Discussion
IEEE 802.11-25/0705r0 An Analysis of SYNC Field for Downlink PPDU
IEEE 802.11-25/1580r0 Follow-up on Sync field for AMP PPDU
IEEE 802.11-25/1249r1 Discussions on DL Sync Field for Non-Backscatter STAs: Part II
Doc.: IEEE 802.11-25/1265r3
July 2025
Wang Ke (OPPO)