## Slide 1: Optical Wireless Channel modelling and Measurements
Date: 2025-09-18
Authors:

## Slide 2: Abstract
This contribution presents channel modelling and measurement campaigns for enhanced light communications. A new channel modelling approach has been introduced which can operate in real environments using point cloud data captured by a LIDAR scanner. The accuracy of the channel models are validated using our optical channel sounder system. Finally, potential use case scenarios available for channel modelling and measurements are discussed in the context of UCM project.
September 2025

## Slide 3: Outline
Introduction
Motivation
ELC channel modelling method
  3D environment modelling based on LIDAR data
  Enhanced modelling methodology
ELC measurement campaigns
Use case scenarios for UCM
Conclusions

## Slide 4: Introduction
Enhanced Light Communictaion (ELC)
  Wireless communication using light
  Mobile, bidirectional, high-speed data
  Light remains in one room, No EMI
Applications
  Leverage unique properties of light (competition with WiFi)
  Industry, hospitals, offices, class- and conference rooms
Fundamental challenges for channel modelling
  LOS vs. NLOS, Path loss, Link blockage
  Weak multipath reflections, but measurable
Two main modeling approaches
  Deterministic : Site-Specific, highly accurate models
  Stochastic : Non-site specific, based on probability distributions
Industrial OWC
Class rooms
Medical OWC
LOS Propagation
NLOS Propagation

## Slide 5: Motivation
SoA: Deterministic channel models
  Manual entry of 3D environment
  Tiles, Iterative, Modified Monte Carlo, Ray tracing
Limitations of present models
  Approaches are very complex and time-consuming
  Not suitable for distributed MIMO with multiple mobile users
  Barely validated in realistic environments
New channel modelling
  Complete 3D modeling using LIDAR point cloud data
  Efficient modelling with significantly reduced complexity
    more efficient generation of MU-MIMO CIRs and mobility
  Experimental validation in various indoor environments
3D model using LIDAR
Lightsource & detector specifications
New ELC channel modelling approach
Channel Response
Channel Parameters
Performance Parameters
Input
Propagation Model
Output
Block Diagram

## Slide 6: 3D modelling using LIDAR
Motivation : Reduce complexity in 3D modelling
Leica RTC360 as LIDAR scanner (wavelength: 1550 nm)
Scanned at multiple positions in the room (to overcome occlusions / invisible regions)
Point cloud data from multiple scans are processed and optimized
LIDAR scanner is calibrated for reflectance estimation [1]
output data: (x,y,z) coordinates, surface normal, and reflectance of each detected point
Leica RTC360
Results in the room before and after intensity correction

## Slide 7: ELC channel modeling methodology
Impulse response divides into 3 main parts
In previous work, the same methodology was used for all three parts
  High complexity
In this work, the simplest approach is used in each part
  Significantly reduced complexity
LOS signal  is modelled analytically
Initial reflections  modelled precisely by using the frequency-domain method [2]
Higher order diffuse reflections  modelled by using the integration sphere method [3]
Total channel model =
Typical impulse response for single link [3]

## Slide 8: LOS channel
Analytical model
LOS channel model: Based on orientation and optical parameters of Tx and Rx
Challenge: Identify LOS blockage and shadowing effects in real environments
  Applied visibility analysis using hidden point removal algorithm, a known methodology in computer graphics
is the transfer function coefficient between Tx and Rx
is the delay time
is the visibility parameter between Tx and Rx

## Slide 9: Visibility analysis
Motivation : Define link blocking and shadowing effects
Define all points in point cloud data that are visible from each Tx, Rx, and surface point position
Use hidden point removal algorithm: Visibility Radius = , optimal value for 1.5 [4]
R = 3
R = 1
R = 4
Position of Tx1(looking towards the corner)
Variation of visible points for different R values

## Slide 10: NLOS with initial reflections
Used frequency-domain (FD) method
  Reflections are represented as consecutive matrix multiplications, instead of convolutions in time domain
Only first M (1, 2, 3) diffuse reflections are modelled [5]-[7]
  Each scanned point in the room is considered as a small surface element (i.e. polygon)
Diffuse channel model
  where is the reflection order up to which NLOS channels are modelled using FD method ( is first NLOS)
  Visibility factor (free LOS) is included in Tx and Rx transfer vectors and in room transfer function
Tx transfer vector between transmitter and all surface elements,
Rx transfer vector from all surface elements to the Rx
Reflectivity matrix  Diagonal matrix, each diagonal element is the reflectivity of surface.
Room intrinsic function
represents the LOS transfer function from surface element to surface element

## Slide 11: Higher order diffuse reflections
Based on integrating sphere model [3]
  well-established since 25 years
All diffuse reflections together can be described by the integrating sphere (IS) model
  first-order low-pass due to exponential decay
  does not include any details of the room
  parameters depend on room size and avarage reflectivity of the room surface
New in this contribution
  subtract the power from or initial reflections from IS model

## Slide 12: Channel measurements
SISO scenarios
  Frequency sweep technique using VNA, narrowband
MIMO scenarios
  8x8 channel sounder, OFDM-based, wideband
Performed all three steps
  3D environment modelling using LIDAR
  Channel modelling
  Measurements using VNA/MIMO channel sounder
Metrics used
  Mean-square error (MSE) between measured and modelled channel
  Singular values
  Throughput
SISO measurement using VNA
MIMO channel sounder

## Slide 13: Empty room
Simple scenario for testing all steps
  LIDAR scan and reflectivity calculation
  SISO & MIMO measurements
  Performance evaluation
Point cloud data of the room
LIDAR scanning
d
SISO Measurements
Mobile scenario
MIMO Measurements

## Slide 14: Empty room
Results
Simulation results compared to measurements
  good agreement between measured and simulated channels
  MSE < 5% for LOS signals with sufficient signal strength
  MSE is higher for distant links, due to limited sensitivity of broadband MIMO channel sounder
Throughput results matched very well
  Mostly determined by strong signals
  Weak signals contribute less
  Throughput is lower if users are nearer to each other
Mobile Scenario
MIMO Scenario
Amplitude Responses at Rx1
Throughput result
Amplitude response of the channel for d = 2.5 m
Amplitude response of the channel for d = 3 m
SISO Scenario

## Slide 15: Conference room
Distributed MU-MIMO scenario
6 x 12 MIMO Measurements
  LOS, downlink scenario, Tx infrastructure is always the same, 3 Rx configurations
    Scenario 1: Rxs are far from each other
    Scenario 2: 2 Rx pairs
    Scenario 3: 4/6 Rxs are at one position
LIDAR scanning
Point cloud data of the room
6x12 MIMO Measurement Scenario

## Slide 16: Conference room
Results
Channel responses
  MSE < 5% for the signals with sufficient signal strength
Throughput results
  average MSE < 1 % for all scenarios at low SNR
  usual “fake capacity” for low-rank scenarios due to the noise in our measurements
Throughput results

## Slide 17: Medical Scenario
Measurement-based performance evaluation
  Communication around operating table
Measured all channels in distributed MIMO matrix
  Frequency sweep technique using VNA
  Including reflections and blockages in the environment
Considered scenario as (virtually) distributed 6x4 MU-MIMO
  Considered 5 different multiplexing schemes
LOS Scenario
Total Throughput
Individual user throughput
NLOS Scenario

## Slide 18: Medical Scenario
Channel modelling and coverage mapping for LiFi
  Communication around operating table
Point cloud data acquisition
  LIDAR placed at multiple positions
Combined Coverage map for all Txs
Tx1
Tx2
Tx3
With 3 Txs pointing towards floor
Point cloud data used for modelling

## Slide 19: Industrial scenario
Measurements in a manufacturing plant
  Using channel sounder system
  Broadband distributed 8×6 MIMO channel measurements
  Highlights potential of distributed MIMO OWC systems
i

## Slide 20: Use case scenarios for UCM
Scenarios available for UCM
  Conference room, office room, class room (data are available in both simulations and measurements)
  Medical (Simulation data/LIDAR available)
  Industry (Manufacturing hall, storage shelf: TBD)
  Data format
    Raw data versus time on Mentor
    Incl. an interpolation routine
    Documentation on channel modelling

## Slide 21: Conclusions
Channel modelling
  LIDAR based 3D scan and reflectance estimation
  accurate, low complexity and efficient channel modelling approach
  useful for large distributed MU-MIMO scenarios and mobile scenarios
Validation by measurements
  good agreement between the results
Available use cases/reference scenarios
  Medical, residential/office, industrial

## Slide 22: References
V. Jungnickel et al. “A physical model of the wireless infrared communication channel”, In: IEEE Journal on Selected Areas in Communications 20.3 (2002), pp. 631–640.
H. Schulze, “Frequency-Domain Simulation of the Indoor Wireless Optical Communication Channel”. In: IEEE Transactions on Communications 64.6 (2016), pp. 2551–2562.
S. Katz et al. “Direct visibility of point sets”, ACM Trans. Graph. 26, 3 (July 2007), 24–es.
K. Tan and X. Cheng. “Surface reflectance retrieval from the intensity data of a terrestrial laser scanner”. In: Journal of the Optical Society of America A 33.4 (2016), pp. 771–778.
S. M. Mana et al., "An Efficient Multi-Link Channel Model for LiFi," PIMRC 2021, pp. 1-6.
S. M. Mana et al., "LIDAR-assisted Channel Modelling for LiFi”, 2022 OFC, San Diego, CA, USA, 2022.
S. M. Mana et al., "LIDAR-Assisted Channel Modelling for LiFi in Realistic Indoor Scenarios", IEEE Access, vol. 10, 2022.
S. M. Mana et al., “Experiments in Non-Line-of-Sight Li-Fi Channels”, GLC 2019.
S. M. Mana et al., "Distributed MIMO Experiments for LiFi in a Conference Room," CSNDSP 2020.
S. M. Mana et al., "LiFi Experiments in a Hospital," 2020 OFC, San Diego, CA, USA, 2020.
S. M. Mana et al,, "Distributed Multiuser MIMO for LiFi: Experiments in an Operating Room," JLT, vol. 39, no. 18, Sept.15, 2021.