## Slide 1: Sync Follower AP during Co-BF sounding
Date: 2025-09-15
Authors:

## Slide 2: Abstract
In CoBF, there are two types of AP in terms of CFO pre-correction roles.
They are defined as follows:
  Sync-reference AP: The AP acting as a frequency reference during sounding stage and beyond
    Does not need to remember CFO re-corrections
  Sync-Follower AP: The AP that aligns its frequency with respect to the Sync-reference AP during sounding stage and beyond
    Remembers pre-corrections
As of D1.0, a Co-BF AP role is determined during the Co-BF MAPC agreement.
In this contribution, we discuss additional considerations when deciding the Co-BF AP role.

## Slide 3: Background
As mentioned in 11bn D1.0, the sync-follower AP maintains a CFO precorrection value computed from an NDPA frame received from the sync-reference AP. The sync-follower AP transmits its cross-BSS NDPA pre-corrected using the CFO precorrection value.

## Slide 4: Role Determination
As mentioned in 11bn D1.0, whether an AP is a sync-reference AP or a sync-follower AP is determined during the Co-BF MAPC agreement. Role switching/updating may also be done by updating the Co-BF MAPC agreement.
After Co-BF group formation, periodic Co-BF sounding and/or Co-BF transmission may be initiated by either the sync-reference or sync-follower AP
MAPC Negotiation
Request
AP 1
AP 2
MAPC Negotiation
Response
Request
Accept
Group formation
Reference & follower roles decided
Reference
Follower
Co-BF
Sounding
Co-BF
Transmission
Co-BF
Transmission
Co-BF
Sounding

## Slide 5: Problem
Right after an initial Co-BF MAPC agreement where one AP becomes a sync-reference AP and another AP becomes a sync-follower AP, the sync-follower AP may first obtain a TXOP and initiate Co-BF sounding. In this case, the sync-follower AP does not have a CFO precorrection value to use.
  Similar situation occurs right after the two APs switch role right when a Co-BF MAPC agreement is updated.
Reference
AP1
Follower
AP2
STA1
associated
with AP1
STA2
associated
with AP2
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
Follower AP wins contention prior
to any pre-correction measurement
CoBF Formation

## Slide 6: Option 1
Before AP 2 transmits the NDPA, the current spec requires that a Co-BF sounding invite and response be exchanged with AP1.
Hence, AP 2 may simply just compute the initial pre-correction value from the Co-BF sounding response frame.
Reference
AP1
Follower
AP2
STA1
associated
with AP1
STA2
associated
with AP2
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
CoBF Formation
CoBF Sounding Invite
CoBF Sounding Response
Pre-precorrection using
Co-BF Sounding Response

## Slide 7: Option 2
Alternatively, the spec may prohibit AP 2 to initiate the first cross-BSS sounding procedure prior to AP 1.
Reference
AP1
Follower
AP2
STA1
associated
with AP1
STA2
associated
with AP2
NDPA
NDP
CSI
BFRP
CoBF Formation
CoBF Sounding Invite
CoBF Sounding Response
NDPA
NDP
CSI
BFRP
Pre-precorrection using
NDPA
Wait for AP 1 NDPA

## Slide 8: Conclusion
In this contribution, we discussed the potential problem during the first cross-BSS Co-BF sounding after establishing the Co-BF MAPC agreement.
We proposed two solutions to make the sync-follower AP behavior more predictable and reliable during Co-BF sounding.

## Slide 9: SP 1
Do you support that a sync-follower AP may use the Co-BF response frame to estimate the CFO pre-correction used during cross-BSS Co-BF sounding sequence it initiates.

## Slide 10: SP 2
Do you support that a sync-follower AP shall not initiate a cross-BSS Co-BF sounding sequence without a valid CFO pre-correction value.