## Slide 1: Efficiency Improvement of NPCA
Date: 2024-05-05
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | OPPO |  |  | v-xinliangxiao@oppo.com
Liuming Lu |  |  |  | 
Chaoming Luo |  |  |  | 
Ning Gao |  |  |  | 

## Slide 2: Introduction
NPCA operation allows STAs to switch to NPCA primary channel for transmission when the BSS primary channel is busy.
When STA switches to NPCA primary channel, it contends the channel access with the STAs of OBSSs operating there. It is possible that the transmissions by the NPCA operation congests the NPCA primary channel.
In order to minimize the effect of the NPCA operation on the NPCA primary channel, the high efficiency of the transmission by the NPCA operation should be guaranteed.
In this contribution, we discuss how to guarantee the high efficiency of the transmission by the NPCA operation.

## Slide 3: Efficiency of NPCA
The below performances of NPCA enabled STAs affect the efficiency of the NPCA operation
  The occurrence probability of the different view problem
  The MCS used on the NPCA primary channel
  The collision probability on the NPCA primary channel
It is very complicated for STAs to measure those performances directly and report them to AP. Also, the report is created after the NPCA operation when the low efficiency of NPCA has already occurred.
Thus, we need to find a simple way to indicate the above performances in advance.
Here, we propose to use RSSI to predict the efficiency of NPCA.

## Slide 4: How to use RSSI for NPCA
RSSI can be measured no matter the NPCA operation is enabled or not. It is simple to measure the RSSI between AP and non-AP STAs.
  E.g., non-AP STA could measure the beacon RSSI.
The high RSSI received by non-AP STA implies that
  The occurrence probability of the different view problem is low
  The MCS used on the NPCA primary channel is high
Thus, if we set a minimum requirement of RSSI of enabling NPCA operation, the efficiency of NPCA operation can be guaranteed.
Then, AP can use the minimum requirement of RSSI to control the number of NPCA enabled STAs, which reduces the collision probability on the NPCA primary channel.

## Slide 5: Procedure of enabling NPCA
AP announces the minimum RSSI requirements of enabling NPCA operation in its BSS.
If a STA cannot meet the minimum RSSI requirements, then the STA shall not enable the NPCA.
If a STA meets the minimum requirements, then the STA sends a request to AP to enable the NPCA.
NOTE: we can set minimum RSSI requirement as an optional parameter.

## Slide 6: Summary
In this contribution, we propose to let AP set a minimum RSSI requirement for STAs to enable NPCA operation.
A minimum RSSI requirement can be used to
  Mitigate the different view problem
  Imply that the high MCS can be used on NPCA primary channel
  Control the number of NPCA STAs

## Slide 7: SP1
Do you agree that AP may announce the minimum RSSI requirements of NPCA operation?