## Slide 1: IMMW Channelization
Date: 2025-07-xx
Authors:
Name | Affiliations | Address | Phone | Email
Cheng Chen | Intel |  |  | cheng.chen@intel.com
Laurent Cariou |  |  |  | 
Qinghua Li |  |  |  | 
Juan Fang |  |  |  | 
Ehud Reshef |  |  |  | 
Tomer Gidoni |  |  |  | 
Oren Avraham |  |  |  | 
Ofer Benjamin |  |  |  | 
Notes: September 2012

## Slide 2: Overview
In this contribution, we propose some initial considerations for IMMW channelization in the mmWave band.

## Slide 3: IMMW channelization proposal
We propose to divide the 14 GHz frequency span (57-71 GHz) to multiple non-overlapping channels (similar concept with the 5-7 GHz channelization).
X MHz channels center frequency is defined by X x N (X MHz harmonics)
  For example, assuming we are going to define 640 MHz and 320 MHz.
    640 MHz x N as the center frequency of 640 MHz channels, we can place 21 channels in total (14 GHz / 640 MHz = 21.875).
    The proposed center frequency keeps 280 MHz from the two sides of the band edge (57 GHz and 71 GHz).
    Each 640 MHz is composed of two adjacent 320 MHz channels, preserving spectral symmetry.

## Slide 4: Channel numbering
We propose to align the channel numbering to be unique across different bandwidth options (similar to the way things are defined in the lower bands).

## Slide 5: IMMW Channelization Proposal – Outline (1)
Total bandwidth: 57-71GHz (14GHz)
Chart: Proposed IMMW Channelization Scheme
| 55 | 57 | 57 | 71 | 71 | 75
US, CAN, EU | 0 | 0 | 2 | 2 | 0 | 0
KOR, JPN, SGP, TW, HK, AUS | 0 | 0 | 1.9 | 1.9 | 0 | 0
BRZ, CHL, MEX, NWZ | 0 | 0 | 1.8 | 1.8 | 0 | 0
CHN | 0 | 0 | 1.7 | 1.7 | 0 | 0
160MHz

## Slide 6: IMMW Channelization Proposal – Outline (2)
If 640 MHz channels are to be defined:
  aligned with 640xN harmonics, total of 21 non-overlapping channels
  Spaced evenly with guard band of 280 MHz from band edge
Chart: Proposed IMMW Channelization Scheme
| 55 | 57 | 57 | 71 | 71 | 75
US, CAN, EU | 0 | 0 | 2 | 2 | 0 | 0
KOR, JPN, SGP, TW, HK, AUS | 0 | 0 | 1.9 | 1.9 | 0 | 0
BRZ, CHL, MEX, NWZ | 0 | 0 | 1.8 | 1.8 | 0 | 0
CHN | 0 | 0 | 1.7 | 1.7 | 0 | 0
160MHz

## Slide 7: IMMW Channelization Proposal – Outline (3)
If 320 MHz channels are to be defined:
  Same concept, with two 320M channels for each 640M channel
Chart: Proposed IMMW Channelization Scheme
| 55 | 57 | 57 | 71 | 71 | 75
US, CAN, EU | 0 | 0 | 2 | 2 | 0 | 0
KOR, JPN, SGP, TW, HK, AUS | 0 | 0 | 1.9 | 1.9 | 0 | 0
BRZ, CHL, MEX, NWZ | 0 | 0 | 1.8 | 1.8 | 0 | 0
CHN | 0 | 0 | 1.7 | 1.7 | 0 | 0
160MHz

## Slide 8: IMMW Channelization Proposal – Outline (4)
640M Channels | 
Channel # | Center Freq
Guard band | 0.28
1 | 57.6
2 | 58.24
3 | 58.88
4 | 59.52
5 | 60.16
6 | 60.8
7 | 61.44
8 | 62.08
9 | 62.72
10 | 63.36
11 | 64
12 | 64.64
13 | 65.28
14 | 65.92
15 | 66.56
16 | 67.2
17 | 67.84
18 | 68.48
19 | 69.12
20 | 69.76
21 | 70.4
Guard band | 0.28
Total # | 21 channels
320M Channels |  |  |  | 
Channel # | Center Freq |  | Channel # | Center Freq
Guard band | 0.28 |  |  | 
1 | 57.44 |  | 23 | 64.48
2 | 57.76 |  | 24 | 64.8
3 | 58.08 |  | 25 | 65.12
4 | 58.4 |  | 26 | 65.44
5 | 58.72 |  | 27 | 65.76
6 | 59.04 |  | 28 | 66.08
7 | 59.36 |  | 29 | 66.4
8 | 59.68 |  | 30 | 66.72
9 | 60 |  | 31 | 67.04
10 | 60.32 |  | 32 | 67.36
11 | 60.64 |  | 33 | 67.68
12 | 60.96 |  | 34 | 68
13 | 61.28 |  | 35 | 68.32
14 | 61.6 |  | 36 | 68.64
15 | 61.92 |  | 37 | 68.96
16 | 62.24 |  | 38 | 69.28
17 | 62.56 |  | 39 | 69.6
18 | 62.88 |  | 40 | 69.92
19 | 63.2 |  | 41 | 70.24
20 | 63.52 |  | 42 | 70.56
21 | 63.84 |  | Guard band | 0.28
 |  |  | Total # | 42 channels

## Slide 9: Conclusions
In this contribution, we propose some initial considerations for IMMW channelization in the mmWave band.
  We propose to divide the 14 GHz frequency span (57-71 GHz) to multiple non-overlapping channels.
  We propose that the center frequency for adjacent channels of X MHz BW are spaced by X MHz.

## Slide 10: SP
Do you support the following design for the 11bq channelization:
  Channels with same BW are non-overlapping.
  Center frequency for adjacent channels of X MHz BW are spaced by X MHz.

## Slide 11: References
[1] 11-25-0363-00-00bq-channelization-in-immw