## Slide 1: A Spatially Consistent Small-Scale Fading Model for Multiple Frequency Bands
Date: 2025-09-17
Name | Affiliations | Phone | email
Stephan Jaeckel | SJC / Fraunhofer HHI | +49 30 60980512 | jaeckel@sjc-wireless.com
Volker Jungnickel | Fraunhofer HHI | +49 162 2552756 | volker.jungnickel@hhi.fraunhofer.de
Authors:

## Slide 2: Abstract
Provide an accessible, tutorial-style introduction to geometric stochastic channel modeling (GSCM)
Content Overview:
  Fundamentals of GSCM: geometry-based approach to multipath modeling.
  Large-scale fading: pathloss, shadowing, and spatial consistency concepts.
  Small-scale fading: multipath clusters, Doppler, and delay spreads.
  Polarization modeling: cross-polar components and depolarization effects.
  Spatial correlation & Sum-of-Sinusoids method: generating correlated fading fields.
  Station mobility: time evolution and trajectory-based channel updates.
Takeaways
  Understanding of how spatially consistent and realistic channels are generated.
  Practical insight into using models like 3GPP TR 38.901 and QuaDRiGa for simulation studies.

## Slide 3: Available Models
IEEE Models:
  TGn/ac/ax model (2.4 or 5 GHz) – docs. 11-03/940r4, 11-09/0308r12, 11-14/0882r4
  TGad/ay model (60 GHz) – doc. 11-15/1150r9
  TGbb model for optical bands - doc. 11-18/1582r4
3GPP Models:
  ITU-R M.2135 (2D, based on WINNER-2, 1-6 GHz)
  3GPP TR 38.901 v19.0 (3D, 0.5-100 GHz) – Macro, Micro, Office
  3GPP TR 36.777 v15.0 (3D, 0.5-100 GHz) – Aerial Vehicles
  3GPP TR 37.885 v15.3 (3D, 0.5-100 GHz) – V2X Sidelink
  3GPP TR 38.811 v15.4 (3D, 2 and 28 GHz) – Non-terrestrial Networks (NTN)
QuaDRiGa (0.1 to 100 GHz), Open-Source

## Slide 4: Types of Channel Models
TGn/ac/ax
TGad/ay/QuaDRiGa
TGbb

## Slide 5: How Geometric-Stochastic Models Work

## Slide 6: Small-Scale-Fading Model
Multiple transmitters and receivers
3D-coordinates (xt,yt,zt), (xr,yr,zr)
Signal path consists of:
  departure direction
  first-bounce scatterer (FBS)
  last-bounce scatterer (LBS)
  arrival direction
Dual-mobility and spatial consistency = anything to anything communication
Spatially correlated random processes [*]
4 steps: delays, angles, powers, spreads
[*] Jaeckel, S.; Raschkowski, L.; Burkhardt, F. & Thiele, L. “Efficient Sum-of-Sinusoids based Spatial Consistency for the 3GPP New-Radio Channel Model” Proc. IEEE Globecom Workshops '18, 2018

## Slide 7: Spatial Consistency
In a spatially consistent propagation channel propagation phenomena do not vary greatly over time and location.
h1
h2
h2

## Slide 8: Sum-of-Sinusoids Model
Represents spatially correlated fading as a sum of multiple sinusoids
Produces a stationary Gaussian process with specified autocorrelation.
Efficiently generates samples along a spatial trajectory (e.g., user movement, station placement).
Computationally efficient: avoids large covariance matrix decompositions.
Used in performance evaluation of MIMO systems, beamforming, and channel estimation.
Suitable for large-scale system-level simulations (e.g., 5G/6G network planning).
Spatially correlated random processes

## Slide 9: Sum-of-Sinusoids Model
SOS Model:
Generation of Normal-distributed parameters
Definition
Autocorrelation Function ACF (1D)
3D-ACF of SOS-Method
Needed!
[*] M. Patzold, U. Killat, and F. Laue, “A deterministic digital simulation model for suzuki processes with application to a shadowed Rayleigh land mobile radio channel,” IEEE Transactions on Vehicular Technology, vol. 45, no. 2, pp. 318–331, May 1996

## Slide 10: Sum-of-Sinusoids Model
Examples

## Slide 11: SSF Model – Delays
Delays are drawn randomly with exponential delay distribution
is the delay distribution, the LSF delay spread,
Delays are normalized (breaks spatial consistency!)
Scaling is required to compensate for the effect of LOS peak (depending on Ricean K-Factor)
Delays are initialized randomly with exponential delay distribution
is spatially correlated normal distributed random variable (e.g. from SOS model)
describes spatial correlation
DS and are not applied yet
No sorting
No empiric KF scaling
Implicit channel reciprocity for dual-mobility
3GPP TR 38.901
QuaDRiGa

## Slide 12: SSF Model – Angles
Azimuth angles use inverse Gaussian PAS
Elevation (zenith) angles use inverse Laplacian PAS
is the path power
is azimuth angle spread from LSF model
is zenith angle spread from LSF model
and are empiric scaling coefficients
Angles are initialized randomly with uniform angle distribution
and are spatially correlated normal distributed random variables
No powers, no , no , no empiric scaling
Implicit channel reciprocity
3GPP TR 38.901
QuaDRiGa

## Slide 13: SSF Model – Cluster Powers
Powers depend only on the delay spread
Cluster powers are normalized
In case of LOS, additional specular component is added in case of LOS propagation
Powers depend on delay and angle spreads
Scaling coefficients , , , adjust delay and angle spreads for multiple frequencies
Same clusters, different powers
LOS path is always present (may have zero-power)
3GPP TR 38.901
QuaDRiGa

## Slide 14: SSF Model – Delay and Angle Spreads
Final values are already included
Output of the SSF model may not match the LSF model (only distributions agree)
Calculate DS from initial delays and powers and adjust delays to include LSF DS
Calculate ASs from initial angles and powers and adjust angles to include LSF ASs
3GPP TR 38.901
QuaDRiGa

## Slide 15: Evaluation Method
Generate random MT positions
Use 3GPP LSF model to generate DS, ASs and KF
  3GPP TR 38.901 UMi scenario [*]
  LOS and NLOS propagation conditions
  3 frequencies: 1 GHz, 6 GHz, and 60 GHz
Use new SSF model to generate delays, angles and path-powers  generate channel coefficients
Calculate DS and ASs from channel coefficients
Compare results with LSF output
[*] 3GPP TR 38.901 v15.0.0; “Study on channel model for frequencies from 0.5 to 100 GHz”; 2018

## Slide 16: Results
Delay Spread (DS)
Delay Spread [ns]
Delay Spread [ns]

## Slide 17: Results
Azimuth of Departure Angular Spread (ASD)
Offset for large ASs
Angular Spread [deg]
Angular Spread [deg]

## Slide 18: Results
Azimuth of Arrival Angular Spread (ASA)
LOS output median ~ 30°
Angular Spread [deg]
Angular Spread [deg]

## Slide 19: MIMO Model
MIMO Channel
Matrix H
L Taps
Receive
Antenna
Tap
Power
Polarization
Transmit
Antenna
Tap Delay
Phase
Offset
Frequency
Offset

## Slide 20: Polarization model
Amplitude of a path
WINNER / 3GPP / IEEE polarization model
Power
Phase
Polarization Change
Receive Antenna Model

## Slide 21: Polarization model (new)
Linear transformations
Rotation
Phase shift
Mirror
Rotation
Rotation
Notes: = theta
Φ = phi
ϴ = theta
= kappa
= gamma
𝜗 = theta
Φ = phi
ϴ = theta
𝜅 = kappa
𝛾 = gamma

## Slide 22: Polarization model
Impact
  Correct XPR for circular polarization ( satellite and air-to-ground communication)
  Change antenna orientations at model runtime ( virtual field trials)
Jaeckel, S.; Börner, K.; Thiele, L. & Jungnickel, V.; "A Geometric Polarization Rotation Model for the 3-D Spatial Channel Model"; IEEE Trans. Antennas Propag., 2012, 60, 5966-5977
Comparison

## Slide 23: Dual-Mobility Outlook

## Slide 24: Conclusions
Small-scale-fading (SSF) model to support:
  Spatial consistency
  Simultaneous mobility of the transmitter and receiver
  Simultaneous simulation of multiple frequencies
Sum-of-Sinusoids
  Efficient method to generate spatially correlated random processes
  Used for both, LSF and SSF
Polarization and MIMO models
Seamless integration with existing models
Open-source implementation available

## Slide 25: Appendix

## Slide 26: Results
Azimuth angles must be inside
Power-angular spectrum limits AS to values below 100°
KF which limits the AS even further
Example:
  Requested AS of 100°
  Variable KF from -20 to 20°
  Achievabe AS around 80° (NLOS)
3GPP UMi-LOS KF is 9 dB with 5 dB STD
  Explains ASA offset in results
Maximal Angular Spread
LOS Output Median ~ 30°

## Slide 27: Scaling coefficients
Delays
Angles