## Slide 1: TGbi, Frame Anonymization Study
Date: 2025-09
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT BlueHalo | Sunrise, FL |  | Graham.smith@bluehalo.com gsmith@wi-ficonsulting.org

## Slide 2: Why this Presentation?
I have put in several CIDs concerning FA and its complexity. I feel that I need to explain why.
I simply want to make sure that the TG has really thought about this and is happy in what it is proposing.
Presentation:
Look at long term presence privacy
Look at Frame Anonymization
Look at alternatives

## Slide 3: Long Term Presence privacy - Intro
STAs are using random MACs?
  Is it only a privacy problem when the user can be associated with the STA?
What type of networks/locations are of concern?
  Hotel, office (small, medium, large), campus, home, restaurant, shop, retail/mall, airport, coffee shop, pub, conference, bus, train, etc.…?
Use Case?
  21/0993 described a hotel use case that is based upon the STA using the same MAC address every time it associates such that the hotel recognizes the client.
  This was mitigated with random MAC and IRM or Device ID.
  Requiring hotel Wi-Fi to implement Frame Anonymization as well as IRM or Device ID is a major step.

## Slide 4: How would this “monitoring’ work?
First need to link MAC and user
To tie a user to a MAC address at association is not easy.
  Needs to be a single point of entry
  Need to observe actual association request by user
  Needs to be an isolated event, i.e., difficult if many STAs are associating.
  Before Random MAC there was no need to observe at actual location, the MAC could be pre-recorded
What type of networks are reasonable to link user and mobile?

## Slide 5
Detecting still present is also not easy, what if an ESS (can 3rd party cover all APs?), or target strays to opposite side of network.
Has target left or just strayed to blind spot?
Can “bad guy” get coverage over entire network, (all the ESS?)
Larger the network the more difficult?
Do we assume a sophisticated set up with several monitoring points?
Who is the target user? Special “at risk” or?

## Slide 6
To detect departure is not easy.
  Observer must be within network coverage - target user is beyond the network before dropping
Target does not indicate “I’m leaving now”. It’s gone…
Again, only really works on single entry/exit point unless sophisticated monitoring

## Slide 7: Long term Presence Monitoring using Wi-Fi
Not as easy in practice as may be first thought.
  In fact, it is difficult and unreliable.
  How much does the “bad guy” rely on Wi-Fi monitoring vs sightings? If serious, the Wi-Fi is very much seconda
Random MAC solves the easy user/MAC address link.
  Cited Use Case was pre-TGbh and did not assume Random MACs.
  Also,
  How useful is monitoring duration of a random MAC?
Essential that the device is linked to a user. Just monitoring Wi-Fi traffic is not enough.
  Natural breaks in traffic, plus roaming make constant monitoring impractical in many cases

## Slide 8: User and MAC address
A random MAC being present for a “long duration” on a network, is not by itself a privacy concern.
ONLY if the MAC is attributed to a user, is there any form of privacy concern.
SO
What type of network is FA aimed at?
What type of user is FA aimed at?
NB. I am assuming that FA is aimed at mobile devices, e.g., phones

## Slide 9: Large networks - A
Examples A: Large Office complex, Campus, Conference
STAs join and leave at similar times, multiple entrances
  Difficult if not impossible to monitor a single STA associating
STAs tend to be present over long periods
  Long term presence is the norm
Networks tend to be ESSs
  Difficult if not impossible to cover complete area
FA? - Numbers are sufficient, BUT, difficult to see how privacy really at risk. Is this a network that FA is targeting?

## Slide 10: Large networks - B
Examples B: Mall, Hospital, Hotel (more fluid traffic than A)
Some STAs join and leave at similar times (staff)
  Long term presence is the norm
  Mobile traffic not constant (users are working, mostly background traffic)
More STAs join, stay and leave throughout day (visitors)
  Difficult to monitor a single STA associating due to numbers
  Difficult if not impossible to cover complete area,
  Mobile traffic tends to be in bursts (times of background, then bursts)
Networks tend to be ESSs
  Difficult if not impossible to cover complete area
  Note: Often phones will be using 5G. If connecting to local Wi-Fi, could be at any time, outside or inside building.
FA? - Numbers are sufficient, BUT, difficult to see if privacy really at risk. Is this a network that FA is targeting?

## Slide 11: Medium size networks - C
Examples: restaurants, shops (mid size),
Single entry/exit point but when does user connect?
  Returning user connects automatically when in range
  New user has to physically connect and be seen
  How many customers use 5G anyway?
Traffic is sporadic, not easy to monitor
User can be observed, limited area.
  How important is Wi-Fi privacy when user(s) can be seen?
FA – Is this a targeted network? Very doubtful if Wi-Fi privacy is important c.f. observable privacy.

## Slide 12: Medium size networks - D
Examples: bars, night clubs
Easier to see customers as they go in and come out.
  Difficult to match to Wi-Fi device as when devices connect is variable.
If privacy is concern, it won’t be the Wi-Fi.
  If a celebrity, then not being seen entering/leaving is the only problem (unless they want to be seen!)
Traffic very bursty per device,
  long periods no activity – have they left or just drinking or dancing?
FA – Is this a targeted network? Is this the market?
  Possibly best case (only case) for FA but relying on Wi-Fi to follow someone is a bit of a stretch.

## Slide 13: Small networks - E
Examples: Home, small shop, doctor’s office, bus, train
  Easy to watch, not real need to rely on Wi-Fi.
  Before random MAC these networks best for finding out the MAC address.
Obviously, FA is of no real use in these examples
  Relying on Wi-Fi monitoring is a big stretch
  Maybe train is different, but not sure I would monitor Wi-Fi to check when person gets off

## Slide 14: Networks/FA Summary
Large networks best for FA but most difficult to monitor
  Large coverage, ESS, multiple entries, etc.
Smaller the network the more practical to match user to device, but the more obvious who is present
  No real need to use Wi-Fi for presence.
  FA not really needed
Traffic models
  FA seems to assume that all STAs are transmitting all the time (i.e., easy to see one MAC disappear and another appear)
  This is not the general case – maybe bus or train, but is FA useful there?
Difficult (for me) to point at ideal case where FA is going to be really useful.
TG needs to identify target case(s) so as to get FA right, i.e., not too complex, not too easy, but just right.

## Slide 15: Long Term Presence monitoring - Questions
How much of a problem is this in reality?
Is the complexity of Frame Anonymization really worthwhile?
  How much complexity is really required when already difficult enough to “follow” target.
  FA is complex, not easy for interoperability
Could FA be simplified?

## Slide 16: Frame Anonymization

## Slide 17: FA considerations
OK, Let’s Assume User/MAC has been identified, and is being monitored and there are enough STAs N in an FA epoch:
After first epoch all N STAs change MAC address,
RESULT
Observer could see N MACs go and N new MACs.
  Now need to monitor N,
  Next change, assuming still N STAs in epoch, still need to monitor N
HENCE,
As long as a STA has gone through one change, not clear if further changes really improves privacy
  Especially if large network where most join early and stay.
SO
WHY do we need (short) repetitive epochs?
  What is case for 1 second epochs, or even 1 second increments?
  Creates problems with sleeping STAs, and transition period becomes complex.
Aside: If STAs are joining and leaving regularly, then better, but then simple reassociation would then work.

## Slide 18: Epoch boundary variations
Q WHY do we need to vary the epoch boundaries?
A “To make it difficult for the observer”
BUT
  Predicting epoch boundary does nothing. It’s the number of STAs in the epoch that matters
  STAs have variable traffic, contention etc., they do not all use their new MACs at once, they are naturally spread out (beyond the epoch boundary)
Knowing when STAs change address does not help the observer.
Observer sees N MAC addresses disappear and N new ones. Knowing when this might happen does not change much, if anything.

## Slide 19: Processing Complexity, c.f. TGbh
TGbh bent over backwards to avoid solutions requiring processing, i.e., hashes and keys
  An early comparison of candidate schemes was to compare processing need/complexity.
Compare Device ID and IRM to
Frame Anonymization:

## Slide 20: Device ID and IRM processing

## Slide 21: FA Processing
EDP_BPE_FA_block = KDF-Hash-Length (PGTK, "EDP BPE frame anonymization", n)
EDP_AP_addresses, Link ID 0, to 14
EpochTSFStartTime(n) = PlannedTSFStartTime(n) for the link + ΔIT
with
PlannedTSFStartTime(n) = FirstPlannedEpochTSFStartTime + (n – EpochNumberOffset) × EpochInterval
ΔIT = int (KDF-Hash-Length(PGTK, "ERCM", n)) mod TimeRange
EDP FA block =KDF-Hash-Length( KDK, "EDP CPE frame anonymization", n)
EDP_BPE_FA_block = KDF-Hash-Length (PGTK, "EDP BPE frame anonymization", n),
OSN = (SN + EDP_SN_offset) mod 212,
OPN = (PN + EDP_PN_offset) mod 248
OGroupAddress = (group address + EDP_Group_Anonymization_Offset) mod 246
OTSF = (Timestamp + EDP_Timestamp_offset) mod 264
NOTE: For AP and STA, encoding and decoding. Not showing ”de-anonymization”

## Slide 22: Could FA be simplified?
Why not initialize PNs and SNs rather than offset?
  How much traffic is buffered over from one epoch to next?
  Increase transition time if really worried.
Why have multiple epochs?
  Need a minimum number of STAs in an epoch to be effective
  IF problem when too many STAs in an epoch (is there one?) then Epochs should be added as number of STAs increases.
  Why have all this selection overhead?
Why have short 1 second epochs periods?
  Only one epoch is enough to hide a STA. Doing it repeatedly does not improve the privacy (if enough STAs in the epoch).
  Multiple epochs is only effective if change in number of STAs in epoch. Longer period is fine.

## Slide 23: Reassociate to same AP
(protected) Reassociation:
  Resets SN, PN
  Assigns new AID
  Authentication state is preserved, no 4 w HS required
  DS MAC retained so consistent on the DS
BUT
  BA agreement and TWT settings are torn down
At present no difference in reassociation to same or new AP
  NB. when roaming, old AP forwards unsent packets and disassociates STA (i.e., it knows the STA).
  Could add indication of a simple reassociation for privacy (instruction to maintain PS, BA, TWT settings) ?
Is in control of the mobile
  Choose time to do it, i.e., when not busy
  No processing overhead.
  Works well for large networks (again what is target network?)

## Slide 24: Reassociation
Non-AP MLD MAC exposed in Authentication.
  Encrypted in protected (re)association request
DS MAC
DS MAC encrypted in protected (re)association request
DS MAC is used for the DS
When reassociating, non-AP MLD uses random STA MAC and random MLD MAC
IRM
IRM provides next non-AP MLD MAC
Non-AP MLD is known
Simply use the non-AP MLD MAC as usual.

## Slide 25: I know 11bi has committed to FA
BUT I truly believe that FA, as it is, is overkill.
Ideally, I would like to see FA simplified
  Identify the target network and work from there
  No need for fast epochs,
  Sort out how epochs get sufficient numbers
  No need for jittering the epoch boundaries.
AND
Add a simpler, alternative (reassociation).
  Add method for reassociation to same AP to be improved? (maintain TWT and BA for example).
  Maybe have a switch start time when AP says, “start now”, and STAs reassociate when they decide good time to do so. No complex processing required.

## Slide 26: Questions/Reactions?
Is the TG really happy with its FA solution?
  How big is this presence problem to solve?
  What is the target network?
  When does FA work, and when might reassociation work?
ACTIONS:
Simplify FA?
Add alternatives? (Not to replace, but add)
  Special (privacy) reassociation to same AP case, maintaining agreements.

## Slide 27: Straw Poll - 1
Does the task group agree that FA needs more work in one or more of the following areas:
  number of epochs,
  epoch periods,
  numbers of non-AP MLDs per epoch,
  Identifying target network(s)
  Reducing processing requirements
  Supplying candidate settings

## Slide 28: Straw Poll - 2
Should the task group investigate adding a method for a non-AP MLD to use reassociation to the same AP to change its parameters?
Note: Investigate Reassociation to same AP for privacy reasons and maintaining agreements (TWT, BA agreement).