## Slide 1: CSI Report for Cross BSS Co-BF Sounding
Date: Sep 12, 2025
Authors:

## Slide 2: Introduction
Coordinated BeamForming (Co-BF) is one of the features that were agreed on for 11bn;
Some progress was made on the following two phases: channel sounding phase, and transmission Phase;
For Co-BF sounding, the cross BSS Co-BF sounding sequence has been agreed as follows;
For the CSI report, the STA would identify the txPow on the UL target receive power and the pathloss between the STA and the associated AP.

## Slide 3: Problem Statement
The received power at the cross BSS AP (AP1) may be lower than expected received power,
  - The PL00 is 60dB, and UL target receive power is set as -70dBm, then the transmit power is -10dBm;
  - The PL10 is 75dB, then the received power at AP1 is -85dBm.
The received power difference at the cross BSS AP among the STAs may be large;
  - The received power of STA0 at AP1 is -85dBm [PL00 = 60dB, PL10 = 75dB], .
  The received power of STA1 at AP1 is -75dBm [PL01 = 60dB, PL11 = 65dB],
  The received power gap between STA0 and STA1 is 10dB [depending on PL Gap].
The cross BSS CSI seems more important for the cross BSS AP but not the associated AP.

## Slide 4: On UL Target Receive Power
For cross BSS Co-BF sounding, it is proposed that the UL target receive power within the BFRP trigger frame is configured for the cross BSS AP but not the associated AP,
  - The STA would identify the txPow on the indicated UL target receive power, and the PL between the STA and cross BSS AP (it can be achieved or estimated in advance).

## Slide 5: On UL Target Receive Power
For UL target receive power configuration for the cross BSS AP:
  The UL target receiver power is set by the initiating AP by implementation,
  Or, the UL target receiver power is reported by the response AP in the Co-BF sounding response frame.

## Slide 6: SP1
Do you support adding the following text to the SFD:
  For cross BSS Co-BF sounding, the UL target receive power, within the BFRP trigger frame transmitted by the initiating AP, is configured for the response AP.

## Slide 7: SP2
Do you support adding the following text to the SFD:
  For cross BSS Co-BF sounding, the UL target receive power for the response AP, is determined
    by the initiating AP’s implementation,
    or, on the UL target receive power reported by the response AP in the Co-BF sounding response frame.