## Slide 1: NDPA Indication of Cross-BSS Sounding Feedback Status
Date: 2025-07-31
Authors:

## Slide 2: Abstract
In this contribution, we discuss the merits of using UHR NDPA to indicate the failure/success of cross-BSS sounding and the coexistence opportunities with other feedback status indication mechanisms .

## Slide 3: Background
In a previous contribution [1], we discussed two options to perform cross-BSS sounding and three options to indicate the status of the cross-BSS CSI feedback
In this contribution, we advance the discussion to add more color to two topics
  Performing cross-BSS sounding in a single TXOP or two TXOPs.
  Using UHR NDPA to communicate the status of cross-BSS CSI feedback
DISCLAIMER: Both proposals are intending to add more flexibility with minimal added complexity. Further, they can coexist with other proposals to provide options for efficient cross-BSS sounding operation

## Slide 4: Cross-BSS Sounding in a Single TXOP (1/3)
To use beamforming transmission in DL, both coordinated AP or coordinating AP need to perform in-BSS sounding whether they will engage in a coordinated beamforming transmission or not.
  The in-BSS sounding does not require coordination between APs where each of them can perform the in-BSS sounding in their own acquired TXOP.
The in-BSS sounding session should include the STAs that an AP plans to schedule in an MU transmission, a beamforming transmission, and/or a coordinated beamforming transmission.
  In fact, an AP may select the STAs that are good candidates for coordinated transmission before performing its in-BSS sounding
  The selection criteria of the STAs is out of scope for this contribution

## Slide 5: Cross-BSS Sounding in a Single TXOP (2/3)
Accordingly, in coordinated sounding procedure, one option is to focus on the cross-BSS sounding rather than the in-BSS sounding
  This does not limit the options of how to perform the sounding, it just adds one more option.
Following this line of thought, a single TXOP cross-BSS sounding may be an attractive option
  Single invite/response exchange to agree on the sounding parameters
  Single contention to acquire the sounding TXOP for both APs
  Cross-BSS channel for both APs ages nicely since it is acquired at almost the same time.
  The refresh rate of cross-BSS sounding can be controlled independently of the refresh rate of in-BSS sounding

## Slide 6: Cross-BSS Sounding in a Single TXOP (3/3)

## Slide 7: Indication of Cross-BSS Sounding Status in NDPA (1/5)
One or more bit(s) in the first or second STA Info fields can be used to indicate that the preceding cross-BSS CSI was not received successfully.
  By receiving this indication, the initiating AP learns the CSI feedback status of cross-BSS1
  The initiating AP decodes the CSI in cross-BSS2 and can determine whether it is received successfully or not
This indication is the earliest possible indication … just after the fact!
By the end of the cross-BSS sounding session, the initiating AP has full knowledge of the status of both cross-BSS sounding feedback
If the initiating AP is the sharing AP in the data transmission phase, it has all it needs to decide how to proceed before the data transmission phase.

## Slide 8: Indication of Cross-BSS Sounding Status in NDPA (2/5)
Early indication in case of cross-BSS sounding in single TXOP

## Slide 9: Indication of Cross-BSS Sounding Status in NDPA (3/5)
When the cross-BSS sounding is performed over two TXOPs, the NDPA indication still can be used for the CSI feedback status indication
Another possibility to indicate the cross-BSS CSI feedback status is to use the CoBF Sounding Invite frame
  Both options can coexist to enable flexibility for a better performance (especially in the case of cross-BSS sounding in a single TXOP)

## Slide 10: Indication of Cross-BSS Sounding Status in NDPA (4/5)
Another possibility to indicate the cross-BSS CSI feedback status in case of cross-BSS sounding over two TXOPs

## Slide 11: Indication of Cross-BSS Sounding Status in NDPA (5/5)
What if the responding AP in sounding is the sharing AP in data transmission?
  The responding AP knows the status of cross-BSS1, but not the status of cross-BSS2
  The responding AP may initiate the data transmission phase assuming cross-BSS2 is received successfully.
  The initiating AP may then reject the data transmission phase in the response frame and provide a rejection reason to indicate this fact, no cross-BSS2 is available.
But this seems asymmetric behavior for both the initiating AP and the responding AP!
  In the micro-level (one sounding round), it seems the behaviors are asymmetric.
  In the macro-level (over a long period of time), any of the APs can change roles and become either the initiating/responding AP or sharing/shared AP.
  Considering this perspective, the behavior is perfectly symmetric over a long period of time.

## Slide 12: To Summarize
Initiating
AP
Responding
AP
NDPA
NDP
Cross-BSS CSI1 Feedback
Overheard by Responding AP
Invite
Response
NDPA
NDP
Cross-BSS CSI2 Feedback
Overheard by
Initiating
AP
CoBF Invite
. . .
CoBF Response
CoBF Trigger
Sharing
AP
Shared
AP
Initiating
AP
Responding
AP
NDPA
NDP
Cross-BSS CSI1 Feedback
Overheard by Responding AP
Invite
Response
NDPA
NDP
Cross-BSS CSI2 Feedback
Overheard by
Initiating
AP
CoBF Invite
. . .
CoBF Response
CoBF Trigger
Shared
AP
Sharing
AP
The sharing AP has full knowledge of the cross-BSS CSI feedback status and can decide whether to send the CoBF Invite or not.
The sharing AP knows the status of cross-BSS CSI1 and shared AP may reject the CoBF invitation if it doesn’t receive cross-BSS CSI2 successfully.
Scenario 1
Scenario 2

## Slide 13: Conclusions and Way Forward
Performing the cross-BSS sounding for both APs in a single TXOP is an attractive option.
A simple indication in the UHR NDPA may be used for early indication of cross-BSS sounding failure.
  CoBF Sounding Invite is another option for this indication in case of cross-BSS sounding over two TXOPs
Indication of the cross-BSS sounding failure as one of the reasons for rejection in the data transmission phase is a complementary solution
  When combined with indication of failure in NDPA, it will allow for the efficient and early indication of cross-BSS sounding failure.
This solution can coexist with other solutions and provide an option for efficient coordinated sounding operation.

## Slide 14: SP 1
Do you agree to add the following to 11bn SFD:
The status of cross-BSS sounding may be indicated in the NDPA as one option for cross-BSS CSI feedback status indication
- One or more bit(s) in the first or second STA Info field can be used to indicate that the preceding cross-BSS CSI was not received successfully or not available at the AP sending the NDPA.

## Slide 15: References
[1] 25/1203r1 Discussions on Cross-BSS Sounding