## Slide 1
IEEE 802.11 TGbp Straw Poll Deck
Chair: Bo Sun (Sanechips)
Vice Chair: Steve Shellhammer (Qualcomm)
            Rakesh Taori (Infineon)
Secretary: Sebastian Max (Ericsson)
          Tech Editor: Yinan Qi (OPPO)

## Slide 2: Abstract
This document accommodates the TGbp straw polls and the results since 2025 Sep interim session.
This document only records straw polls that intended for a TG motion (including SFD motion and PDT motion).

## Slide 3
2025 Sep Interim Session
AM1, Sep 18, 2025

## Slide 4: PDT Straw Polls
SP #1:
Do you agree to accept the proposed spec text in 11-25/1333r2 as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification when incorporate the proposed spec text to generate IEEE P802.11bp D0.1?
Result: No objection

## Slide 5: PDT Straw Polls
SP #2:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1439r2 (You-Wei Chen)
Result: No objection

## Slide 6: PDT Straw Polls
SP #3:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1373r2 (Steve Shellhammer)
Result: No objection

## Slide 7: PDT Straw Polls
SP #4: [deferred to PM1 Thu]
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1344r4 (components of arch, Rojan Chitrakar)
Result:

## Slide 8: PDT Straw Polls
SP #5:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1548r3 (timing related parameters, Amichai)
Result: No objection

## Slide 9: PDT Straw Polls
SP #6:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1410r2 (Nelson Costa)
Result: No objection

## Slide 10: PDT Straw Polls
SP #7: [deferred to PM1 Thu]
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1636r3 (Nelson Costa)
Result:

## Slide 11: PDT Straw Polls
SP #8:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1599r3 (Weijie Xu)
Result: No objection

## Slide 12: PDT Straw Polls
SP #9:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1568r4 (Yinan Qi)
Result: No objection

## Slide 13: PDT Straw Polls
SP #10:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1600r5 (Yinan Qi)
Result: No objection

## Slide 14: PDT Straw Polls
SP #11:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1584r1 (Bin Qian)
Result: No objection

## Slide 15: PDT Straw Polls
SP #12:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1364r3 (PHY DL Modulation and Coding, Panpan Li)
Result:

## Slide 16: PDT Straw Polls
SP #13:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1615r4 (Chuanfeng He)
Result:

## Slide 17: PDT Straw Polls
SP #14:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1616r3 (Chuanfeng He)
Result:

## Slide 18: PDT Straw Polls
SP #15:
Do you agree to accept the following PDT proposal as part of IEEE P802.11bp D0.1, and grant the tech editor privilege to make editorial modification?
11-25/1545r1 (Rui Cao)
Result:

## Slide 19: SFD PHY SP Set #1 (Amichai Sanderovich)
SP #1: Do you agree to add the following text into section 4.4.3 of the 11bp SFD ?
11bp defines mandatory forward error correcting code (FEC) of coding rate ½ for the data portion of UL active transmission in 2.4 GHz at rates of 0.25,1Mbps and non-coded mode at rate of 4Mbps
[Reference contributions: 11-25/1002r1, 11-25/1215r1]
Result:
SP #2: Do you agree to add the following text into section 4.4.3 of the 11bp SFD ?
11bp defines forward error correcting code (FEC) for the data portion of UL active transmission in 2.4 GHz based on the code as defined in 17.3.5.6 in 80211-2020
[Reference contributions: 11-25/1002r1 , 11-25/1215r1]
Result:

## Slide 20: SFD PHY SP Set #1 (Amichai Sanderovich)
SP #3: Do you agree to add the following text into section 4.4.3 of the 11bp SFD ?
802.11bp amendment will recommend the use of a subset of all available S1G channels for WPT transmission, for each regulatory domain, in order to minimize interference to other devices
Note: How to determine the subset is TBD
[Reference contributions: 11-25/1002r1]
Result:
SP #4: Do you agree to add the following text into section 4.4.3 of the 11bp SFD ?
802.11bp amendment will recommend the use of a subset S1G ISM channels ch for WPT transmission where ch minimizes |Fch – 900| over the regulatory domain and Fi is the center frequency of channel i in MHz
Details of specific channels, channel widths and regulatory domains TBD
[Reference contributions: 11-25/1002r1]
Result:

## Slide 21: SFD PHY SP Set #2 (Alice Chen)
SP #1: Do you agree to add the following text into the 11bp SFD ?
In the data field of AMP UL active transmission in 2.4 GHz,
    250kbps data rate only uses 1us chip duration and rate 1/2 binary convolution code (BCC)
    1Mbps data rate only uses 0.25us chip duration and the same rate 1/2 BCC
    4Mbps doesn’t use BCC
[Reference contributions: 11-25/1215r1, 11-25/1552r0, 11-25/1262r1, 11-25/0790r0]
Result:

## Slide 22: SFD PHY SP Set #3 (Shengquan Hu)
SP #1: Do you agree to add the following text into the 11bp SFD ?
The Uplink Sync Field Transmission from a non-Backscatter STA for all data rates shall have a length 48.
[Reference contributions: 11-25/1552r0]
Result:
SP #2: Do you agree to add the following text into the 11bp SFD ?
Length-48 sync sequence for UL non-backscatter transmission is constructed by repeating length-24 base sequence twice, i.e. S48 = [S24 S24]
The length-24 base sequence is given as below:
  S24=[1, 1, 1, 1, 1, 0, 1, 0, 0, 1, 1, 0, 0, 1, 1, 0, 0, 0, 0, 1, 0, 1, 0, 0]
[Reference contributions: 11-25/1552r0]
Result:

## Slide 23: SFD PHY SP Set #4 (Steve Shellhammer)
SP #1: Do you agree to add the following text into the 11bp SFD ?
The first segment of the Downlink Sync Field transmitted to non-Backscatter STAs, uses the sequence 𝑾 for the 250 kb/s data rate or the sequence for the 1 Mb/s data rate. The sequences are:
  𝑾 = 01011010010111000110001011101100
  = 10100101101000111001110100010011
[Reference contributions: 11-25/1554r0]
Result:

## Slide 24: SFD PHY SP Set #5 (You-Wei Chen)
SP #1: Do you agree to add the following text into the 11bp SFD ?
An DL AMP PPDU in 2.4 GHz is identified in its U-SIG with the following setting:
  PHY version value set to 0
  One or multiple Validate bit subfields sets to 0 or subfield(s) set to a validate state.
  PPDU Type And Compression Mode value sets to 3.
[Reference contributions: 11-25/?]
Result:

## Slide 25: SFD PHY SP Set #6 (Nelson Costa)
SP #1: Do you agree to add the following text to the 11bp SFD ?
The AMP DL PPDU for bistatic backscattering operation in 2.4GHz shall be PPDU subtype 2.
  PPDU subtype 2 consists of the 802.11bp preamble, an AMP SYNC field, and an AMP Data field and an Excitation field.
  The AMP SYNC is the same sync design as for active Tx non-AP AMP STA.
  The AMP Data uses the same Manchester encoded OOK with data rates of 250kbps, 1 Mbps.
The AMP Uplink PPDU for bistatic backscattering operation in 2.4GHz shall reuse the following fields from active Tx.
  The AMP SYNC is the same sync design as for active Tx non-AP AMP STA.
  The AMP Data uses the same Manchester encoded OOK with data rates of 250kbps, 1 Mbps. 4 Mbps is TBD.
[Reference contributions: 11-25/1541]
Result:

## Slide 26: SFD PHY SP Set #6 (Nelson Costa)
SP #2: Do you agree to add the following text to the 11bp SFD ?
The receiver requirements for a non-AP AMP STA capable of bistatic backscatter shall be the same as that of an active Tx non-AP AMP STA. This includes,
  Clock accuracy, center frequency accuracy.
[Reference contributions: 11-25/1541]
Result:

## Slide 27: SFD PHY SP Set #7 (Lumin Liu)
SP #1: Do you agree to add the following text into the 11bp SFD ?
AMP Sync field for uplink backscattering transmission has a structure of [S, S, S] for both 2.4GHz and sub-1GHz.
  S = [1 1 0 1 0 1 0 0].
[Reference contributions: 11-25/1556r0]
Result:
SP #2: Do you agree to add the following text into the 11bp SFD ?
The same chip duration shall be used for AMP backscattering uplink Sync field and AMP backscattering uplink data field in sub-1GHz.
[Reference contributions: 11-25/1556r0]
Result:

## Slide 28: SFD PHY SP Set #8 (Panpan Li)
SP #1: Do you agree to add the following text into the 11bp SFD ?
11bp shall adopt the following channelization scheme for EU:
    Bands: 865-868MHz
    BW: 200kHz
    Channel center frequency: 865.1+N*0.2, N=0,…,14;
Note: support of 400kHz bandwidth in 915-921MHz is TBD.
[Reference contributions: 11-25/?]
Result:

## Slide 29: SFD PHY SP Set #8 (Panpan Li)
SP #2: Do you agree to amend the motion #97 in the 11bp SFD as below ?
The AMP-S1G Downlink PPDU shall support single data rate:
      62.5 kb/s
[Reference contributions: 11-25/?]
Result:
SP #3: Do you agree to add the following text into the 11bp SFD?
    The AMP-S1G Uplink PPDU shall support at least the following data rates:
      250 kb/s
      1 Mb/s
[Reference contributions: 11-25/?]
Result:

## Slide 30: SFD PHY SP Set #9 (Rui Cao)
SP #1: Do you agree to add the following text into the 11bp SFD ?
The AMP SYNC in DL PPDU for mono-static backscattering operation is [0 1 1 1 1 0 1 0] for both 2.4GHz and sub-1GHz bands?
The SYNC chip duration for sub-1GHz is 8us
[Reference contributions: 11-25/1543r0]
Result:

## Slide 31: SFD MAC SP Set #1 (Rojan Chitrakar)
SP #1: Do you agree to amend FM-9 as below in the 11bp SFD ?
An AMP AP transmits an AMP Trigger frame indicating a time-slot based random access session for non-AP AMP STAs. The frame may carry following parameters:
  Session ID: Identifies the random access session
  ACW: Indicates the upper limit of the random access contention window
    ACWmin: Indicates the minimum value of the upper limit of the random access contention window
    ACWmax: Indicates the maximum value of the upper limit of the random access contention window
  Encoding of parameters is TBD.
  Other parameters are TBD.
[Reference contributions: 25/1246r0, 25/1242r0]
Result:

## Slide 32: SFD MAC SP Set #1 (Rojan Chitrakar)
SP #2: Do you agree to amend MM-27 as below in the 11bp SFD ?
Upon receiving an AMP Trigger frame indicating a time-slot based random access session, a non-AP AMP STA performs the following actions:
  If it is a new random access session, the non-AP AMP STA initializes ACW and randomly chooses an ABO Counter (ABOC) in the range [0, ACW]. Else, if it a known random access session and the non-AP AMP STA’s previous transmission in the session was unsuccessful, the non-AP AMP STA updates the ACW to (2*ACW+1) and randomly chooses an ABOC in the range [0, ACW].
  If the ABOC is less than the number of slots (N) allocated by the AMP Trigger frame, the non-AP AMP STA transmits an uplink AMP PPDU carrying the uplink response in one of the slots allocated by the AMP Trigger frame. Else, ABO Counter is decremented by N.
[Reference contributions: 25/1246r0, 25/1242r0]
Result:

## Slide 33: SFD MAC SP Set #1 (Rojan Chitrakar)
SP #3: Do you agree to add the following text to the 11bp SFD ?
The Type field is the first 4 bits of the Frame Control field of AMP frames and differentiates between:
  AMP WUR frames: AMP frames for communication with AMP Enabled non-AP STAs
    The frame format of AMP WUR frames inherit from WUR frames defined by IEEE 802.11ba.
  Non-backscatter AMP frames: AMP frames for communication with Active Tx non-AP AMP STAs
  Backscatter AMP frames: AMP frames for communication with backscatter non-AP AMP STAs
[Reference contributions: 25/1547r0, 25/1102r1, 25/0817r0, 25/0818r0]
Result:

## Slide 34: SFD MAC SP Set #1 (Rojan Chitrakar)
SP #4: Do you agree to add the following text into the 11bp SFD ?
The size of the ID field(s) in AMP frames for communication with Active Tx non-AP AMP STAs and Backscatter non-AP AMP STAs is 16 bits.
[Reference contributions: 25/1547r0, 25/1102r1, 25/0817r0, 25/0818r0]
Result:
SP #5: Do you agree to add the following text the 11bp SFD ?
The size of the Type Dependent Control field, if present in the MAC Header field of AMP frames for communication with Active Tx non-AP AMP STAs and Backscatter non-AP AMP STAs is 8 bits.
[Reference contributions: 25/1547r0, 25/1102r1, 25/0817r0, 25/0818r0]
Result:

## Slide 35: SFD MAC SP Set #1 (Rojan Chitrakar)
SP #6: Do you agree to add the following text into the 11bp SFD ?
The length of the Frame Body field, if present in AMP frames for communication with Active Tx non-AP AMP STAs and Backscatter non-AP AMP STAs, is indicated in octets by a Length field in the MAC Header.
  The size of the Length field is TBD bits
[Reference contributions: 25/1547r0, 25/1102r1, 25/0817r0, 25/0818r0]
Result:
SP #7: Do you agree to add the following text into the 11bp SFD ?
A second ID field may be present to indicate Transmitter ID in AMP frames for communication with Active Tx non-AP AMP STAs.
[Reference contributions: 25/1547r0, 25/1102r1, 25/0817r0, 25/0818r0]
Result:

## Slide 36: SFD MAC SP Set #1 (Rojan Chitrakar)
SP #8: Do you agree to add the following text into the 11bp SFD ?
A Protected field is present in the Frame Control field of AMP frames for communication with Active Tx non-AP AMP STAs to indicate whether the AMP frame is protected by a security algorithm.
  If the AMP frame is protected, a Protection Control field is carried in the Frame Body of the AMP frame. The size of the Protection Control field is TBD bits.
  The security algorithm is TBD
[Reference contributions: 25/1547r0, 25/1102r1, 25/0817r0, 25/0818r0]
Result:
SP #9: Do you agree to add the following text into the 11bp SFD ?
11bp defines one type of AMP frames for communication with Backscatter non-AP AMP STAs to carry a UHF command.
  The UHF command, excluding CRC if any, is carried in the Frame Body field of the AMP Frame.
  NOTE – The UHF commands are defined by the EPC® Radio-Frequency Identity Generation-2 Ver-2 UHF RFID Standard
[Reference contributions: 25/1547r0, 25/1102r1, 25/0817r0, 25/0818r0]
Result:

## Slide 37: SFD MAC SP Set #2 (Ian Bajaj)
SP #1: Do you agree to add the following text into the 11bp SFD ?
IEEE 802.11bp allows AMP Service Period parameters to be carried in a broadcast AMP frame (name TBD).
Note: The presence of the AMP Service Period parameters is configurable.
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1244r0, 11-25/1560r0]
Result:
SP #2: Do you agree to add the following text into the 11bp SFD ?
The AMP Service Period parameters to be carried in a broadcast AMP frame include SP ID, SP Start Time, SP Interval, and SP Minimum Wake Duration. The SP ID serves to uniquely identify the AMP Service Period. The SP Interval is the time interval between two subsequent service periods with the same SP ID. The SP Start Time is the start time of the AMP Service Period.
Note: The SP Minimum Wake Duration refers to the minimum wake up time defined in Motion #75 (MM-22)
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1244r0, 11-25/1560r0]
Result:

## Slide 38: SFD MAC SP Set #2 (Ian Bajaj)
SP #3: Do you agree to add the following text into the 11bp SFD ?
The timing granularity of the AMP AP’s partial timestamp carried in a broadcast AMP frame is 64us.
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1244r0, 11-25/1560r0]
Result:
SP #4: Do you agree to add the following text into the 11bp SFD ?
The length of the AMP AP’s partial timestamp carried in a broadcast AMP frame is 24 bits.
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1244r0, 11-25/1560r0]
Result:

## Slide 39: SFD MAC SP Set #2 (Ian Bajaj)
SP #5: Do you agree to add the following text into the 11bp SFD ?
IEEE 802.11bp defines the AMP TSF field to carry the AMP AP’s partial timestamp TSF [6:29] in a broadcast AMP frame.
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1244r0, 11-25/1560r0]
Result:
SP #6: Do you agree to add the following text into the 11bp SFD ?
The short timestamp when present in the AMP trigger frame carries the AMP TSF field, TSF [6:29] of the AMP AP’s partial TSF.
Other lengths of short timestamp configured to be present in the AMP trigger for some modes of operation is TBD.
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1244r0, 11-25/1560r0]
Result:

## Slide 40: SFD MAC SP Set #2 (Ian Bajaj)
SP #7: Do you agree to add the following text to the 11bp SFD ?
IEEE 802.11bp defines AWUR frame as one type of AMP frame with the Frame Body including WUR Frame (excluding FCS).
Note: AWUR means Ambient Wake-up Radio.
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1244r0, 11-25/1560r0]
Result:

## Slide 41: SFD MAC SP Set #2 (Ian Bajaj)
SP #8: Do you agree to add the following text to the 11bp SFD ?
The AMP Service Period parameters when present in the AMP trigger frame include SP ID, SP Start Time, SP Interval, and SP Minimum Wake Duration. The SP ID serves to uniquely identify the AMP Service Period. The SP Interval is the time interval between two subsequent service periods with the same SP ID. The SP Start Time is the start time of the AMP Service Period.
Note: The SP Minimum Wake Duration refers to the minimum wake up time defined in Motion #75 (MM-22).
[Reference contributions: 11-25/0039r0, 11-25/0285r1, 11-25/0787r0, 11-25/1244r0, 11-25/1560r0]
Result:

## Slide 42: SFD MAC SP Set #3 (Hui Luo)
SP #1: Do you agree to add the following text into the 11bp SFD ?
802.11bp shall specify a provisioning protocol that can initialize or update a PMK identified by a PMK ID with mutual authentication using a PSK shared between a configuration AMP AP and an AMP non-AP STA, where (1) the PSK is built in the AMP non-AP STA and obtained by the configuration AMP AP using an OOB method and; (2) the AMP non-AP STA can have an option to send back an encrypted PMK_ID and PMK using an encryption key derived from PSK-based mutual authentication?
Note:
    The secure AMP communication method is defined in Motion 64, 65, 66.
    Whether to include backscatter non-AP STAs in this method is TBD
[Reference contributions: 11-25/1437, 11-25/1086, 11-25/0819]
Result:

## Slide 43: SFD MAC SP Set #3 (Hui Luo)
SP #2: Do you agree to add the following text into the 11bp SFD ?
802.11bp shall specify an optional data field identifying a PMK ID and an AMP AP ID in the first authentication message in which the AMP AP sends ANonce to an AMP non-AP STA, such that the AMP non-AP STA can derive a PMK for secure communication with the AMP AP from a pre-configured PMK identified by the PMK ID for scalability purpose?
Note:
  The secure AMP communication method is defined in Motion 64, 65, 66.
  Whether to include backscatter non-AP STAs in this method is TBD.
[Reference contributions: 11-25/1437, 11-25/1086, 11-25/0831]
Result:

## Slide 44: SFD MAC SP Set #4 (Liwen Chu)
SP #1: Do you agree to add the following text into the 11bp SFD ?
For backscatter use case, the Frame Control field in DL frame carries the UL Rate field to indicate the data rate of the UL frame being solicited.
[Reference contributions: 11-25/1363]
Result:
SP #2: Do you agree to add the following text into the 11bp SFD ?
For backscatter use case, the 16-bit CRC computed over the STA’s EPC is used as the STA’s ID.
[Reference contributions: 11-25/1363]
Result:

## Slide 45: SFD MAC SP Set #5 (Yinan Qi)
SP #1: Do you agree to add the following text into the 11bp SFD ?
AMP non-AP STAs are allowed to report at least the following energy harvesting related parameters
  Indication of whether or not to support WPT function.
  Other parameters are TBD.
[Reference contributions: 11-25/1566r1, 11-25/1263r0]
Result:

## Slide 46: SFD MAC SP Set #6 (Sam Shi)
SP #1: Do you agree to add the following text into the 11bp SFD ?
11bp uses shortened ANonce/SNonce (exact size TBD, e.g. 32/64/128 bits) for transient key derivation in AMP secure operation.
[Reference contributions: 11-25/1593r0]
Result:
SP #1: Do you agree to add the following text into the 11bp SFD ?
11bp use short local addresses, as defined in Motion #68, for transient key derivation in AMP secure operation.
[Reference contributions: 11-25/1593r0]
Result:

## Slide 47: SFD MAC SP Set #7 (Chuanfeng He)
SP #1: Do you agree to add the following text into the 11bp SFD ?
For a non-AP AMP STA, duty-cycle configuration includes AMP Wake Interval to indicate the duration between the start of two consecutive AMP service periods that the AMP STA should enter an awake state.
[Reference contributions: 11-24/1775r1, 11-25/0341r0, 11-25/0831r0, 11-25/1252r0, 11-25/1581r2]
Result:

## Slide 48: SFD MAC SP Set #7 (Chuanfeng He)
SP #2: Do you agree to add the following text into the 11bp SFD ?
AMP AP transmits an AMP trigger frame indicating Duty-cycle configuration parameters, which include:
    Start time of the first AMP service period
    Number of AMP service periods (N) within a Wake Interval
    AMP service period duration
    AMP Wake Interval
    Other parameters are TBD
[Reference contributions: 11-25/0341r0, 11-25/0831r0, 11-25/1252r0, 11-25/1581r2]
Result:

## Slide 49: SFD MAC SP Set #7 (Chuanfeng He)
SP #3: Do you agree to add the following text into the 11bp SFD ?
Upon receiving an AMP trigger frame indicating a number of AMP service periods, a non-AP AMP STA randomly selects an AMP service period from the number of AMP service periods.
[Reference contributions: 11-25/0341r0, 11-25/0831r0, 11-25/1252r0, 11-25/1581r2]
Result:
SP #4: Do you agree to add the following text into the 11bp SFD ?
802.11bp defines short timestamp with the timing granularity of 1024 µs.
[Reference contributions: 11-25/1774r1, 11-25/0814r0, 11-25/0342r0, 11-25/1251r0, 11-25/1583r0]
Result:

## Slide 50: SFD MAC SP Set #7 (Chuanfeng He)
SP #5: Do you agree to add the following text into the 11bp SFD ?
802.11bp defines short timestamp with the length of 8 bits.
[Reference contributions: 11-25/1774r1, 11-25/0814r0, 11-25/0342r0, 11-25/1251r0, 11-25/1583r0]
Result: