## Slide 1: Multi-AP Co-SR Follow up
Date: 2025-09-29
Authors:
Name | Affiliation | Address | Phone | Email
Lei Zhou | New H3C |  |  | Zhou.leih@h3c.com
Jun Zhang | New H3C |  |  | 
Lei Kong | New H3C |  |  | 
Renmu Luo | New H3C |  |  | 
Xiangxin Gu | Spreadtrum |  |  | 
Yingqiao Quan | Spreadtrum |  |  | 

## Slide 2
Recap on Co-SR
11bn has defined a new spatial reuse mechanism at the TX OP level, where APs can coordinate their transmission power to achieve co-channel reuse at the TXOP level.
  Sharing AP uses a Trigger frame to notify the shared AP of the obtained TXOP.
  The specific content of the trigger frame is still under discussion, including power coordination schemes.
Sharing AP
Shared AP
Co-SR Invite
Co-SR Response
Co-SR Trigger
UHR PPDU
UHR PPDU

## Slide 3
Further discussion on Co-SR
AP can adjust power over the full bandwidth or partial bandwidth to meet the spatial multiplexing requirements of different scenarios.
  Full band power coordination(Supported in D1.0)：The coordinating AP notifies the coordinated AP to transmit data simultaneously via control frames, but limits the power of the full bandwidth to avoid downlink interference between APs.
  Partial band power coordination： The coordinating AP notifies the coordinated AP to transmit data simultaneously, limits the power on the partial bandwidth to avoid downlink interference, while keeping the power on other bandwidth portions unchanged to ensure edge user performance. It can be combined with features such as OFDMA and DSO.
coordinating AP
coordinated AP
Full band power coordination
band
TxPower
band
TxPower
band
TxPower
band
TxPower
Partial band power coordination
band
TxPower
band
TxPower
band
TxPower
band
TxPower
coordinating AP
coordinated AP
coordinating AP
coordinated AP
coordinating AP
coordinated AP

## Slide 4
Partial band power coordination Co-SR
Coordinating AP
Coordinated AP
Sub-band1
Sub-band2
Coverage
11.bn supports a maximum bandwidth of up to 320 MHz, while many terminals support less than 320 MHz. In such cases, power coordination across sub-bands can further improve the spectrum efficiency of Co-SR.
When coordinating power by sub-band, Sub-band1 can be constrained to low-power transmission, and Sub-band2 to high-power transmission. For near users of the coordinated AP, low-power transmission can be used in Sub-band1 to reduce interference to the edge users of the coordinating AP. For the edge users of the coordinated AP, high-power transmission can be applied in Sub-band2, while the coordinating AP schedules near users in Sub-band2 to control interference.
Adopt power collaboration of sub-bands for edge and near-point users

## Slide 5
Partial band power coordination Co-SR(2)
During the Co-SR negotiation phase, enhance the capability to support Partial Band Power Coordination Co-SR, including adding support for Partial Band Power Coordination Co-SR in the MAPC Negotiation Request frame and MAPC Negotiation Response frame.
In the Co-SR transmission phase, the Co-SR Trigger frame enhances the sub-band information shared in the User Info field, enabling subband power control.
To reduce the complexity of AP sub-band scheduling, the number of subbands can be controlled, e.g., up to 4; only used when the AP operating bandwidth is 160 MHz or 320 MHz.
AID 12 | 。。。 | Sub_band_num | Sub_band1_RU | Sub_band1_Power_reduce | Sub_band2_RU | Sub_band2_Power_reduce | ….
User Info field for partial band power coordination in the Co-SR trigger frame

## Slide 6
Proposal
Introduce Partial Band Power Coordination Co-SR to enable more efficient and flexible spatial reuse.
During the Co-SR negotiation phase, support negotiation of the Partial Band Power Coordination Co-SR.
During the Co-SR transmission phase, expand the Co-SR Trigger frame is to support power coordination of sub-bands.

## Slide 7: Straw Polls
SP1: Do you agree to include the following into the TGbn SFD?
Introduce Partial Band Power Coordination Co-SR to enable more efficient and flexible spatial reuse.
Results: Y, N, A
SP2: Do you agree to include the following into the TGbn SFD?
Support negotiation of the Partial Band Power Coordination Co-SR.
Results: Y, N, A
SP3: Do you agree to include the following into the TGbn SFD?
Expand the Co-SR Trigger frame is to support power coordination of sub-bands.
Results: Y, N, A

## Slide 8
Thank you