## Slide 1: Protecting the integrity of synchronisation frames
Date: 2025-10-02
Authors:

## Slide 2: Abstract
Beacon protection fills a security gap left open by protected management frames, as Beacon frames were not protected with the IGTK.
Beacon protection does not extend to Probe Response frames, resulting in a significant vulnerability in the synchronization process between a non-AP STA and an AP.
Attackers remain capable of exploiting Probe Response frames, resulting in comparable damage to that caused by targeting Beacon frames.
Furthermore, beacon protection can only be used post-association.

## Slide 3: Problem
802.11 defines beacon protection using a “beacon integrity group temporal key (BIGTK): A random value, assigned by the access point (AP), that is used to protect Beacon frames from that AP”.
The BIGTK is only used for integrity purposes (i.e. it is used to compute a MIC which is appended to the Beacon frame, but the frame is not encrypted).
The purpose of computing this MIC is to prove to the STA that each Beacon it receives is sent by the genuine AP, and not by an active attacker.
Without access to the BIGTK a sender could not have computed the correct MIC.

## Slide 4: Problem
Without beacon protection an attacker that does not have the IGTK can still launch active attacks against a BSS by sending spoofed Beacon frames with incorrect information.
Beacon Protection is so important that it is mandatory for EHT APs. The 802.11be amendment says:
  “The main MAC features in an EHT STA that are not present in HE STA or VHT STA or HT STA are the following:
  — Mandatory support for GCMP-256
  — In an EHT AP, mandatory support for MLO
  — In an EHT AP, mandatory support for beacon protection
  […]”.

## Slide 5: Problem
802.11 reference from section 11.1.5 Adjusting STA timers:
  “A STA in an infrastructure BSS or PBSS shall adopt the TSF timer value in a Beacon, S1G Beacon, Probe Response, PV1 Probe Response, DMG Beacon, or Announce frame transmitted by the BSS’s AP or PCP”.
802.11 reference from section 11.1.4.6 Operation of Supported Rates and BSS Membership Selectors element and Extended Supported Rates and BSS Membership Selectors element:
  “Upon receipt, the Supported Rates and BSS Membership Selectors element in Beacon and Probe Response frames is delivered to the management entity in a STA via the BSSBasicRateSet parameter in the MLME-SCAN.confirm primitive. The BSS membership selector information in Beacon and Probe Response frames is delivered to the management entity in a STA via the BSSMembershipSelectorSet parameter in the MLME-SCAN.confirm primitive”.

## Slide 6: Problem
802.11 reference from section 11.7.4 Interpretation of transmit power capability:
  “As regards the units of the Minimum Transmit Power Capability and Maximum Transmit Power Capability fields within the Power Capability element sent in a STA’s (Re)Association Request frame to an AP, if all of the following apply:
  — The STA is extended spectrum management capable.
  — The STA has dot11SpectrumManagementRequired or dot11RadioMeasurementActivated equal to
  true.
  — A Beacon or Probe Response frame has been received from the AP by the STA.
  — The Beacon or Probe Response frame includes one or more Transmit Power Envelope elements”.

## Slide 7: Problem
802.11 reference from section 35.15.3 Channel switching methods for an EHT BSS:
  “NOTE—If the EHT AP after switching to the new channel has an EHT BSS operating channel width wider than 160 MHz or EHT BSS operating channel width including at least one punctured 20 MHz subchannel, its associated EHT STAs that have performed channel switching or extended channel switching can also determine that information in the EHT Operation element in the Beacon or Probe Response frames received from the EHT AP on the new channel.”
This list is not exhaustive.

## Slide 8: Problem
STAs will treat Probe Response frames, which are unprotected, with a similar level of trust as protected Beacon frames – so STAs will modify their parameters (e.g. TSF) based on information from an unprotected Probe Response frame.
Probe Response frames can also carry a(n Extended) Channel Switch Announcement element. 802.11 states in Table 9-69—Probe Response frame body: “The Channel Switch Announcement element is optionally present if dot11SpectrumManagementRequired is true or dot11ExtendedChannelSwitchActivated is true” and “The Extended Channel Switch Announcement element is optionally present if dot11ExtendedChannelSwitchActivated is true”.

## Slide 9: Problem
In this scenario the attacker ensures Beacon frames sent by the genuine AP cannot be correctly received by the STA.

## Slide 10: Problem
When the STA elicits Probe Response frames, the attacker ensures the frame sent by the AP cannot be received, and injects its own malicious frame.
A malicious Probe Response frame can e.g. have a(n Extended) Channel Switch Announcement element, thus leading the STA to perform a channel switch, burning power and wasting time on a different channel, and being unable to communicate with the AP.

## Slide 11: Problem
In this scenario the attacker ensures the non-associated scanning STA will not receive Beacon or Probe Response frames from the genuine AP, just malicious ones injected by the attacker.

## Slide 12: Problem
The STA will be misled into believing the AP can support a different set of features, although the most sensible attack would use a subset of the AP’s features.
This would cause the STA to use a less capable association, or even deter the STA from ever associating.
Some elements are present in the Association Response frame that the AP sends to the STA (e.g. EHT Capabilities element) but the STA does not have to, and typically does not, reconsider its association parameters at that point.
Not all elements are allowed to be included in an Association Response frame (e.g. Power Constraint element).

## Slide 13: What would a solution look like?
A new key could be added – e.g. Synchronisation Temporal Key (STK)
  This key could provide integrity protection for multicast and unicast Probe Response frames + Beacon frames
  It can encapsulate BIGTK (e.g. have the same value, STK support implies BIGTK support)
  Needs capability signaling, KDE
  Con: yet another integrity key (i.e. on top of IGTK, BIGTK, CIGTK)
The scope of BIGTK could be extended to cover Probe Response frames as well
  Just needs capability signaling
  Con: The naming will be confusing
Extend the preassociation security negotiation (PASN) exchange, where used, to pass this new key from the AP to the STA.

## Slide 14: What would a solution look like?

## Slide 15: What would a solution look like?

## Slide 16: Straw poll
A mechanism to protect Probe Response frames should be added to foil active attacks
Y – add new key
Y – extend BIGTK
N

## Slide 17: Straw poll
A mechanism to protect Beacon and Probe Response pre-association should be added
Y
N