## Slide 1: TGbi, EPP Reassociation Proposal
Date: 2025-10
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT BlueHalo | Sunrise, FL |  | Graham.smith@bluehalo.com gsmith@wi-ficonsulting.org

## Slide 2: Introduction
In 25/1632r0 it was discussed that in a busy large network, a reassociation to the same AP could be used to change MAC address, reset SN and PN, and allocate a new AID
A Reassociation, however, also deletes effectively all agreements.
Hence, it was suggested that a special reassociation for privacy purposes may be possible.
This proposal satisfies CID 2023

## Slide 3: Encrypted Reassociation
An encrypted reassociation to the same AP does still require the 4 w HS to establish a new session key. It is, however, optimized for speed by using PMK caching to skip the initial authentication steps.
How it works:
PMK Caching: Client reassociates with same AP. AP can cache the PMK from previous session. Eliminates need to perform full EAP authentication again.
Optimized Handshake: 4-way HS performed to generate new session keys based on the cached PMK. Significantly faster as only the 4w HS , no authentication phase.

## Slide 4: Ads and Cons
Provides a method for Non-MLO devices.
  Frame Anonymization (FA) is MLO only.
Provides a simple alternative to MLO devices in large busy networks. No processing.
  Difficult to distinguish between joining and reassociating devices.
Under control of the non-AP device. Can choose when to change.
  Would reassociate when no traffic, also this makes it more difficult to follow as 4w HS present in both joining and reassociating.
Loading considerations, 4w HS required each time, compared to FA set up.
  As discussed in 25/1632 the difficulties of tracking a device in a large network in practice means that no real need to do this often.
  Devices are joining all the time anyway.

## Slide 5: Reassociation
11.3.5.4.
“…the following states, agreements and allocations shall be deleted or reset to initial values:
1) All EDCAF state
2) Any block ack agreements that are not GCR agreements
3) Sequence number
4) Duplicate detection caches
5) Anything queued for transmission
6) Fragmentation and reassembly buffers
7) Power management mode
8) WNM sleep mod
9) TDLS agreements
10) TPKSAs established with any peers
11) TSPECs
12) DMG TSPECs
13) GLK-GCR agreement
14) MSCS
15) SCS
16) (#11be)TWT

## Slide 6: EPP Reassociation
New MAC address (DS MAC remains)
SN reset
PN reset
AID allocated

## Slide 7: Outline of proposal
Add “Dot11EPPReassociationActivated”
Add a “EPP Reassociation Support” bit to the RSNXE
  AP uses it to show support
  STA uses it to indicate EPP Reassociation.
Non-AP STA/MLD can include bit only if:
  (Dot11EPPReassociationActivated is true)
  AP or AP MLD has “EPP Reassociation Support” bit set to 1.
  Encrypted Reassociation Request
  Reassociating to same AP
  DS MAC Address element is present
NOTE: Did originally consider adding an EPP Reassociation element for the STA to include in the Reassociation Request. The element would have no body and felt that the Support bit was enough

## Slide 8: Proposal
Add dot11EPPReassociationActivated
  For AP or AP MLD to indicate support
  For non-AP STA or non-AP MLD to indicate EPP Reassociation
dot11EPPReassociationActivated OBJECT-TYPE
SYNTAX TruthValue
MAX-ACCESS read-write
STATUS current
DESCRIPTION
"This is a control variable.
It is written by an external management entity or the SME.
Changes take effect for the next MLME-START.request primitive or MLMEJOIN.request primitive.
This attribute, when true, indicates the capability to support use of EPP Reassociation is enabled. The capability is disabled otherwise."
DEFVAL { false }
::= { dot11EPPStationConfigEntry 14 }

## Slide 9
31 | DS MAC Address Support | The DS MAC Address Support field is set to 1 when dot11DSMACAddressActivated is true and is set to 0 otherwise
32 | EPP Robust Individually Addressed Beamforming/CSI/CQI Frame Non-TB Tx Support | An EPP STA sets the EPP Robust Individually Addressed Beamforming/CSI/ CQI Frame Non-TB Tx Support field to 1 if dot11EPPRobustIndividuallyAddressedBea mformingCSICQIFrameNonTBTxActivate d is true. Otherwise, this field is set to 0. See 12.16.3 (EPP Robust Individually Addressed Management Frames and Robust Individually Addressed Beamforming/CSI/ CQI Frames).
34 | SAE Password Identifier Change Support | A non-AP STA that supports changing the SAE Password Identifier sets this to 1. Otherwise, this is set to 0.
ANA | EPP Reassociation Support | The EPP Reassociation Support field is set to 1 when dot11EPPReassociation Activated is true and set to 0 otherwise.
Add “EPP Reassociation Support” bit to Extended RSN Capabilities field.
Table 9-373—Extended RSN Capabilities field (continued)

## Slide 10
12.16.6.1 Non-MLO procedure
A non-AP STA can change its MAC address, reset SN and PN and be allocated a new AID by reassociating to the same EPP AP using EPP Reassociation. If dot11EPPReassociationActivated is true, an EPP AP sets the EPP Reassociation Support field in the RSNXE to 1 to indicate support for EPP Reassociation. The non-AP STA is reassociating using EPP Reassociation if the Reassociation Request frame is encrypted, the EPP Reassociation Support field in the RSNXE is set to 1, the Current AP Address is the same as the new AP’s address (reassociating to the same AP), and the DS MAC Address element is present.
----------
On a successful EPP Reassociation, the EPP AP and non-AP STA shall reset the SN and PN and the EPP AP shall allocate a new AID to the non-AP STA but shall not change any pre-existing states or agreements.
12.16.6.2 MLO procedure
A non-AP MLD can change its MAC address, reset SN and PN and be allocated a new AID by reassociate to the same EPP AP MLD using EPP Reassociation. If EPPReassociationActivated is true, an EPP AP MLD sets the EPP Reassociation Support field in the RSNXE to 1 to indicate support for EPP Reassociation. The non-AP STA MLD is reassociating using EPP Reassociation if the Reassociation Request frame is encrypted, the EPP Reassociation Support field in the RSNXE is set to 1, the Current AP Address is the same as the new AP’s address (reassociating to the same AP MLD), and the DS MAC Address element is present.
----------
On a successful EPP Reassociation, the EPP AP MLD and non-AP MLD shall reset the SN and PN and the EPP AP MLD shall allocate a new AID to the non-AP MLD but shall not change any pre-existing states or agreements.

## Slide 11: Text
Proposed text is in 25/1733r0