## Slide 1: Equivalence of JSVD, SSVD and SLQD (A Unified Interference Alignment Framework in CoBF)
Date: 2025-Oct
Authors:
Name | Affiliation | Address | email
Aiguo Yan | Samsung | 3655 N First St, San Jose, CA 95134 | aiguo.yan@samsung.com
Zigui Yang |  |  | 
Dongwoon Bai |  |  | 
Jung-Hyun Bae |  |  | 
Minki Ahn |  | Republic of Korea | 
Eunsung Jeon |  |  | 
Myeongjin Kim |  |  | 

## Slide 2: Background
We presented “Interference Alignment techniques for CoBF” (11/25-1513 and 11/25-1514) in 802.11 Sept meeting
This contribution will further elucidate both similarities and differences among 3 different methods (i.e., Joint-SVD, Separated-SVD, and Separated-LQD).
It is beneficial to understand the pros and cons of each technique theoretically, on top of numerical simulation results.

## Slide 3: A CoBF Configuration Example
Intuitions:
Existing schemes (Joint or sequential SVD) treat both inBSS and xBSS channels SAME way.
We propose to treat xBSS channels Differently so that the SVD is always performed for inBSS channels.
Rationales: There is NO xBSS data during the normal CoBF data transmission phase.
We use Virtual Antenna technique to achieve dimension reduction for Partial Nulling

## Slide 4: Problem Formulation
For simplicity, we assume 2 APs in a CoBF configuration have same # of TX antennas.
When # of total RX antennas (of all STAs) is larger than # of TX antennas/AP, we proposed to derive Virtual Antennas of Reduced Dimensions with Pre-Processing.
From mathematical point of view, JSVD/SSVD/SLQD are different Pre-Processing methods.
The key question now is which method has the best overall merits (performance, complexity, flexibility and so on), both theoretically and numerically.

## Slide 5: Joint-SVD: A Default Method in 11bn
(1): Used in Partial Nulling
(0): Not used

## Slide 6: Separated-SVD (SSVD)

## Slide 7: Separated-LQD (SLQD)
V11 is from SVD of H11
V12 is from LQD
Lower Triangular

## Slide 8: Summary of Dimension Reduction
3 methods for dimension reduction/decomposition/alignment:
For a inBSS channel, diagonal matrix is required.
For a xBSS channel, diagonal matrix is NOT required.
The Lower Triangular Matrix enables that only needs to be computed ONCE, and submatrix is always from this .
Not Unitary

## Slide 9: Discussions (1/2)
The goal of this page is to stimulate discussions among the 802.11 community. We understand that not everyone would agree with the assessment below.
JSVD seems introducing extra dependence on xBSS channels for inBSS performance. Feedback can’t be reused for SU/MU-MIMO
SSVD has better performance than JSVD (11/24-1789), but limitation on flexibility. Good for Re-use.
SLQD has full flexibility as JSVD, and has lowest complexity potentially (LQD/QRD vs SVD). The inBSS performance has no dependence on xBSS channels, and is better than with JSVD. Good for Re-use.

## Slide 10: Discussions (2/2)
JSVD also has additional potential concerns:
With SLQD , each submatrix is guaranteed to be unitary, and hence of full rank
Need all sub-matrices having full ranks, at least, for the pseudo-inverse

## Slide 11: JSVD vs SLQD
A close comparison of JSVD vs SLQD
Both JSVD and SLQD have very similar (or same) shape/form.
Existing feedback mechanism for CoBF JSVD can be reused for SLQD
The precoder design in the BFer can be same with JSVD or SLQD.
The receiver design in the BFee can be same with JSVD or SLQD.
JSVD enables both full and partial nullings, so does SLQD.

## Slide 12: Conclusion & Future works
JSVD, SSVD and SLQD are equivalent interference-alignment methods.
SSVD/SLQD ensure regular SVD is performed with inBSS channels. This enables reuse of CoBF sounding results for SU/MU.
It is beneficial to have more comprehensive simulation to quantify all benefits of SSVD/SLQD
We propose to have EXPLICIT signaling between Bfer and Bfee on JSVD, SSVD or SLQD, as well as individual/independent SVD which is the default method in sequential sounding.

## Slide 13: References
25/1513: Interference-Alignment-in-CoBF-with-Sequential-Sounding ; (Aiguo of Samsung)
25/1514: Interference-Alignment-in-CoBF-with-Joint-Sounding; (Aiguo of Samsung)
25/1041: Options-in-reuse-of-cobf-sounding-results; (Aiguo of Samsung)
24/1836: On CoBF Capabilities; (Aiguo of Samsung)
24/1789: CoBF-partial-nulling-feedback-types; (Rani of Huawei)
24/1542: Sounding schemes for coordinated beamforming; (Sameer of QCOM)
24/1433: Enhancing BF Feedback mechanism in 11bn; (Aiguo of Samsung)
24/1432: Unified CoBF and MUMIMO Schemes with Zero MUI; (Aiguo of Samsung)
23/1998: Zero-MUI Coordinated Beamforming; (Shimi of Huawei)
23/1514: Channel Information Feedback for Smooth Beamforming - Follow Up; (Eunsung of Samsung)
22/2022: Channel Information Feedback for Smooth Beamforming; (Eunsung of Samsung)
22/1896: TXBF based on the Optimal SVD; (Aiguo of Zeku)
22/1820: BF Feedback with the Optimal SVD; (Aiguo of Zeku)
22/1413: Thoughts-on-High-Reliability-Communications; (Aiguo of Zeku)
IEEE paper: “Interference Alignment and Degrees of Freedom of the K-User Interference Channel” (Viveck R. Cadambe and Syed Ali Jafar, 2008)