## Slide 1: Further Considerations on Interference Mitigation Pilots
Name | Affiliation | Address | Phone | email
Ke Zhong | Ruijie Networks Co., Ltd. |  |  | zhongke@ruijie.com.cn
Fachang Guo |  |  |  | 
Date: 2025-10-09
Authors:

## Slide 2: Abstract
Introduction
Further Considerations on Interference Mitigation Pilots
Conclusion

## Slide 3: Introduction
In PAR of IEEE P802.11bn, the Ultra High Reliability (UHR) capability is defined to offer improved rate-vs-range performance, lower latency, and reduced power consumption for AP and STA, compared to Extremely High Throughput (EHT) MAC/PHY operation [1].
IM in the current Draft 1.0 version:
A UHR STA may transmit a UHR PPDU with IM enabled if all of the following conditions are met:
— The UHR PPDU is a SU transmission using the UHR MU PPDU.
— The Punctured Channel Information field in the U-SIG field is set to 0 (no puncturing).
— The UL/DL field in the U-SIG field is set to 1, or the UL/DL field in the U-SIG is set to 0 and the data field uses only one spatial stream.
— The Data field does not use UHR-MCS 15.
Interference is one of the most detrimental factors limiting the performance of WLAN systems. To achieve the goal of UHR, the motion for interference mitigation was passed in the September 2024 Interim meeting [2]:
Define a mode with additional pilots, located within the data portion of the PPDU, which are used for interference estimation and mitigation.
  Note: zero-energy pilots alternative to be considered as well
[Motion #35, [1] and [87]]
The Draft 1.0 specifies the criteria under which a UHR STA is permitted to transmit a UHR PPDU with IM enabled [2]:

## Slide 4: Further Considerations on Interference Mitigation Pilots
Potential extension 1:
The current Draft 1.0 only specifies the number of spatial streams used in the DL: the UL/DL field in the U-SIG is set to 0 and the data field uses only one spatial stream.
Potential extension: extend to specify the number of spatial streams used in the UL, i.e., when the UL/DL field in the U-SIG is set to 1. For example, update the current Draft 1.0 if up to two spatial streams can be used in the UL:
  The UL/DL field in the U-SIG field is set to 1 and the data field uses up to two spatial streams, or
  The UL/DL field in the U-SIG field is set to 1 and the maximum number of spatial streams allowed in data field is two.
Potential extension 2:
The current Draft 1.0 only specifies IM in UHR MU PPDU: the UHR PPDU is a SU transmission using the UHR MU PPDU.
Potential extension: extend to include trigger-based IM, i.e., IM in UHR TB PPDU should also be specified.
  It is necessary to define the triggering mechanism and the IM scheme for UHR TB PPDU.
AP
STA
Trigger
UHR TB PPDU with IM enabled

## Slide 5: Conclusion
This contribution proposes two potential extensions to Draft 1.0 regarding the further development of IM.
  Potential extension 1: extend to specify the number of spatial streams used in the UL.
  Potential extension 2: extend to include trigger-based IM.

## Slide 6
Do you agree to include the following into the 11bn SFD for IM?
  The UL/DL field in the U-SIG field is set to 1 and the data field uses up to two spatial streams, or the UL/DL field in the U-SIG is set to 0 and the data field uses only one spatial stream.
    Yes:
    No:
    Abstain:
Straw Poll 1

## Slide 7
Do you agree to include the following into the 11bn SFD for IM?
  Specify related triggering mechanism and the IM scheme for UHR TB PPDU.
    Yes:
    No:
    Abstain:
Straw Poll 2

## Slide 8: References
[1] IEEE 802.11-23/0480r3, UHR proposed PAR, Laurent Cariou (Intel)
[2] IEEE P802.11bnTM/D1.0