## Slide 1: Discussion on Co-BF Sounding Invite frame and Co-BF Sounding Response frame
Name | Affiliation | Address | Phone | email
Ke Zhong | Ruijie Networks Co., Ltd. |  |  | zhongke@ruijie.com.cn
Fachang Guo |  |  |  | 
Date: 2025-10-09
Authors:

## Slide 2: Abstract
Introduction
Discussion on Co-BF Sounding Invite frame and Co-BF Sounding Response frame
Conclusion

## Slide 3: Introduction
In PAR of IEEE P802.11bn, the Ultra High Reliability (UHR) capability is defined to offer improved rate-vs-range performance, lower latency, and reduced power consumption for AP and STA, compared to Extremely High Throughput (EHT) MAC/PHY operation [1].
— The responding AP may indicate it accepts or declines to participate in the cross-BSS UHR Co-BF sounding or Co-BF joint NDP sequence in the Co-BF Sounding Response frame. The information of the minimum sounding NSS capability of the participating non-AP STAs are exchanged by the Co-BF Sounding Invite frame and the Co-BF Sounding Response frame.
— In a Co-BF Sounding Invite frame, the Duration/ID field is set to the estimated time, in microseconds, required to transmit at least the UHR NDP Announcement frame sent by the Co-BF sounding initiator, plus one Co-BF Sounding Response frame, plus one NDP, plus applicable IFSs and any necessary ICF/ICR for STA(s).
— In a Co-BF Sounding Response frame that is sent as a response to the Co-BF Sounding Invite frame, the Duration/ID field is set to the estimated time, in microseconds, required to transmit at least the UHR NDP Announcement frame sent by the Co-BF sounding initiator, plus one NDP, plus applicable IFSs and any necessary ICF/ICR for STA(s).
A UHR Co-BF beamformer that initiates a UHR Co-BF sounding sequence, using a Co-BF Sounding Invite frame is the initiating AP. A UHR Co-BF beamformer that responds to the Co-BF Sounding Invite frame from the initiating AP is the responding AP. Before the cross-BSS UHR Co-BF sounding sequence or Co-BF joint NDP sounding sequence, a Co-BF Sounding Invite frame and a Co-BF Sounding Response frame shall be exchanged between the initiating AP and responding AP [2].
Per Draft 1.0, a Co-BF Sounding Invite frame and a Co-BF Sounding Response frame shall contain the following information [2]:

## Slide 4: Current information in Co-BF Sounding Invite frame and Co-BF Sounding Response frame – Recap [3]
Further information to be exchanged is TBD
— An AP shall use the BSRP NTB Trigger frame variant for the Sounding Invite frame
  The Sounding Response frame shall be M-BA
  TBD whether there’s another frame variant allowed for the Sounding Invite/Response frame
[Motion #447, [264] and [396, 397]]
— Any Co-BF sounding sequence that includes Cross-BSS CSI collection shall be initiated by a two-way handshake between the two APs participating in the sequence
  The two-way handshake exchange consists of a Sounding Invite frame and a Sounding Response frame.
  The Sounding Invite/Response frame exchange is used to:
    Confirm the availability of both APs for CSI collection.
    TBD for indication whether each AP will include ICF/ICR exchanges with its client or not.
    Further information to be exchanged is TBD.
[Motion #450, [264] and [396, 397, 400, 401]]

## Slide 5: Current information in Co-BF Sounding Invite frame and Co-BF Sounding Response frame – Recap [3]
— There shall be a frame-exchange before the Co-BF sounding between the two APs which will at-least serve the following goals:
  Unavailability/decline indication from the responding AP
    Used by responding AP to refuse participation in a COBF sounding process
  Exchange of sounding Nss capability of the STAs being sounded in the two BSSs
    The minimum sounding Nss capability of the participating STAs in each BSS will be exchanged
  Note: Design of the frames is TBD by MAC group
[Motion #306, [264] and [321]]
— A Shared (Responding) AP may reject a Co-BF/Co-SR transmission or Co-BF sounding invitation received from a Sharing (Initiating) AP.
  In case of rejection, the Shared (Responding) AP can include the reason for rejection in the Co-BF/Co-SR Response or Co-BF Sounding Response frame.
  Reasons for rejecting a Co-BF/Co-SR transmission or Co-BF sounding invitation are TBD.
[Motion #480, [264] and [413]]
— The Co-BF Sounding Invite frame carries the following information:
  Bandwidth
  Punctured Channel Information
[Motion #519, [264] and [420-422]]

## Slide 6: Discussion on Co-BF Sounding Invite frame and Co-BF Sounding Response frame
Proposed potential further information to be exchanged in Co-BF Sounding Invite frame:
Potential further information | Number of needed bits | Potential values
GI+LTF Size | 1 bit | 2 EHT-LTF+0.8µs GI or 2 EHT-LTF+1.6µs GI.
Number of UHR-LTF Symbols | 1 bit | 4 or 8.
Maximum Total NSS Allowed for shared AP | 1 bit | 1 or 2.
Number of Co-BF Users in sharing BSS | 2 bits | 1, 2 or 3.
STA ID | 11 bits | Set to a value of the TXVECTOR parameter STA-ID.
NSS | 1 bit | NSS indicates the number of spatial streams supported for each user within a sharing BSS, which can be 1 or 2.
Note: It is proposed that at least one of the above items of information be exchanged in the Co-BF Sounding Invite frame.

## Slide 7: Discussion on Co-BF Sounding Invite frame and Co-BF Sounding Response frame
Proposed potential further information to be exchanged in Co-BF Sounding Response frame:
Potential further information | Number of needed bits | Potential values
Extra LTF Allowed | 1 bit | 4 or 8.
Number of Co-BF Users in shared BSS | 2 bits | 1, 2 or 3.
STA ID | 11 bits | Set to a value of the TXVECTOR parameter STA-ID.
NSS | 1 bit | NSS indicates the number of spatial streams supported for each user within a shared BSS, which can be 1 or 2.
Note: It is proposed that at least one of the above items of information be exchanged in the Co-BF Sounding Response frame.

## Slide 8: Conclusion
This contribution proposes potential further information to be exchanged in Co-BF Sounding Invite frame and Co-BF Sounding Response frame.
Proposed potential further information to be exchanged in Co-BF Sounding Invite frame (at least one is required):
Potential further information | Number of needed bits | Potential values
GI+LTF Size | 1 bit | 2 EHT-LTF+0.8µs GI or 2 EHT-LTF+1.6µs GI.
Number of UHR-LTF Symbols | 1 bit | 4 or 8.
Maximum Total NSS Allowed for shared AP | 1 bit | 1 or 2.
Number of Co-BF Users in sharing BSS | 2 bits | 1, 2 or 3.
STA ID | 11 bits | Set to a value of the TXVECTOR parameter STA-ID.
NSS | 1 bit | NSS indicates the number of spatial streams supported for each user within a sharing BSS, which can be 1 or 2.
Proposed potential further information to be exchanged in Co-BF Sounding Response frame (at least one is required):
Potential further information | Number of needed bits | Potential values
Extra LTF Allowed | 1 bit | 4 or 8.
Number of Co-BF Users in shared BSS | 2 bits | 1, 2 or 3.
STA ID | 11 bits | Set to a value of the TXVECTOR parameter STA-ID.
NSS | 1 bit | NSS indicates the number of spatial streams supported for each user within a shared BSS, which can be 1 or 2.

## Slide 9
Do you agree to include at least one of the following into the 11bn SFD for further information to be exchanged in Co-BF Sounding Invite frame?
  GI+LTF Size
  Number of UHR-LTF Symbols
  Maximum Total NSS Allowed for shared AP
  Number of Co-BF Users in sharing BSS
  STA ID
  NSS
    Yes:
    No:
    Abstain:
Straw Poll 1

## Slide 10
Do you agree to include at least one of the following into the 11bn SFD for further information to be exchanged in Co-BF Sounding Response frame?
  Extra LTF Allowed
  Number of Co-BF Users in shared BSS
  STA ID
  NSS
    Yes:
    No:
    Abstain:
Straw Poll 2

## Slide 11: References
[1] IEEE 802.11-23/0480r3, UHR proposed PAR, Laurent Cariou (Intel)
[2] IEEE P802.11bnTM/D1.0
[3] IEEE 802.11-24/0209r19, Specification framework for TGbn, Ross Jian Yu (Huawei)