## Slide 1: Direct UL versus Buffer State Reporting
Date: 2025-10-14
Authors:

## Slide 2: Use Case
n unknown AMP STAs need to be queried by one AMP AP.
AMP AP transmits AMP TFs, announcing a random access period with random access slots.
  The AMP AP knows the required duration for the STA’s data. Each random access slot has the correct duration to transmit the data + ACK (Direct-RA UL)
  The AMP AP expects (short) “AMP Buffer Status Reports (BSRs)” in the random access slots, containing a short id. Then, it will poll the AMP STA’s data in a dedicated TXOP (2-step UL)
An AMP STA, after the reception of the AMP TF, randomly selects a slot and transmits
  its data
  ”AMP BSR”, waits for the UL-Poll, transmits its data.
Assume fRA(n) RA slots are required to collect all n AMP STA’s data.
  Number of required RA slots is the same in (a) or (b)!
KPI: Duration to receive data from all AMP STAs

## Slide 3: Assumptions (see also IEEE 802.11-25/1572)
UL PHY Overhead 64µs
DL PHY Overhead 92µs
PSDU Speed 250kb/s
MPDU Header 5B
Direct UL Poll TF payload: 2B
Random Access TF payload: 8B
ACK payload: 0B
”AMP-BSR” payload: 2B
CTS-to-self duration 44µs
Inter Frame Space 16µs
TXOP Duration 2.5ms, sufficient for
  6 AMP-BSR RA slots for 2-step UL
  3 Direct-RA UL slots (4B data)
  2 Direct-RA UL slots (8B data)
  1 Direct-RA UL slots (16B data)

## Slide 4: 1 AMP STA, Data 16B, fRA(1) = 1
Direct-RA UL
CTS-to-self
IFS
AMP-TF for RA (1 TXOP / 1 slot)
RA-Slot for data + IFS + ack
1.588ms
2-step UL
CTS-to-self
IFS
AMP-TF for RA (1 TXOP / 6 slots)
RA-Slot for AMP-BSR
CTS-to-self
IFS
AMP-TF for UL Data
IFS
Data + IFS + ack
3.788ms

## Slide 5: 1 AMP STA, Data 16B
fRA(n) = 1, so one slot required: Same as on previous slide
2 slots required:
  Duration increases for Direct-RA (two TXOPs)
  Same duration for 2-step RA (one TXOP holds 6 RA slots)
Threshold = 3

## Slide 6: 10 AMP STAs, Data 16B
fRA(n) < 14:
  Direct-RA takes less time
fRA(n) ≥ 14:
  2-step RA takes less time
Threshold: 14

## Slide 7: 100 AMP STAs, Data 16B
fRA(n) < 119:
  Direct-RA takes less time
fRA(n) ≥ 119:
  2-step RA takes less time
Threshold: 119

## Slide 8: Data 16B
fRA(n) < 1.17×n + 2.06:
  Direct-RA takes less time
fRA(n) ≥ 1.17×n + 2.06:
  2-step RA takes less time

## Slide 9: Results
Gradient essentially depends on number of Data-RA slots per TXOP:
  4B data allows 3 Data-RA slots per TXOP
  8B data allows 2 Data-RA slots per TXOP
For 16B data and more:
  If a bit more than 1 RA-slot per AMP STA is needed, 2-step RA has a lower duration

## Slide 10: fRA(n)
This analysis is independent on fRA(n)
The AMP AP’s & AMP STA’s implementation determines the real-world fRA(n)
Example (see IEEE 802.11-25/yyyy for details):
  25 AMP STAs
  5 different simple slot allocation algorithms by the AP
    Constant number of slots, all awake AMP STAs contend
    AMP AP adapts the number of slots based on the last RA period
  E[fRA(25)] between 105 and 170

## Slide 11: Summary
Evaluated the performance of
  Direct-RA UL:
    AMP AP offers RA slots
    AMP STA selects one slot randomly & transmits data
  vs
  2-step UL:
    AMP AP offers RA slots
    AMP STA selects one slot randomly to transmit short BSR
    AMP AP polls the AMP STA directly
Under the assumptions (slide 3), in essentially all cases 2-step UL is faster
Contact me to get the Matlab script