## Slide 1: Comparing Designs for Uplink Random Access
Date: 2025-10-14
Authors:

## Slide 2: Abstract
During the September 2025 TGbp meetings two approaches for slotted Uplink Random Access were presented & discussed:
  IEEE 802.11-25/1546, “AMP Channel Access – follow up”
  IEEE 802.11-25/1573, “AMP System Performance Evaluation: First Results”
Here, we compare both approaches.

## Slide 3: Assumptions (see also IEEE 802.11-25/1572)
UL PHY Overhead 64µs
DL PHY Overhead 92µs
PSDU Speed 250kb/s
MPDU Header 5B
Direct UL Poll TF payload: 2B
Random Access TF payload: 8B
ACK payload: 0B
”AMP-BSR” payload: 2B
CTS-to-self duration 44µs
Inter Frame Space 16µs
TXOP Duration 2.5ms
Non-AP STA Power consumption (decreased by 10 compared to 1572)
  0.1 mW while transmitting an AMP PPDU
  0.01 mW while receiving AMP PPDU
  0 mW while listening
  0 mW while sleeping & harvesting power

## Slide 4: Frame Exchange Sequences (same as in IEEE 802.11-25/1572)
Triggered Random Access
  (may be split into multiple TXOPs depending on the number of RA slots)
Uplink Data Transmission
AMP AP
AMP STA1
AMP STA2
t
AMP TF (RA)
RA Slot 1
RA Slot 2
RA Slot 3
AMP-BSR
AMP-BSR
receive
receive
listen
listen
LBT
CTS-to-self
AMP AP
AMP STA1
AMP STA2
t
CTS-to-self
UL Slot for STA 1
AMP TF (Poll 1)
AMP-ACK
listen
listen
AMP-Data
receive
receive
receive
LBT
t

## Slide 5: Approach 1: Contention-Window (CW) based,
Inspired by UORA (Uplink OFDMA-based Random Access), introduced by HE (TGax)
A non-AP AMP STA maintains an AMP Contention Window (ACW) and an AMP Backoff Counter (ABO)
  ACW initialized to ACWmin
  ABO initialized to a random value [0, ACW]
AMP AP signals random access slots in a Trigger Frame
  STA counts down ABO by the number of slots
  When reaching zero, the STA transmits
Uplink transmission failed:
  ACW = 2×ACW + 1 (limited by ACWmax)
  Re-try

## Slide 6: Approach 2: AP-driven
Inspired by EPC RFID Gen2 UHF inventory operation
AMP AP signals start of a random access (RA) session
  Consisting of one or more Trigger Frames (TFs)
  Each TF announces a number of RA slots (limited by the TXOP duration)
  The first TF signals the RA session start
A non-AP AMP STA receives the first TF of a RA session
  STA initializes an AMP Backoff Counter (ABO) randomly to [0, number of RA slots]
For every received TF of a RA session (including the first)
  STA counts down the ABO by the number of RA slots
  When reaching zero, the STA transmits
Uplink transmission failed: Re-try in the next session

## Slide 7: AMP AP (same as IEEE 802.11-25/1572)
Transmit power 1 W
Center frequency 2.412 GHz
Initiates triggered random access period with n slots every 102.4 ms
If it receives “AMP-BSRs”, it will poll the AMP non-AP STAs
AMP TF (RA)
RA Slot 1
RA Slot 2
RA Slot 3
LBT
CTS-to-self
Triggered RA
102.4ms
Triggered RA
AMP AP

## Slide 8: AMP non-AP STA (same as in IEEE 802.11-25/1572 with new power consumption values)
At t=0, one AMP STA appears randomly within 1m circle around AMP AP
  Initial energy 0 J
  RF energy harvesting on 2.4 GHz, free-space pathloss
  Only the AP emits energy, no other sources / wireless power transfer
  Harvest threshold -35 dBm
  Harvest loss 10 dB
  Power consumption
    0.1 mW while transmitting an AMP PPDU
    0.01 mW while receiving AMP PPDU
    0 mW while listening
    0 mW while sleeping & harvesting power
Harvests until it has 2.5 ms×0.1 mW energy
  Then, wakes-up and listens for random access period
    Transmits its AMP-BSR in one of the random access slots to indicate its presence
  Listens for uplink poll
    Transmits its data
    Receives acknowledgement
1m
AMP AP
AMP non-AP STA
Rx
Tx
Listen
Sleep

## Slide 9: Simulation
CW-based
  ACWmin = 7, ACWmax = 31 (as default in UORA)
  AP announces [6, 12, 18, 24] RA slots every 102.4ms using [1, 2, 3, 4] TFs
AP-driven
  AP announces [6, 12, 18, 24] RA slots every 102.4ms using [1, 2, 3, 4] TFs
KPI: Duration between
  t=0 (STA enters the AP’s coverage area) and
  Reception of the UL data

## Slide 10: Results for 10 STAs (dotted: CW-based, solid: AP-driven)
Essentially no collisions
  BSRs are always received
Duration only depends on the charging speed: more TFs, higher speed
6 RA slots: identical results
12 or more RA slots:
  CW-based slightly better as ACWmin = 7.

## Slide 11: Results for 25 STAs (dotted: CW-based, solid: AP-driven)
Again, very few collions
Duration again depends on charging speed
  Slightly better than for 10 STAs due to more frame exchanges corresponding to more energy
Very similar results for CW-based and AP-driven
CW-driven is slightly better for 18 / 24 RA slots
  ACW is usually 7, so smaller than 18 or even 24.

## Slide 12: Results for 50 STAs (dotted: CW-based, solid: AP-driven)
Duration depends on charging speed & collisions
6 RA slots is not sufficient
  CW-based: long waiting times due to increased ACW
  AP-driven: too many collisions
More than 12 slots sufficient to reduce the collisions
  Very similar results for CW-based and AP-driven approach

## Slide 13: Results for 100 STAs (dotted: CW-based, solid: AP-driven)
Chaos for 6 RA slots
  Many collisions and / or high ACWs
More than 6 RA slots show similar results for CW-based and AP-driven

## Slide 14: Results for 250 STAs (dotted: CW-based, solid: AP-driven)
System is overloaded, very long durations
  CW-based results in high ACW
  AP-driven results in many collisions

## Slide 15: Adaptive number of RA slots
No static configuration is optimal
  Few slots: low resource (channel time) consumption, but many collisions
  Many slots: High resource consumption, collisions are mitigated
AP may adapt the number of slots per RA session
  This is completely implementation specific, no need to specify this in the standard
  Similar to the “Example slot-count selection algorithm” in the (informative) Annex D of the EPC RFID Gen2 UHF
Example algorithm
  Determine occupancy = (number of received AMP-preambles) / (total number of slots)
  Occupancy > 0.5: Double the number of RA slots, up to maximum
  Occupancy < 0.25 Halve the number of RA slots, down to minimum

## Slide 16: Results for Adaptive number of RA Slots (dotted: CW-based, solid: AP-driven)
Minimum 6 RA slots, maximum 48 RA slots
Results are better than all results with static number of RA slots
CW-based & 250 STAs have reduced performance as ACWmax = 31, so 16 slots are barely used

## Slide 17: Summary
Compared two approaches for the AMP Uplink Random Access Phase:
  CW-based: non-AP STAs maintain a contention window similar to UORA, the AMP AP provides the RA slots
  AP-driven: the AMP AP announces the ACW together with the matching number of slots, the non-AP STAs follow the AMP AP’s instructions
Results are very similar
  For static number of slots per random access session the CW-based flexibility brings a gain
  If the AMP AP adapts the number of slots per random access session, AP-driven’s disadvantage is removed
AP-driven approach allows for implementation-specific optimizations, keeping the AMP non-AP STAs as simple as possible