## Slide 1: DUO non-AP STA as the TXOP holder
Date: 2025-08-25
Authors:

## Slide 2: Introduction
A DUO non-AP STA is allowed to send unsolicited ICF to report its incoming unavailability event, as shown in P802.11bn D1.0.
  A DUO non-AP STA that is operating in DUO mode and that is a TXOP holder may indicate in a BSRP NTB Trigger frame addressed to the DUO assisting AP whether it will be unavailable after a specific point in time, and, if known, for how long, by including a Feedback User Info field (see 9.3.1.22.7 (Feedback User Info field)) that has a Feedback Type field set to 0 and that contains both an Unavailability Target Start Time field and an Unavailability Duration field (see 9.3.1.22 (Trigger frame format)).

## Slide 3: Introduction
The behaviors of the STAs after the DUO report are undefined.
If the DUO non-AP STA doesn't terminate the TXOP early, no in-BSS STAs can access the channel until the end of TXOP
  All the STAs within the BSS have intra-BSS NAV set to the end of the TXOP

## Slide 4: Introduction
If the DUO STA terminates the TXOP early by sending a CF-End frame, it loses the TXOP and needs to compete for the channel access again
  Introduce more delay, may degrade the performance of low-latency services
  It may be infeasible for the DUO STA to send the CF-End frame before the unavailability period

## Slide 5: Proposal DUO Operation Indication
The Remaining TXOP Allocation may be indicated by TXOP Allocation field in the BSRP NTB Trigger frame
TXOP Allocation = 0, the DUO STA releases the remaining TXOP once the unavailability period starts
TXOP Allocation = 1, the DUO STA wants to continue the TXOP after the unavailability period finishes
 | B0 B9 | B10 B19 | B20 | B21 B23
 | Unavailability Target Start Time | Unavailability Duration | TXOP Allocation | Reserved
Bits: | 10 | 10 | 1 | 3

## Slide 6: Proposal DUO Operations
The DUO non-AP STA may release the TXOP after the start of the unavailability period
  The AP may become the TXOP holder until the end of the TXOP
  or the AP may terminate the TXOP by transmitting a CF-End frame

## Slide 7: Proposal DUO Operations
The DUO non-AP STA may restore as the TXOP holder after the end of the unavailability period
  The AP becomes the TXOP holder until the end of the TXOP
  The AP allocates the remaining TXOP to the DUO non-AP STA at the end of the unavailability period

## Slide 8: Summary
A DUO non-AP STA that is a TXOP holder is allowed to send unsolicited ICF to report its incoming unavailability event
The behaviors of the STAs after the DUO report are undefined in Draft 1.0.
Terminating the TXOP early introduces more delay, which degrades the performance of low latency services
The DUO STA should indicate the behaviors of the BSS after the start of the unavailability period

## Slide 9: SPs
SP 1
  Do you support to indicate the BSS behaviors in the DUO ICF?
SP 2
  Do you support that the AP becomes the TXOP holder of 1) the remaining TXOP if the DUO STA releases the TXOP or 2) the unavailability period if the DUO STA doesn't release the TXOP?
SP 3
  Do you support the DUO STA may restore as the TXOP holder after the unavailability period?

## Slide 10: References
[1] IEEE P802.11bn/D1.0