## Slide 1: 3 Responses to Interpretations for July 2008
Date: 2008-07-18
Authors:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Interpretation Request #1
Introduction:
Service Providers use Multi-SSID many ways:
  extra SSID for particular use-case, device-class, WEP...
  very important for non-enterprise (hotspots, homes...)
But…There are interop issues
  Beacon timing
    Some devices cannot cope with a variable or very-short beacon interval
      no problems if 50mSec apart, BUT t=SIF gives problems with some devices !
    Needs defining for multi-SSIDs
      All clients need to cope with such timing
      Spacing beacons by just SIFS/DIFS
Question:
If an AP device is generating multiple BSSID signals what is the proper spacing between those SSIDs?

## Slide 3: Interpretation Request Response #1
The IEEE 802.11-2007 only defines one MAC/PHY pair as a STA. When a product virtualizes multiple STAs within the same physical device, the interaction of the virtual STAs are currently outside the scope of the standard, however the use of multiple BSSID/SSID functionality is currently being defined.
The commenter (and others interested) are invited to come and participate with the 802.11 WG.

## Slide 4: Interpretation Request #2
Section 7.3.1.17 of [1] says that the Max SP Length subfield of the QoS Info field is reserved when all four U-APSD flags are set to 0. Section 7.1.1 of [1] says that reserved fields and subfields are set to 0 upon transmission and are ignored upon reception.
If a non-AP STA sets all four U-APSD flags to 0 in the QoS Info field in the QoS Capability IE in the Association Request, and then uses an ADDTS Request to set up a delivered-enabled TS (and also sets up a trigger-enabled TS -- perhaps the same TS), how many buffered MSDUs and MMPDUs may the AP deliver to this non-AP STA during an SP triggered by this non-AP STA?

## Slide 5: Interpretation Response #2
The standard does not specify, when the bits are set to 0, a maximum limit to how many MSDU or MMPDUs are buffered by an AP. Therefore the maximum number would be AP implementation dependent value and would be dependent on the amount of traffic buffered at the AP (See table 7-25 bit 5-6). When Bit 5 and 6 are not set to 0, then a limit is prescribed.

## Slide 6: Interpretation Request #3
An interpretation is requested on the following:
Section 7.3.2.20 of [1] says that the Minimum PHY Rate field of the TSPEC IE is “the desired minimum PHY rate to use for this TS, in bits per second, that is required for transport of the MSDUs belonging to the TS in this TSPEC.”
What are the exact semantics of this field?
Does this need to correspond to an operational rate of the AP which the non-AP STA can transmit at, for a TS with an uplink component (vice-versa for a TS with a downlink component)? [*]
If not, must it be a rate supported by the PHY being used (though perhaps not a rate supported by the non-AP STA and/or AP)?
If not, must it be less than or equal to the highest rate supported by the PHY being used? Or the highest rate supported by the non-AP STA and AP?
And if the answer to question marked with [*] is no, then how is K.2.2 to be used?

## Slide 7: Interpretation Request #3-- Example
An example may help. Say we're using 802.11a, the AP supports 6, 12, 24 and 48 Mbps, and the STA supports 6, 9, 12 and 24 Mbps (here "supports" means both tx and rx). Which of the following values would be valid values in the Minimum PHY Rate field for an uplink TSPEC, and for those values, what value would be used for to compute the MPDUExchangeTime in section K.2.2 of [1]?
24 000 000 (supported by both STAs)
9 000 000 (not supported by AP)
48 000 000 (not supported by non-AP STA)
18 000 000 (valid .a rate, but not supported by either STA)
36 000 000 (valid .a rate, but not supported by either STA and higher than non-AP STA's highest rate)
27 000 000 (valid .a rate, but only in "half-clocked" operation)
54 000 000 (highest rate on .a; not supported by either STA)
1 111 111 111 (not a valid rate for any PHY; higher than highest rate on any PHY)
111 111 111 (not a valid rate for any PHY; higher than highest rate on .a)
11 111 111 (not a valid rate for any PHY, but in .a rate range)
1 111 111 (not a valid rate for any PHY; lower than lowest rate on .a)
111 111 (not a valid rate for any PHY; lower than lowest rate on any PHY)
11 000 000 (not a valid .a rate, but valid .b rate and in .a rate range)
1 000 000 (not a valid .a rate and not in .a rate range, but valid .b rate)

## Slide 8: Response for Interpretation Request #3
In clause 7.3.2.30, the Minimum PHY Rate field definition:
  The Minimum PHY Rate field is 4 octets long and contains an unsigned integer that specifies the desired minimum PHY rate to use for this TS, in bits per second, that is required for transport of the MSDUs belonging to the TS in this TSPEC21.
    Footnote 21: This rate information is intended to ensure that the TSPEC parameter values resulting from an admission control negotiation are sufficient to provide the required throughput for the TS. In a typical implementation, a TS is admitted only if the defined traffic volume can be accommodated at the specified rate within an amount of WM occupancy time that the admissions control entity is willing to allocate to this TS.

## Slide 9: Response for Interpretation Request #3 (cont)
The standard does not require the use any of the Operational Rates for the value of the Minimum PHY Rate.
K2.2 is part of an Informative Annex, and is provided to assist implementers, but it does not specify required functionality.