IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Next PNC Identification |
| Date Submitted | 16 Jun 2005 |
| Source | Bill Shvodian 8133 Leesburg Pike Suite 700 Vienna, VA 22182 | Voice: +1-703-269-3047 Fax: E-mail: bill dot shvodian at freescale dot com |
| Re: | LB 29 – TG3b draft |
| Abstract | This document describes a mechanism to enable smooth transition to a new PNC for the situation where the PNC turns off or moves out of range without performing a PNC handover. |
| Purpose | This document is provided in support of 802.15.3b activities in order to alleviate an identified deficiency in the 802.15.3 protocol. |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

Motivation

802.15.3 provides a mechanism for the PNC to perform handover of the PNC functionality.  The PNC is supposed to perform handover when a more capable DEV joins the piconet, or when it knows that it is going away.  Unfortunately, it is not always possible for the PNC to always know that it is going away.  The PNC may suddenly be turned off or lose power.  If mobile, the PNC could also move out of range of the other DEVs in the piconet.  When this happens the other DEVs are left unable to communicate because there is no more PNC.

In theory, one of the remaining DEVs could assume the role of PNC when it determines that the PNC is no longer active or in range, but there are drawbacks to this.  First, there is no standard way of saving the piconet.  A new piconet has to be formed.  Second, multiple DEVs in the piconet could simultaneously assume the role of PNC in the new piconet. Third, since it is a new piconet every DEV would have to join the new piconet and re-establish all communications.

Overview

The PNC always attempts to select another DEV in the piconet to become PNC if the PNC goes away without handing over.  If there is no other PNC capable DEV in the piconet, that is indicated.  If there is one other PNC capable DEV in the piconet, that DEVs is identified as the next PNC.  If there are multiple PNC capable DEVs the PNC chooses the best qualified DEV to be the next PNC and periodically advertises the next PNC via an IE in the Beacon.

In addition to the information in the PNC rating field, the PNC should also consider the information on which DEVs can hear which other DEVs in the piconet.  It is important that the new PNC is a DEV that as many as possible DEVs in the piconet can reliably communicate with.  In order to allow the PNC to determine which DEVs can hear other DEVs in the piconet, each DEV should listen to all MCTAs or the CAP and make note of which other DEVs in the piconet it can hear and how well.  A new command is introduced to provide this information to the PNC.  Since each DEV transmits a management frame to the PNC at least once per association timeout period (ATP), if the DEV has nothing else to send to the PNC it should send the new command with the information about all of the DEVs in the piconet.

Proposed Text

Add the following definitions to clause 3

Preliminary Handover - Transferring all info from the PNC to a next PNC.

Sending the Next PNC IE in the beacon

Implicit Handover - Next PNC takes over after defined scan and timeout

when the old PNC has disappeared.

Add 7.4.18 Next PNC IE

The Next PNC IE shall be formatted as illustrated in Figure xx.  The Next PNC field contains the DEVID of the DEV that the PNC has chosen to be the Next PNC.  The Next PNID field is the PNID that the next PNC shall use if it takes over as PNC as described in 8.2.3a.

| Octets: 2 | 1 | 1 | 1 |
| --- | --- | --- | --- |
| Next PNID | Next PNC | Length = 3 | Element ID |

Add to last paragraph of 7.5.3.1 PNC handover request

It shall be set to two in order to indicate “Handover Information Transfer, no handover.”

Add 7.4.19 Piconet channel status IE

The Piconet Channel Status Information Element shall be formatted as illustrated in Figure xx.  The Bitmap of DEVs in Range is a 256 bit bitmap of all of the DEVs in the piconet that can be heard by the DEV sending the command.  The bit corresponding to the DEVID is set to “1” if a frame was correctly received from a DEV with that DEVID since the last Piconet Channel Status IE was sent, otherwise the bit shall be set to “0.”    The Channels Status Details field shall be set to one if the DEV scanned for power save DEVs and set to zero otherwise.

| Octets: 1 | Octets: 32 | 2 | 2 |
| --- | --- | --- | --- |
| Channel Status Details | Bitmap of DEVs in Range | Length = 33 | Element ID |

Add to Table 48:

Element ID: 0x11

Element: Piconet Channel Subclause: 7.19

Present in Beacon: No

Add to Table 51

Information Element: Piconet channel status

Subclause: 7.4.19

PNC allowed to request: may request

DEV allowed to request: may request

Add to Table 52

Information Element: Piconet channel status

Subclause: 7.4.19

May Respond, May Respond, May Respond

Add to Table 53

Information Element: Piconet channel status

Subclause: 7.4.19

PNC Allowed to send? May send

DEV Allowed to send? May send

Add 8.2.3a Next PNC

Next PNC shall not be used for dependent piconets.

Although the PNC will normally attempt to perform a handover when it shuts down or leaves the piconet, this may not always be possible.  The PNC could be powered off in such a way that handover is not performed.  It could also move out of range of the rest of the DEVs in the piconet, or vice versa.  In order to avoid the interruption in communication that would occur when the PNC disappears without handover, the PNC may choose a DEV in the piconet to be the next PNC.

The PNC may periodically evaluate the PNC capabilities of the members of the piconet and other factors to decide which DEV should be the next PNC..  In addition to the PNC capabilities field, the PNC should use information provided by the DEVs in the Piconet Channel Status IE to determine which potential PNC could best be heard by the other DEVs in the piconet.  In this context of the piconet channel status IE, heard means correctly receiving a MAC header.

Always AWAKE DEVs, as described in 7.4.11, should continuously determine the DEVs they can hear.  Otherwise,  a DEV will only hear DEVs that have streams set up to communicate with them.  However, if the CAP is used in the piconet, each DEV should also keep track of DEVs that are heard in the CAP.  If MCTAs are used in the piconet, DEVs that are not extremely power sensitive should listen to all of the uplink MCTAs to determine the DEVs that it can hear.

DEVs are required to send a frame to the PNC at least once per ATP.  If the DEV has nothing else to send, it should send the Piconet Channel Status command.

The Next PNC IE, as described in 7.4.x,  should be inserted in the beacon at least once per the minimum ATP of the DEVs in the piconet.  The Next PNC IE should also be inserted in all of the appropriate wake beacons for power save DEVs.  If no DEVs in the piconet are PNC capable, the PNC shall set the DEVID in the Next PNC IE to zero whenever the Next PNC IE is sent.

If a DEV has been chosen as next PNC, the PNC shall periodically perform preliminary handover as defined in 8.2.3b

The PNC also selects the Next PNID for the Next PNC IE. The PNC shall select a Next PNID  such that it is different from any other PNID that has been detected as described in 8.10.3.

When the DEV identified as the next PNC fails to detect mMaxLostBeacons +1 consecutive beacons, it shall scan the channel for any frames.  The next PNC may start scanning whenever a single beacon is missed.  Since no frames can be transmitted in dynamic CTAs, the CAP or MCTAs if the beacon is not received, the next PNC shall use the presence of any frames from the current piconet as an indication that the beacon is still being transmitted but the next PNC has lost contact with the PNC.  In this case the next PNC shall not take over the role of PNC for that piconet.  If no MAC headers are correctly received during the 2 superframe duration scan, the next PNC shall begin sending out beacons using the same superframe duration and channel.  The process of the next PNC taking over as PNC is known as implicit handover.  There is a possibility that the next PNC has left the range of all of the other DEVs in the piconet as opposed to the original PNC going out of range or powering off.  In order to reduce the possibility of two piconets in close range using the same PNID, the next PNC shall use the Next PNID as the PNID of the piconet.

The next PNC shall start its beacon after the time it would have expected the beacon from the previous PNC so that if they are both in range of some DEVs their beacons won’t collide.  The next PNC should choose a position for the beacon that was unused based on the previous CTAs, to minimize the probability of collision.

DEVs that are not identified as the next PNC should store the NextPNID from the beacon.  When the DEVs that are not identified as the next PNC fail to detect mMaxLostBeacons they should start scanning for beacons.  If they do not see beacons with the current PNID, but see beacons with the Next PNID and the PNC Address of the Next PNC, they are automatically associated with that piconet.

Add to Table 33

Managed Object: MACPIB_NextPNCCapable

Octets: 1 bit

Definition: Set to one if the DEV is capable of performing the becoming the next PNC as described in 8.2.3a, and shall be set to zero otherwise.

Access: Read Only

Modify figure 41 as follows:

b3 = next PNC capable

7.4.11

Add the following text:

The next PNC capable bit shall be set to 1 if the DEV is capable of performing the next PNC functionality as described in 8.2.3a, otherwise the bit shall be set to zero.

8.2.3b Preliminary handover

Preliminary Handover shall not be used by a dependant PNC.

If a DEV has been chosen as next PNC, the PNC shall periodically send handover information to that DEV so that it has the information it needs to take over as PNC.  This sending of handover information is known as preliminary handover.  In order to send the handover information, the PNC shall send the Handover Request command with the Handover Status field set to Preliminary Handover.  A DEV receiving this frame shall only store the information for use at a later time, but not take over as PNC at this time.

Information transfer shall take place as shown in Figure 94a.  In addition, any security information may be transferred as defined in 9.4.1.

When all the information has been received, the next PNC shall send the Handover Response command with Reason Code set to Success, Ready for Handover.

The current PNC may issue a handover based on previously transferred information by sending the Handover Request command with the Handover Status field set to Handover Based on Previous Information. Once the chosen PNC capable DEV is prepared to start operating as PNC, it shall respond to the current PNC with a PNC Handover Response command with Reason Code set to Success, Ready for Handover.

The handover process now proceeds as described in 8.2.3 from the point where the Handover Response command is sent.

Annex D PICS

MF3.xx Next PNC IE O O

MF4.xx  Piconet Channel Status O O

MLFxx Next PNC capable FD2: O O

MLFxx Piconet Channel Status reporting O O

Issue Discussion based on feedback from Cairns:

- Maybe some DEVs in the new piconets can hear each other even if the PNCs can’t.

  - If the next PNC hears any DEVs that can hear the old PNC and are still transmitting, it shall not take over as next PNC. Done.

  - The next PNID will help sort out the issue if the original PNC is still transmitting, but the Next PNC is out of range of the original PNC or any DEVs that can still hear the original PNC. Done

  - The DEVs should report to their PNC if there is an interfering piconet and the PNCs will sort out by changing channels as in legacy 802.15.3.  Done

- Next PNC may need to scan for >1SF but <2 SF before becoming PNC for backward compatibility.

  - Not sure if this would help anything, because 802,15,3 is silent on how many missed beacons before a DEV starts a new piconet.

  - Both the NextPNC and the legacy DEV that is attempting to create a new piconet shall scan until they start sending their own beacons, so if they hear the other DEV they will not start a piconet.  It will be a low probability event where both the NextPNC and a legacy DEV start sending beacons at the exact same instant.  This should be no more likely than two legacy DEVs starting new piconets and colliding.

- PNID assignment: same vs. New.  Why?

  - Maybe overlapping piconets will automatically resolve dual PNID.

  - But if security mode 90 is used, problems could occur because DEVs could accept frames with the same PNID but from the wrong  piconet.  Recommend keeping next PNID.

- Old DEV interoperability issues.

  - Old DEVs won’t know about Next PNID and will have to join the new piconet.  Same situation as legacy 802.15.3,  No change.

- Scanning requirements – compatibility.

  - No change required legacy DEV behavior is undefined when PNC disappears.

- Next PNC may need to change channels as well

  - This would complicate things too much in a crowded channel environment.  If the channel is busy, the DEV can optionally change channel and start a new piconet.  No change.

- Newly created streams may not be in handover list yet.

  - If the stream disappears, the DEV will have to request a new stream.  DEVs need to be able to handle when PNC terminates a stream but the DEV doesn’t receive the stream termination announcement.  No Change.

- Only pre-handover to 3b DEVs.  How does it know?

  - In Cairns it was decided that Device capability would be used to indicate 3b functionality.  Next PNC and Channel status capability would be mandatory for 802.15.3b implementations.

- What does bitmap mean?  Can only header, or payload be heard?  Or base rate payloads?

  - Maybe 2 bits per DEV?  Or multiple bits 0 – nothing heard, 1 header heard, 1 lowest rate, 2, next rate, etc?

  - MCTAs and Beacons always sent at base data rate.  For now, it is proposed that the bit map will use one bit that indicates that headers are being received correctly.  Base rate should also be heard if header can be heard.  No change.

- How does channel status information fit in with PNC priorities?

  - Tiebreaker - Done

  - Can over ride PNC capabilities.  – Done.

- Maybe scan as soon as first beacon missed

  - Optional.  Done

- No current requirement that DEV waits ATP before starting a piconet?  No.

- Corner cases

  - What if 2 start piconets?  How do you clean up if 2 piconets start?  First one should hear the other and defer.  If 2 start, they will not both have the same PNID.

  - What if PNC and next PNC disappear?  Same situation as legacy 802.15.3

  - What if many devices can’t hear next PNC?  They will have to create another piconet, preferably on a separate channel.

- Knut says merging piconets won’t work.  Not sure if splitting the piconet will work

  - Splitting the piconet should work.  DEVs will be disassociated from the original piconet after ATP.

- Beacon offset should be fixed offset from original beacon.  Should hit CAP or other contention period to maximize the DEVs that hear it.  Done.

- Knut wants STP (Stream Timeout Period) to time our streams – re-request or lose.

  - New concept.  Not covered here.

Changes made based on Knut’s e-mail Comments:

- changed channel status bitmap to be bit set to 1 if any frames correctly received from that DEV since the last channel status command sent.

- Added MACPIB_NextPNCCapable and MACPIB_NextPNCAware

- Kept NextPNID due to lack of feedback from the BRC.

- Added Handover status of “Handover Information Transfer, no handover..”

- Added Definitions for preliminary handover and implicit handover.

Changes made based on James’ e-mail Comments:

- Changed text on use of the channel status IE bitmaps to “The PNC shall consider the bitmaps in the Piconet Channel status commands when choosing the next PNC.”

- Changed from Mandatory to Optional in PICS

Changes made based on James’ additional e-mail comments from 6/17/05

- Cchanged Shalls to Mays.

- Changed the beacon alignmet for the NnextPNC to an unused portion of the old superframe.

- Added references in the text for preliminary handover and implicit handover.

- Added text that the PNC shall not choose a PNID of the current piconet or one that it has heard “recently” or one that has been reported by remote scan or overlapping PNID.

Comments post SB Tuesday 9/20/05 meeting

- X change PNC shall handover to will

- X  maxlostbeacons+1 instead of 5?

- Should not try to be next PNC and should discard information about next PNC?

- X Maybe listen for longer - no

- X Same beacon time or offset?

- X New PNC should scan during old beacon time

- X Don’t have to say purposely

- X Beacons don’t collide -> beacons won’t collide.

- X Change nextPNIC to nextPNID

- X Table 33 – need full editing instructions – octets – 1bit, managed objects, access (R/w)

- X Did I add NextPNC capable to the capability field? 7.4.11 bit 14

- X PNC shall check nextPNC capable and only assigne if capable

- X What is next PNC aware for? deleted

- X Section 8.2.3a ?

- X To two to (done)

- X Should we change piconet channel status  to an IE so you can probe for? yes

- X How long to scan for?

- X Should we indicate that the DEV tried to scan for all sleeping DEVs?  If DEV is sleeping with no channel time, PNC will  know.  Maybe list doesn’t include DEVs in power save?  Can’t hear APS DEVs.  Add a bit (octet) at the end to say (I didn’t scan for power save)

- X Start of 8.2.x change from shall to will

- X Should be handover, not handoff

- X Channel Status command should be caps (but not in titles)

- X Should be DEVs, not devices

- X Should be Always awake, not listen always

- X Listen to source, not listen source - x

- X Says what PNC does, Need to say what the DEVs do.  Aware.  Shall or should transfer to the new piconet.  Shall not go back to the old piconet.  Not aware, old rules apply.

- X Overlapping piconet Uses same duration and channel

- X IE instead of command for “devs I can hear”

- X Can IEs be probed?

- X Many more edits on the fly

- Dependent piconet issues