IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Task Group 4a for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Calculating parameter macackwaitduration for the UWB PHY types |
| Date Submitted | 18 May 2006 |
| Source | [Ben Rolfe] [ ] [ ] | Voice: [408-395-7207] Fax: [] E-mail: [ben@blindcreek.com] |
| Re: | 802.15.4a Draft 2 Comment Resolution |
| Abstract | Formula for calculating macackwaitduration for UWB PHY, at mandatory and optional data rates. |
| Purpose | Resolve comments on Draft 2 regarding missing definition of macackwaitduration |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

NOTE: This revision (0) is not yet complete.

Author: Ben Rolfe   Date: 30-April-2006

In draft 2 of 15.4a, macAckWaitDuration is used and defined in principle but no value is given. To calculate the macAckWaitDuration depends on the maximum frame duration which for UWB depends on several PHY parameters which are not all constante, for example, depends on the data rate.  This note is about calculating the frame length for the 15.4a UWB PHY. Based initially on "Vern's notion of the frame length" email thread by Vern Brethour <vern.brethour@timedomain.com>.

The following shows the two formula to calculate the frame length, in microseconds, for determining MAC maximum waiting time for MPDU transmission and ACK.  The first is for the mandatory data rate and the 100Kbps data rate.  For these cases the PHY header and payload are sent at the same data rate.  The second is for optional data rates, which are different because the PHY header is sent at a different rate than the payload.

In matlab/C code:

frameLen = ( NominalSymbolTime * ( nPreambleSymbols + nDelimSymbols + ((nPHYheaderSymbols+(nPPDUoctects*nBitsPerOctet)) / overallFECrate) ) * dataRateFactor );

In the second case the preamble and PHY header are sent at a different data rate than the body. In this case the preamble time is the same as the first case, and the body time depends on the body data rate. Shown here in three parts: the preamble and PHR separate for clarity.